## Slide 1: 20 MHz transmission in NGV continued
Date: 2019-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Yujin Noh | Newracom |  |  | yujin.noh at newracom.com

## Slide 2: Background
FRD&SFD Motion #4 passed [1]
  “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.”
PAPR on 20MHz transmission was discussed [2].
  Two comments received
    PAPR values when no phase rotation applied
    Backward compatibility issues on 11p devices on upper 10MHz of 20MHz channel.
With those comments verified, this submission is trying to decide phase rotation to be applied to duplicated fields.

## Slide 3: PAPR (Peak-to-Average Power Ratio)
PAPR is well-known to be high when sequence is duplicated in frequency domain.
  Given L-STF, L-LTF, and L-SIG for 10MHz PPDU repeated at legacy portion in 20 MHz PPDU, it is obvious that being simply repeated causes high PAPR for legacy portion of the preamble
Low PAPR value is important in reducing implementation cost of Tx Power Amplifier (PA) and Rx dynamic range related function blocks.
  PAPR could be a nice guideline on actual backoff and dynamic ranges that the implementations need to consider

## Slide 4: Simulation Configuration
99.9% PAPR
  The max power is set to a value of top 99.9%
8x oversampled time domain signal
GI considered as part of the OFDM symbol
L-SIG PAPR
  All combination of values in R1-R4 (RATE field) and R5-R16 (LENGTH field)
Data PAPR
  40 MHz 11ac DC2 (downclocked by 2) based
  Random values applied to more than 100,000 data OFDM symbols with MCS0, MCS2, MCS4, MCS6 and MCS8 (256QAM ¾)

## Slide 5: Options
Considering no legacy devices (e.g. 11n, 11ac and 11ax) in the specially assigned channels, different options can be taken into account.
  Legacy gamma vector with {1, +j}
  Phase rotation in MCS0 DCM (Dual Carrier Modulation)
  CSD (Cyclic Shift Delay)
  etc

## Slide 6: Legacy gamma vector with {1, +j}
Simple way to reuse what we have used (11n-like approach)
  + 1 is multiplied to lower 10 MHz subchannel
  +j is multiplied to upper 10 MHz subchannel
PAPR simulation shows L-SIG is identified as bottleneck of 20 MHz PPDU transmission.
  PAPR of data portion is even better than PAPR of L-SIG field.
PAPR values here could be used as reference for further analysis.
PAPR [dB] (99.9%, 8x oversampled) in 20 MHz |  |  | 
Gamma Vector | L-STF | L-LTF | L-SIG (Median)
[1 1] | 5.0997 | 6.1761 | 9.0650
[1 -1] | 4.8133 | 6.1506 | 9.0354
[1 j] | 5.2497 | 5.7927 | 9.3806
[1 -j] | 5.2497 | 5.7948 | 9.3751
1.7dB

## Slide 7: Phase rotation in MCS0 DCM
It is accepted to mitigate the PAPR issues for DCM MCS 0 in 11ax and 11bd [1]
  + 1 is multiplied to lower 10 MHz subchannel
  (-1)k is multiplied to upper 10 MHz subchannel
    k: subcarrier indices
Generally providing improved PAPR over L-STF, L-LTF and L-SIG comparing to reference PAPR values
Legacy portion (especially L-SIG) is not a bottleneck anymore comparing to data portion.
PAPR [dB] (99.9%, 8x oversampled) in 20 MHz |  | 
L-STF | L-LTF | L-SIG (Median)
4.8133 (5.2497) | 5.8799 (5.7927) | 6.9529 (9.3806)
gamma vector
{1, +j}

## Slide 8: Impact on 11p devices on the Secondary Channel
For example, assuming that phase rotation in MCS0 DCM is applied to the secondary 10 MHz channel,
L-STF consists of non-zero values described below, when 11p receiver conducts carrier sense and auto-correlation operation, there is no impact on performance.
  The L-STF is given below, after rotating the tones in the upper subchannel (subcarriers 6 – 58) multiplied by -1 in alterative way.
As for L-LTF since those phase rotation would be interpreted as channel impact, no performance degradation of 11p device is expected.

## Slide 9: CSD (Cyclic Shift Delay) 1/2
Cyclic delayed sequence applied to 10 MHz subchannel.
  + 1 is multiplied to lower 10 MHz subchannel
  is multiplied to upper 10 MHz subchannel
    k: subcarrier indices
Depending on TCS, some CSD values provide improved PAPR over L-STF, L-LTF and L-SIG comparing to reference PAPR values
 | PAPR [dB] in 20 MHz (99.9%, 8x oversampled) |  | 
CSD (ns) (TCS) | L-STF | L-LTF | L-SIG (Median)
-25 | 5.0489 | 5.7085 | 9.228
-50 | 4.3818 | 5.5877 | 8.5107
-75 | 3.8746 | 4.6096 | 8.0954
-100 | 3.5696 (5.2497) | 5.1641 (5.7927) | 7.3959 (9.3806)
-125 | 4.6851 | 5.3532 | 7.3918
-150 | 5.0674 | 5.8687 | 7.5948
-175 | 5.1405 | 5.6444 | 7.6878

## Slide 10: CSD (Cyclic Shift Delay) 2/2

## Slide 11: PAPR values of 20 MHz NGV PPDU
PAPR [dB] (99.9%, 8x oversampled) | L-STF | L-LTF | L-SIG (Median) | 20 MHz NGV-DATA
[ 1, 1] | 5.0997 | 6.1761 | 9.0650 | 
[ 1, +j ] | 5.2497 | 5.7927 | 9.3806 | 7.7349
Phase rotation in DCM+MCS0 | 4.8133 | 5.8799 | 6.9529 | 
CSD -100ns applied | 3.5696 | 5.1641 | 7.3959 | 
Updated

## Slide 12: Summary
20 MHz phase rotation {+1, +j} seems not to provide much benefits in terms of PAPR reduction
  PAPR simulation shows L-SIG is identified as bottleneck of 20 MHz PPDU transmission.
    PAPR of data portion is even better than PAPR of SIG field
With phase rotation applied to every other tone of L-LTF differently, it may impact on performance of 11p devices on upper 10MHz depending on its implementation.
  E.g. ) Channel estimation if channel smoothing implemented
Given phase rotation features for 20MHz on the table, since PAPR barely improves comparing to no phase rotation without any impact on 11p devices, no phase rotation seems to be a simple approach.
Updated

## Slide 13: SP 1
Which option do you prefer for 20 MHz transmission in 11bd?
  Opt. 1: No phase rotation applied to upper 10MHz channel
  Opt. 2: Gamma vector with {1, +j}

## Slide 14: SP 2
Do you agree to add the following to section 3 in 11bd SFD?
  The function is used to represent a rotation of the tones.
    Where BW is channel bandwidth
    k is subcarrier indices
  Y/N/A
For a 10 MHz PPDU transmissions,
= 1
For a 20 MHz PPDU transmissions,

## Slide 15: SP 3
Do you agree to add the following to section 3 in 11bd SFD?
  The function is used to represent a rotation of the tones.
    Where BW is channel bandwidth
    k is subcarrier indices
  Y/N/A
For a 10 MHz PPDU transmissions,
= 1
For a 20 MHz PPDU transmissions,

## Slide 16: SP 4
Do you accept updated spec text in doc 11-20/0051r1?
Y/N/A

## Slide 17: Reference
[1] 11-19/0514 Motion Booklet for IEEE 802.11 TGbd
[2] 11-19/1154r0 20 MHz transmission in NGV