## Slide 1: Phase Rotation Follow-up
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In the September F2F meeting, TGbe agreed that
  EHT PPDU starts with the legacy preamble part
  11be supports 320 MHz and 160+160 MHz PPDU
In [1], we discussed the phase rotation which is applied to the legacy preamble part of EHT PPDU to reduce PAPR
In this contribution, we propose several options for the phase rotation in 320 / 160+160 MHz

## Slide 3: Assumptions
Each coefficient of the phase rotation is employed to each 20MHz channel
Candidates for each coefficient of the phase rotation are 1, -1, j, -j for simplicity
We consider PAPR of L-LTF to obtain optimized coefficients while PAPR is investigated for all legacy preamble parts, i.e., L-STF, L-LTF and L-SIG
When calculating PAPR, contiguous 320MHz bandwidth and 4x IFFT are considered

## Slide 4: Phase Rotation (1/3)
We take account of two cases as follows to obtain an optimized phase rotation and to investigate PAPR for various options
  Case 1: entire bandwidth allocation (i.e., non-preamble puncturing)
  Case 2: 20MHz based preamble puncturing
We also consider the following options to design a phase rotation in 320MHz
  Option 1: repeat 11ax 80MHz phase rotation
  Option 2: repeat 11ax 80MHz phase rotation and apply additional coefficients to 80MHz segments
  Option 3: repeat new 80MHz phase rotation which is optimal in 80MHz when considering Case 2
  Option 4: repeat new 80MHz phase rotation and apply additional coefficients to 80MHz segments
  Note that additional coefficients in option 2 and 4 are optimized considering either case 1 or case 2

## Slide 5: Phase Rotation (2/3)
Option 1
  [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
Option 2
  A*: [1 -1 -1 -1 j -j -j -j j -j -j -j 1 -1 -1 -1]
  B**: [1 -1 -1 -1 j -j -j -j 1 -1 -1 -1 j -j -j -j]
Option 3
  [1 1 -1 -1 1 1 -1 -1 1 1 -1 -1 1 1 -1 -1]
  PAPR comparison for 80MHz between 11ax phase rotation and new one ([1 1 -1 -1]) is shown in Appendix A
Option 4
  A*: [1 1 -1 -1 j j -j -j -j -j j j -1 -1 1 1]
  B**: [1 1 -1 -1 1 1 -1 -1 j j -j -j -j -j j j]
*: additional coefficients applied to 80MHz segments are optimized considering Case 1, i.e., entire bandwidth allocation
**: additional coefficients applied to 80MHz segments are optimized considering Case 2, i.e., 20MHz based preamble puncturing

## Slide 6: Phase Rotation (3/3)
PAPR
  In Appendix B, PAPR for the L-SIG part is shown
    Its trend is the same as that of L-STF or L-LTF
 |  | Case 1 |  | Case 2 (max PAPR*) | 
 |  | L-STF | L-LTF | L-STF | L-LTF
Option 1 |  | 8.2600 | 9.1864 | 12.8812 | 13.9576
Option 2 | A | 5.5493 | 6.3714 | 11.4481 | 12.5284
 | B | 8.2167 | 9.2159 | 10.7392 | 11.8183
Option 3 |  | 11.2703 | 11.8144 | 11.2703 | 12.1967
Option 4 | A | 7.3583 | 8.4605 | 10.6648 | 11.7440
 | B | 8.8950 | 9.6281 | 10.8912 | 11.7023
Unit: [dB]
*: Various 20MHz based preamble puncturing patterns can be considered which have different PAPRs, and thus, we only present the maximum PAPR

## Slide 7: Discussion
In case 1
  Option 2-A is the best followed by Option 4-A
  Option 1 and Option 2-B follow Option 4-A and have similar PAPR
In case 2
  Option 2-B, Option 4-A and Option 4-B have similar and relatively low PAPR
If we consider a unified phase rotation
  Option 4-A is desirable because it has a relatively good PAPR in case 1 and it is one of the best options in case 2
  Option 2-B is also worth considering because it has comparable PAPR and reuses the conventional phase rotation
The best option is not the same between case 1 and case 2, and thus, we can consider different phase rotation values according to whether 20MHz based puncturing is applied or not
  For a simple implementation, we can unify the phase rotation when 20MHz based puncturing is applied

## Slide 8: Conclusion
We have proposed various options for the phase rotation employed to the legacy preamble part in 320 / 160+160 MHz and have shown their PAPR as well
Our preference is depending on whether 20MHz based puncturing is applied
  If 20MHz based puncturing is not applied, we prefer Option 2-A
  If 20MHz based puncturing is applied, we prefer Option 4-A, Option 4-B or Option 2-B

## Slide 9: Straw Poll #1
Do you agree that preamble puncturing can be considered in order to design phase rotation for 320/160+160 MHz?
Y/N/A: //

## Slide 10: Straw Poll #2
Which option do you prefer for the phase rotation in 320/160+160 MHz
  Option 1: Unified phase rotation regardless of whether the preamble puncturing is applied or not
  Option 2: Different phase rotation according to whether the preamble puncturing is applied or not
Option 1/Option 2/A: //

## Slide 11: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  [1 -1 -1 -1 j -j -j -j j -j -j -j 1 -1 -1 -1] is used for the phase rotation in 320/160+160 MHz when the preamble puncturing is not applied
Y/N/A : //

## Slide 12: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  [1 -1 -1 -1 j -j -j -j 1 -1 -1 -1 j -j -j -j] is used for the phase rotation in 320/160+160 MHz when the preamble puncturing is applied
Y/N/A : //

## Slide 13: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  [1 1 -1 -1 j j -j -j -j -j j j -1 -1 1 1] is used for the phase rotation in 320/160+160 MHz regardless of whether the preamble puncturing is applied or not
Y/N/A : //

## Slide 14: References
[1] 802.11-19/1493r0 Phase Rotation for 320MHz

## Slide 15: Appendix A
PAPR comparison for 80MHz
  11ax phase rotation: [1 -1 -1 -1]
  New phase rotation: [1 1 -1 -1]
 | Case 1 |  | Case 2 (max PAPR) | 
 | L-STF | L-LTF | L-STF | L-LTF
11ax phase rotation | 4.4380 | 5.3962 | 6.8606 | 7.9370
New phase rotation | 5.8847 | 6.6178 | 5.8847 | 6.6178
Unit: [dB]
L-SIG

## Slide 16: Appendix B
PAPR for L-SIG
Case 1
Case 2

## Slide 17: Appendix C
Case 1
Case 2
PAPR for the Data part