## Slide 1: MLA MAC Addresses Considerations
Date: 2020-01-09
Authors:

## Slide 2: Introduction
We discuss the following in this presentation
  Recap of current MLA architecture proposal and focus on the link MAC addresses and the MLD address
  Present some considerations and proposals on the MAC addresses on the AP side

## Slide 3: Current MLA Architecture recap
Each MLD has a single MAC-SAP that interfaces with upper layers
MLD has a unique MLD Address to identify the MLD instance
Each STA (link) has its own MAC Address
  They could be the same or different between links
  They could be the same or different than the upper MAC Address
Upper MAC
Lower MAC

## Slide 4: Current MLA Architecture recap (cont’d)
Upper-MAC maintains the following, shared by all links
  MLD address
  Single BA session, single SN space (per TID)
    So MPDUs can be tx/retx on any link and have a common BA scoreboard
  Single Association and security context
    Single multi-link association established via signaling over a single link
    Single 4-way handshake to establish a single (common) security context
  Single PN (per MLD)
    Helps maintain existing data reception processes on the receiver
      i.e., Replay check follows reordering based on common SN
    Single replay detection block follows reordering and BA block

## Slide 5: MLD Address Considerations
A single MLD address should be the LAN MAC address of the MLD (i.e., M in the figure) for other devices on the same LAN to communicate with
The MLD address needs to be a unique value (e.g., EIU-48) between MLDs. It can be one of the following:
  Set to a value completely independent of any of the link MAC address
  Set to the link MAC address of one of the links e.g., M=x and (x≠y or x=y)

## Slide 6: Link MAC Address Considerations for AP MLD
The link MAC addresses should be different to avoid confusing the legacy clients
  Beacon uses link MAC address
  BSS Color uses link MAC address. Otherwise the colors of the BSSs on two different bands will be the same from the same MLD. Each link will need to have its own color
Have to be different in non-colocated case when two APs use the same channel on the two links on the same client (so their beacons won’t confuse the client)

## Slide 7: Link MAC Address Considerations for AP MLD (Cont’d)
Prefer AP MLD to have different link MAC addresses on each link
Prefer all DL frames also carry the same link MAC addresses OTA in the TA/RA
    Traditional receiver filtering
    SIFs turn around
    TA/RA protected by the MIC for receiver to authenticate the frame

## Slide 8: Link MAC Address Considerations for non-AP MLD
MLA STA may have the same or different link MAC addresses on each link
Prefer all UL frames also carry the same link MAC addresses OTA
    Traditional receiver filtering
    SIFs turn around
    TA/RA protected by the MIC for receiver to authenticate the frame

## Slide 9: Usage of the MLD Address
In general the MLD address is used for procedures that are common for all links (i.e., common to all links and at the MLD level) between the peer MLDs. E.g.,
Authentication and PTK generation
On the DS, the MLD will be identified by the MLD Address
  Indicating the SA/DA of a packet going to/from the DS
BA setup between peer MLDs
  The (single) BA session per TID established between the two peer MLDs is identified by their MLD addresses
  The current <RA, TA, TID> carried in the BA setup frames are still using the link MAC addresses
All MLD level management processing
Note: TA/RA in the MAC header is always the link MAC Address

## Slide 10: Conclusion
We presented some considerations of MLA MAC addresses
Conclusions:
  The MAC addresses sent OTA are the link MAC addresses
  AP MLD uses different MAC addresses on each link
  Non-AP MLD may use same or different MAC addresses on each link
  An MLD address may be the same as one of the MAC Addresses of the STAs that are affiliated with the MLD

## Slide 11: SP1
Do you support the following?
The value of the RA/TA fields sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLD corresponding to that link

## Slide 12: SP2
Do you support the following?
An AP MLD uses different MAC addresses on each STA affiliated with it

## Slide 13: SP3
Do you support the following?
A non-AP MLD uses different MAC addresses on each STA affiliated with it

## Slide 14: SP4
Do you support the following?
The block ack agreement that is negotiated between two MLDs for a TID is identified using <originator MLD address, recipient MLD address, TID>
NOTE: The value of the RA/TA sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLD corresponding to that link