## Slide 1: Multi-link Architecture
Date: 2019-11-11
Authors:

## Slide 2: Background
Two configurations for multi-link were proposed in [1]
  Packet level aggregation
  Flow level aggregation
  Packet level aggregation is much more promising compared with flow level aggregation
  Increases the peak throughput by enabling simultaneous operations in different links
  Dynamic load balance
  Improves the robustness and latency performance by duplicate transmission or the same traffic transmission over more than one link and so on
  In this work, we just show our opinion on the architecture for packet level aggregation
  Try to reuse the existing PHY and MAC
  Note: here the device which supports packet level aggregation is called multi-link capable transparent device in the following slides

## Slide 3: Multi-link Capable Transparent Device Architecture
For the multi-link capable transparent device, it has a shared high MAC and a few independent low MAC and PHY components
  Exposes a single MAC SAP to the upper layer
  In the high MAC, may perform multi-link management, such association，authentication
At the transmitter side
  Distribute the traffic to each low MAC, perform load balancing
  Assign a multi-link packet number to a received packets from the upper layer
  Each low MAC is able to perform independent EDCA，CCA，sounding, may perform security mechanism
  May maintain the sequence number assignment for link based block acknowledgement as well as link specific MAC processing
Multilink Management
Common Queues
Traffic Steering
Buffer Queues
EDCAF
PHY 1
Buffer Queues
EDCAF
PHY 2
TX 1
TX 2
Low MAC 1
Low MAC 2
High MAC
Single MAC SAP

## Slide 4: Multi-link Capable Transparent Device Architecture
At the receiver side
  Collect the packets from the multiple links
  Perform buffer reordering based on the multi-link packet number, and send them to the upper layer in the order
  Perform link-based block acknowledgement based on its own scoreboard
Multi-link packet number was assigned for each packet in the high MAC [1] and [2]
  Only needed by high MAC layer
  Used for buffer ordering
  Bigger space size than the sequence number, and needs additional signaling (maybe zero overhead)
Multilink Management
Reordering Buffer
Common Queues
RX Buffer
Scoreboard
PHY 1
RX Buffer
Scoreboard
PHY 2
RX 1
RX 2
Low MAC 1
Low MAC 2
High MAC
Single MAC SAP

## Slide 5: References
[1] IEEE 802.11-19/0823r2 Multi-link aggregation
[2] IEEE 802.11-19/1575r0 Multi-link BA operation