## Slide 1: Multi-link Architecture
Date: 2019-11-11
Authors:

## Slide 2: Background
Two configurations for multi-link were proposed in [1]
  Packet level aggregation
  Flow level aggregation
  Packet level aggregation is much more promising compared with flow level aggregation
  Increases the peak throughput of a TID by enabling simultaneous operations in different links
  Dynamic load balance of a TID
  Improves the robustness and latency performance by duplicate transmission over more than one link and so on
  In this work, we just show our opinion on the architecture for packet level aggregation (MLD)
  Try to reuse the existing PHY and MAC

## Slide 3: Multi-link Device Architecture
For the multi-link device, it has a shared high MAC and a few independent low MAC and PHY components
  Exposes a single MAC SAP to the upper layer
  In the high MAC, perform global sequence number, such association，authentication
At the transmitter side
  Distribute the traffic to each low MAC, perform load balancing
  Assign a global sequence number to a received packets from the upper layer
  Each low MAC is able to perform independent EDCA，CCA，sounding, may perform security mechanism
  May maintain the sequence number assignment for link based block acknowledgement as well as link specific MAC processing
Multilink Management
Common Queues
Traffic Steering
Buffer Queues
EDCAF
PHY 1
Buffer Queues
EDCAF
PHY 2
TX 1
TX 2
Low MAC 1
Low MAC 2
High MAC
Single MAC SAP

## Slide 4: Multi-link Device Architecture
At the receiver side
  Collect the packets from the multiple links
  Perform buffer reordering based on the global sequence number, and send them to the upper layer in the order
  Perform link-based block acknowledgement based on its own scoreboard
Global sequence number was assigned for each packet in the high MAC [1] and [2]
  Is only needed by high MAC layer
  Can be used for buffer ordering
  Bigger space size than the sequence number, and needs additional signaling (maybe zero overhead)
  If using SN field, it can not support legacy fragmentation.
Multilink Management
Reordering Buffer
Common Queues
RX Buffer
Scoreboard
PHY 1
RX Buffer
Scoreboard
PHY 2
RX 1
RX 2
Low MAC 1
Low MAC 2
High MAC
Single MAC SAP

## Slide 5: Scoreboard
Is that possible to just have one scoreboard shared by more than one STA of the MLD?
  This kind of scoreboard should be a RAM which provide more than one port to be read and written simultaneously
  However, true two dual RAM is more expensive than the existing single port RAN
  Three-port RAM is rarely used now
  Hence, we suggest to have a scoreboard for each one STA of the MLD.
  If there is a sequence number for each link, the sizes of each scoreboard could be different, depending on the data rate of the corresponding link
  There is no overhead for bitmap in BA which could be the same size as today

## Slide 6: Summary
We propose the following items
  Have a scoreboard for each one STA of the MLD
  Global sequence number is not indicated by SN field
  Sequence number for a link could be optionally assigned

## Slide 7: References
[1] IEEE 802.11-19/0823r2 Multi-link aggregation
[2] IEEE 802.11-19/1575r0 Multi-link BA operation