## Slide 1: Consideration of EHT-LTF
Date: 2020-01-12
Authors:
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jinmin1230.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
The extensions of 16 streams and 240&320MHz have been discussed for new features in 11be
  Especially, multi-AP and MU-MIMO are the use cases of high order MIMO system (e.g. 16 spatial streams )
To support 16 streams and 240&320MHz, we need to define EHT-LTF for those new requirement
In this contribution, we consider how to design EHT-LTF in respect of overhead and PAPR performance

## Slide 3: Overhead Analysis
We assume that,
  MU-MIMO cases
    4 users, 4 spatial stream per user (Total number of spatial streams is 16)
  We assume 16x16 P-matrix with 2xLTF
The figure shows the ratio(%) between length of LTF and length of PPDU
  Even in case of 10k byte data size(TXTIME=227.2us), LTF length is more than 50% of total PPDU length
  With 4x LTF, overhead problem becomes worse
80MHz MU PPDU in 11ax
MCS 6 (16QAM, R=¾)
2x LTF, 0.8us GI

## Slide 4: Candidates for EHT-LTF overhead reduction
It’s easy way to adopt 2x & 1x LTF structure in 11be
  11ax defined 2x & 1x HE-LTF to find middle ground between overhead and performance
  However, as in previous page, even if we use 2x LTF, overhead portion is not negligible in high order MIMO or short packet scenario
There were some contributions to further reduce overhead
  In [1,3], they proposed interleaved LTF sequence between streams in multi-AP scenario
    We think it is also applicable to SU-MIMO and it is simple way to reduce overhead
  In [2], orthogonal sequence was proposed to reduce overhead
We think new techniques as well as the methods above should be investigated for further overhead reduction

## Slide 5: How to Generate 320MHz LTF
We think that 320MHz EHT-LTF sequence can be generated by duplication of 160MHz HE-LTF
  It is possible because 320MHz tone plan consists of duplicated tone plan of HE160
  Also, duplication method is widely used to generate longer sequence
    It can guarantee PAPR performance when phase rotation is applied
      ex.) For 160MHz HE-LTF in 11ax, 80MHz sequence is duplicated with phase rotation to reduce PAPR
  So, we investigate PAPR performance of proposed sequences (4x, 2x, 1x EHT-LTF) generated by duplication of 160MHz HE-LTF
    Since there isn’t agreement on how to generate 240MHz BW (puncturing from 320MHz or new channelization, etc.), we’d like to focus 320MHz LTF first.

## Slide 6: 4x EHT-LTF Sequence for 320MHz (1/2)
In a 320 MHz transmission using a 4x EHT-LTF,
  EHTLTF-2036,2036= [LTF160MHz_lower_4x, zeros(1,23), LTF160MHz_upper_4x]
    LTF160MHz_lower_4x = [LTF80MHz_lower_4x, zeros(1,23), LTF80MHz_upper_4x]
    LTF160MHz_upper_4x = [(-) LTF80MHz_lower_4x, zeros(1,23), LTF80MHz_upper_4x]
      LTF80MHz_lower_4x and LTF80MHz_upper_4x are already defined in 11ax
        So, we can simply define 4x EHT-LTF sequences for 320MHz
  We apply phase rotation to LTF80MHz_lower_4x of LTF160MHz_upper_4x since it has the best performance than other phase rotation cases
    0.1dB is better than applying phase rotation to LTF80MHz_upper_4x
  We don’t need to consider smaller segmented sequence than LTF80MHz_lower_4x or LTF80MHz_lower_4x if PAPR performance is acceptable (see next page)

## Slide 7: 4x EHT-LTF Sequence for 320MHz (2/2)
PAPR performance (RHELTF vs. PHELTF)
  Except for center RU26 and RU996 in 3rd & 4th 80MHz, RU2x996 in 2nd 160MHz and RU4x996 in 320MHz, PAPRs for all RUs are identical as in 11ax
    Also, theses exceptional RUs have reasonable PAPR performance comparing PAPR of data (see the Appendix)
  So, we conclude that proposed sequences with phase rotation is a good candidate for 4x EHT-LTF for 320MHz
3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 4.25, 4.43 4.25 4.43 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78 | 3.78
4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 |  | 4.97 |  | 4.44 |  |  | 4.97 |  | 4.44 | 
5.38 |  |  |  |  | 5.35 |  |  |  | 5.31 |  |  |  |  | 5.53 |  |  |  |  | 5.48 |  |  |  |  | 5.50 |  |  |  | 5.48 |  |  |  |  | 5.50 |  |  | 
5.50 |  |  |  |  |  |  |  |  | 5.51 |  |  |  |  |  |  |  |  |  | 5.60 |  |  |  |  |  |  |  |  | 5.53 |  |  |  |  |  |  |  | 
5.97 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.29 for first 80MHz, 7.22 for second 80MHz, 6.29 for third 80MHz, 7.22 for fourth 80MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7.09 for first 160MHz, 7.20 for second 160MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7.09 dB for 320MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PAPR (dB) for 26, 52, 106, 242, 484, 996, 2x996 and 4x996 tones RU

## Slide 8: 2x EHT-LTF Sequence for 320MHz (1/2)
In a 320 MHz transmission using a 2x EHT-LTF,
  EHTLTF-2036,2036= [LTF160MHz_lower_2x, zeros(1,23), LTF160MHz_upper_2x]
    LTF160MHz_lower_2x = [LTF80MHz_lower_2x, zeros(1,23), LTF80MHz_upper_2x];
    LTF160MHz_upper_2x = [(-) LTF80MHz_lower_2x, zeros(1,23), LTF80MHz_upper_2x];
      LTF80MHz_lower_2x and LTF80MHz_upper_2x are already defined in 11ax
        So, we can simply define 2x EHT-LTF sequences for 320MHz
  We apply phase rotation to LTF80MHz_lower_2x of LTF160MHz_upper_2x since it has the best performance than other phase rotation cases
    0.5dB is better than applying to LTF80MHz_upper_2x
  We don’t need to consider further segmented sequence than LTF80MHz_lower_4x or LTF80MHz_lower_4x if PAPR performance is acceptable(see next page)

## Slide 9: 2x EHT-LTF Sequence for 320MHz (2/2)
PAPR performance (RHELTF vs. PHELTF)
  Except for all RU484s and RU996 in 3rd & 4th 80MHz, RU2x996 in 2nd 160MHz and RU4x996 in 320MHz, PAPRs for all RUs are identical as in 11ax
    Also, theses exceptional RUs have reasonable PAPR performance
  So, we conclude that proposed sequences with phase rotation is a good candidate for 2x EHT-LTF for 320MHz
4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.37 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46
4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 | 
5.42 |  |  |  |  | 5.41 |  |  |  | 5.42 |  |  |  |  | 5.41 |  |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  | 
5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  | 
6.33, 6.40, 6.33, 6.40 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.40, 6.33, 6.40, 6.33 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.09 for first 80MHz, 6.69 for second 80MHz, 6.09 for third 80MHz, 6.69 for fourth 80MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.72 for first 160MHz, 6.99 for second 160MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.69 dB for 320MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PAPR (dB) for 26, 52, 106, 242, 484, 996, 2x996 and 4x996 tones RU

## Slide 10: 1x EHT-LTF Sequence for 320MHz
In a 320 MHz transmission using a 1x EHT-LTF,
  EHTLTF-2036,2036= [LTF160MHz_lower_1x, zeros(1,23), LTF160MHz_upper_1x]
    LTF160MHz_lower_1x = [LTF80MHz_lower_1x, zeros(1,23), LTF80MHz_upper_1x];
    LTF160MHz_upper_1x = [LTF80MHz_lower_1x, zeros(1,23), (-) LTF80MHz_upper_1x];
      LTF80MHz_lower_1x and LTF80MHz_upper_1x are defined in 11ax
        So, we can simply define 1x EHT-LTF sequences for 320MHz
  Different from 4x & 2x LTF sequences, we apply phase rotation to LTF80MHz_upper_1x of LTF160MHz_upper_1x to reduce PAPR
    0.3dB is better than applying to LTF80MHz_lower_1x as in 4x & 2x LTF
  Since 1x LTF is not adequate for MU PPDU as in 11ax, we only estimate PAPR in entire 320 MHz BW (RU4x996, RHELTF vs. PHELTF)
    Worst PAPR for 320MHz = 5.26dB

## Slide 11: Further Considerations
Even though PAPR is reasonable in our simulation, we have to investigate for puncturing cases and multiple RUs
In puncturing cases, we consider puncturing pattern in unit of 20MHz as in 11ax
  Different from 11ax, we consider that any sub-channel(s)(in unit of 20MHz) can be punctured
Moreover, since TGbe agreed that multiple RU can be allocated to single STA, we may need to check PAPR performance in various combinations
  The PAPR performance will be investigated after multiple RU discussion

## Slide 12: Puncturing in 80MHz
Considering any 20MHz sub-channel can be punctured
  We consider that the center 26-tone RU is not allocated if either of the two 20 MHz sub-channels which the center 26-tone RU straddles get the preamble punctured
  Depending how to define puncturing pattern in 11be, the worst PAPR can be different
    If we only consider some practical puncturing patterns, the worst PAPR could be smaller
 |  | Worst PAPR dB(the number of punctured sub-channel for worst cases) |  |  |  | 
 |  | Non-punctured | 1 sub-channel punctured | 2 sub-channels punctured | 3 sub-channels punctured | 4 sub-channels punctured
80 MHz | 4x | 6.29 | 7.94(2) | 7.98(1&4) | N/A | N/A
 | 2x | 6.08 | 8.22(4) | 8.53(2&3) | N/A | N/A
 | 1x | 5.00 | 7.85(4) | 8.61(1&3) | N/A | N/A
1
2
3
4
punctured
punctured
Ex) 2 sub-channels punctured cases for 4x LTF in 80MHz

## Slide 13: Puncturing in 160MHz
Considering any 20MHz sub-channel can be punctured
  Since we consider completely flexible puncturing patterns, the PAPR is high. However, if we only include some practical puncturing patterns, the worst PAPR could be smaller
 |  | Worst PAPR dB(the number of punctured sub-channel for worst cases) |  |  |  | 
 |  | Non-punctured | 1 sub-channel punctured | 2 sub-channels punctured | 3 sub-channels punctured | 4 sub-channels punctured
160 MHz | 4x | 7.09 | 8.32(7) | 10.20(4&7) | 9.78(4,7&8) | 9.62(2,6,7&8)
 | 2x | 6.72 | 8.99(3) | 10.67(4&6) | 10.33(2,4&6) | 9.91(2,3,4&6)
 | 1x | 5.12 | 8.06(1) | 9.84(4&7) | 9.52(4,6&7) | 10.54(1,3,5&8)
punctured
punctured
Ex) 2 sub-channels punctured cases for 4x LTF in 160MHz
5
6
7
8
1
2
3
4

## Slide 14: Puncturing in 320MHz
Considering any 20MHz sub-channel can be punctured
  Similar to previous results, PAPR highly increases up depending on the puncturing pattern.
 |  | Worst PAPR dB(the number of punctured sub-channel for worst cases) |  |  |  |  |  |  |  | 
 |  | Non-punctured | 1 sub-channel punctured | 2 sub-channels punctured | 3 sub-channels punctured | 4 sub-channels punctured | 5 sub-channels punctured | 6 sub-channels punctured | 7 sub-channels punctured | 8 sub-channels punctured
320 MHz | 4x | 7.09 | 9.07 (12) | 10.45 (1&12) | 11.41 (1,2&12) | 12.14 (1,2,11,12) | 12.13 (1,2,3,11,12) | 12.48 (2,3,4,6,9,14) | 12.47 (1,2,4,8,11,12,16) | 12.40 (1,2,4,5,8,11,12,16)
 | 2x | 6.69 | 8.92 (11) | 10.26 (4&9) | 11.10 (4,9&11) | 11.56 (4,9,10,11) | 12.19 (4,9,10,11,14) | 13.25 (4,6,9,10,11,14) | 13.06 (2,4,6,9,10,11,14) | 12.87 (2,4,6,7,9,10,11,14)
 | 1x | 5.26 | 8.28 (3) | 9.17 (5&15) | 10.19 (5,15&16) | 10.77 (5,14,15,16) | 11.37 (2,5,10,15,16) | 12.32 (4,5,6,8,12,15) | 12.24 (2,5,6,10,14,15,16) | 12.77 (1,3,5,8,9,11,14,15)
punctured
punctured
Ex) 2 sub-channels punctured cases for 4x LTF in 320MHz
13
14
15
16
9
10
11
12
5
6
7
8
1
2
3
4

## Slide 15: Conclusion
To extend 16 spatial streams and 240&320MHz BW, we need to develop EHT-LTF and we should take into account overhead and PAPR performance
  If possible, we think it is desirable to design EHT-LTF using a similar way with 11ax for simplicity
Since the PAPR performance is not good in the completely flexible puncturing pattern, we can consider two options
  Opt1: Restrict puncturing cases by practical puncturing patterns
  Opt2: Consider defining new sequences

## Slide 16: Straw poll 1
Do you agree to add the following text into SFD?
  EHT-LTF should be designed to support 16 spatial streams.
    2x and/or 1x HE-LTF concept as in 11ax may be used for EHT-LTF overhead reduction

## Slide 17: Straw poll 2
Which option do you prefer for 11be 240/320MHz EHT-LTF design by minimizing PAPR?
  Opt1: Restrict preamble puncturing cases by practical puncturing patterns (The detail on puncturing patterns is TBD)
  Opt2: Consider defining whole new sequences

## Slide 18: References
[1] 19/1535r0, “Sounding-for-ap-collaboration”
[2] 19/1585r1, “Orthogonal-sequence-based-reference-signal-for-ltf-reduction”
[3] 19/1593r0, “Joint-sounding-for-multi-ap-systems”

## Slide 19: Appendix
Median PAPR in Data
RU type | DATA (BPSK) | DATA (QAM)
80MHz | 8.77 dB | 9.16 dB
160MHz | 9.18 dB | 9.54 dB
320MHz | 9.53 dB | 9.86 dB