## Slide 1: Multi-link Management
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Motivation
Some key usage cases are proposed with multi-band capability [1-3]
  Steering/load balancing, aggregation, AP power save, coexistence with other stds, QoS, etc.
In this contribution, we suggest some procedures for the above-mentioned usage cases for multi-band and address some considerations

## Slide 3: Recap on Terminologies [1-2]
Multi-link AP logical entity
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Multi-link non-AP logical entity
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Supported
multi-link set
Disabled
multi-link set
Enabled
multi-link set

## Slide 4: Turning off links
A STA MLLE can turn off some of its operating links
  A STA MLLE can turn off its radio to save the power with existing disassociation procedure
  When the STA wants to turn on Link 1 again, association may not be required
    If parameter update is needed, it can be performed on Link 2 or Link 3 in advance
Multi-link AP logical entity
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Multi-link non-AP logical entity
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Multi-link AP logical entity
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Multi-link non-AP logical entity
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3

## Slide 5: Alternating active links
An MLLE can alternate its active link among the supported multi-link set
  This can be achieved by turning on a link among disabled multi-link set and then turning off a link among enabled multi-link set
Multi-link AP logical entity
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Multi-link non-AP logical entity
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Multi-link AP logical entity
AP 1 on 2.4 GHz
AP 2 on 5 GHz
AP 3 on 6 GHz
Multi-link non-AP logical entity
STA 1 on 2.4 GHz
STA 2 on 5 GHz
STA 3 on 6 GHz
Link
1
Link
2
Link
3
Establish Link 3
Disconnect
Link 2

## Slide 6: Switching band of STA with a common radio [3]
A STA can operate with a common radio among the supportable links
  Antennas of the STA with shared radio can use either 5 GHz or 6 GHz
  Adopting this shared radio can allow the STA to support both bands
  To this end, link switching procedure needs to be defined
    Existing channel switching procedure can be reused for this: Extended channel switch announcement element can support channel switch mode (forcing STAs to stop transmissions), new operating class, new channel number, and channel switch count (time period until the channel switch event)
    Else, a new procedure for link switching can be newly defined
Multi-link AP logical entity
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Multi-link non-AP logical entity
STA 1
on 5 GHz
Link
1
Link
2
AP 3
on 6 GHz
Link
3
Multi-link AP logical entity
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Multi-link non-AP logical entity
STA 1
on 6 GHz
Link
1
Link
2
AP 3
on 6 GHz
Link
3

## Slide 7: Switching band of STA with a common radio
For some APs with spatial limitation (e.g., Soft AP), an AP may operate with a common radio as well
  Antennas attached to MLLEs can operate either 5 GHz or 6 GHz
  It can be achieved by existing channel switching procedure
  With this band switching, crowded channel can be avoided and traffic load can also be balanced
  However, in this case, legacy 5 GHz stations would loss their connection
Multi-link AP logical entity
AP 1
on 2.4 GHz
AP 2
on 5 GHz
Multi-link non-AP logical entity
STA 1
on 2.4 GHz
STA 2
on 5 GHz
Link
1
Link
2
Multi-link AP logical entity
AP 1
on 2.4 GHz
AP 2
on 6 GHz
Multi-link non-AP logical entity
STA 1
on 2.4 GHz
STA 2
on 6 GHz
Link
1
Link
2

## Slide 8: Switching band of STA with a common radio
Multi-link non-AP logical entity B (Shared radio support)
Multi-link non-AP logical entity B (Shared radio support)
STA B1
on 6 GHz
To overcome this disconnection problem of legacy STAs, a subset of links may remain in the frequency band where they originally existed
  For instance, assuming AP 1 has 4 antennas, the AP 1 is split into AP 1 and AP 2, and they are allocated on 5GHz and 6GHz, respectively
  STAs supporting shared radio concept (STA MLLE B) can selectively move to a new AP (AP 2)
  Legacy STA can maintain its connection with the AP
Multi-link AP logical entity
AP 1
on 5 GHz
Multi-link AP logical entity
Link
2
AP 2
on 6 GHz
AP 1
on 5 GHz
Multi-link non-AP logical entity A (No shared radio support)
STA A1
on 5 GHz
Link
1
Multi-link non-AP logical entity A (No shared radio support)
STA A1
on 5 GHz
Link
1
STA B1
on 5 GHz

## Slide 9: Considerations
When it comes to turning off the link to save the power, any explicit signaling may not be needed
  If an MLLE has a common queue, the MLLE has only to re-map between TID and link
  On the other hand, if an MLLE has seperated queues over links, seamless transfer may not be possible
In case of alternating links, existing reassociation procedure can be used
  This case is same with the above-mentioned turning off cases
If some radios can change its frequency band, this procedure is analogous to existing (extended) channel switching
  In this case, legacy devices may not be supported due to the switched band
To support the legacy devices, a subset of links may remain on the link where they existed
  To this end, some additional information can be included in addition to existing channel switching
  Since a BSS is newly created, information regarding the BSS can be announced such as Band Information, NSS, BSSID, Beacon Interval, and so on
  Some attributes, e.g., NSS, for the remaining AP may be changed and they needs to be announced

## Slide 10: Straw Poll 1
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that an MLLE can support a non-AP STA which can switch its operating band (e.g., 5 GHz and 6 GHz)

## Slide 11: Straw Poll 2
Do you agree to add the following text to the TGbe SFD?
  TGbe shall support that an MLLE can support an AP STA which can switch its operating band (e.g., 5 GHz and 6 GHz)

## Slide 12: References
[1] 19/0773r7, “Multi-link operation framework”
[2] 19/1358r0, “Multi-link operation management”
[3] 19/1528r1, “Multi-link: Link management”