## Slide 1: Multi-link Management
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Motivation
There have been lots of contribution dealing with multi-link management issues [1-3]
  Steering/load balancing, aggregation, AP power save, coexistence with other stds, QoS, etc.
Channel/link switch operation would be one of solutions to avoid traffic congestion in multi-link
In this contribution, we introduce channel/link switch operation for multi-link and address some considerations

## Slide 3: Recap on terminologies [1-2]
AP multi-link device (AP MLD)
AP 1
AP 2
AP 3
Non-AP multi-link device (Non-AP MLD)
STA 1
STA 2
STA 3
Link
1
Link
2
Link
3
Disabled
multi-link set
Enabled
multi-link set

## Slide 4: Channel switch operation in multi-link
Channel switch operation is already defined in legacy .11
  It can be performed by existing channel switch announcement
  Based on the channel switching procedure, AP2 and STAs which are associated with the AP2 move to other channel after the announcement
  With this channel switching, crowded channel can be avoided so that traffic load can be balanced
  Also, transmission on one link concurrent with reception on the other link may become possible
  In multi-link, channel switch operation may be used more frequently since established connections are still alive during switching
AP MLD
AP 1
AP 2
Non-AP MLD
STA 1
STA 2
AP MLD
AP 1
AP 2
Non-AP MLD
STA 1
STA 2
Link 1
Link 2’
Link 1
Link 2
Channel switch announcement
Move to other channel

## Slide 5: Link switch operation initiated from AP side
An AP MLD may request a non-AP MLD so that the non-AP MLD can perform a link switch operation
  In this scenario, only a STA moves to other link supported by the AP MLD
  So, AP2 keeps providing access for other associated STAs as was
  An existing channel switch announcement can be reused with slight modification
  Link switch response from the non-AP MLD needs to be defined in order to let the AP MLD know when to switch transmitter AP
  Also, alive check procedure may be needed whether STA2 successfully moved or not
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
Link 1
Link 2
AP 1
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
Link 1
Link 2’
AP 1
Move to other link
supported by AP MLD
1) Link switch request
2) Link switch response
Switch transmitter AP which transmits to STA2
3) Alive check

## Slide 6: Link switch operation initiated from STA side
On the other hand, a non-AP MLD may also request link switch operation
  A STA affiliated with a non-AP MLD may change its operating link among the links supported by an AP MLD
    Information for link to move may be informed by the AP MLD in advance
  To this end, link switch operation from STA side needs to be defined
  Same as earlier, alive check procedure may be needed whether STA2 successfully moved or not
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
Link 1
Link 2
AP 1
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
Link 1
Link 2’
AP 1
Move to other link
supported by AP MLD
1) Link switch request
2) Link switch response
Switch transmitter AP which transmits to STA2
3) Alive check

## Slide 7: Diagram for link switch operation
After multi-link setup, STA1 and STA2 become associated with AP1 and AP2, respectively
  At multi-link setup stage, information can be exchanged between the MLDs, i.e., non-AP MLD can be aware of the existence of APs and their operating channels
The AP MLD or the non-AP MLD initiates link switch operation as mentioned earlier
Additional alive check operation may be performed to make sure that STA2 successfully switch its link
After that, a new link is established between the AP and the STA
During ML setup procedure, required information (e.g., supportable frequency band/channel) can be exchanged between AP MLD and STA MLD
AP 2
AP 3
Link switch operation request/response
Data transmission
Switch operating link
Renew information of
non-AP MLD
Data transmission
STA 1
STA 2
AP MLD
non-AP MLD
AP 1
Link 1
Link 2
Multi-link setup with information exchange
Link 2’
Alive check operation

## Slide 8: Link switch operation with STA’s shared radio
Due to spatial limitations in a physical device, some STAs affiliated with a MLD may support multiple frequency bands
  E.g., either 5 GHz or 6 Ghz band
Assuming this, link switch operation would be used more efficiently in multi-link scenario
Link switch procedure shown below can be done initiated either from AP MLD or from non-AP MLD
Link 1
Link 2’
Link 1
Link 2
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
AP 1
AP MLD
AP 2
AP 3
Non-AP MLD
STA 1
STA 2
AP 1
2.4GHz
5GHz
6GHz
2.4GHz
5GHz
6GHz
2.4GHz
5GHz/6GHz
2.4GHz
5GHz/6GHz
Change its operating band and move to other link supported by AP MLD

## Slide 9: Link switch operation with AP’s shared radio
For some APs with spatial limitation (e.g., Soft AP), these APs may operate with a shared radio as well
  APs affiliated with the AP MLD can operate either 5 GHz or 6 GHz
However, as shown in figure below, legacy/single-link 5 GHz stations would lose their connections in this case
AP MLD
AP 1
AP 2
Non-AP MLD B (Shared radio support)
STA B1
STA B2
AP MLD
AP 1
AP 2
Non-AP MLD B (Shared radio support)
STA B1
STA B2
2.4GHz
5GHz/6GHz
2.4GHz
5GHz/6GHz
2.4GHz
5GHz/6GHz
2.4GHz
5GHz/6GHz
Non-AP MLD A
(No shared radio support)
STA A1
Non-AP MLD A
(No shared radio support)
STA A1
5GHz
5GHz
Lose connection

## Slide 10: Link switch operation with AP’s shared radio
Non-AP MLD B (Shared radio support)
Non-AP MLD B (Shared radio support)
STA B1
To overcome this disconnection problem of legacy STAs, a subset of links may remain in the frequency band where they originally existed
  For instance, assuming AP 1 has 4 antennas, the AP 1 is split into AP 1 and AP 2, and they are allocated on 5GHz and 6GHz, respectively
  STAs supporting shared radio (non-AP MLD B) can selectively move to a new AP (AP 2)
  Legacy STA can maintain its connection with the AP
  Since a BSS is newly activated, information regarding the BSS can be announced such as Band Information, Max # of Nss, BSSID, Beacon Interval, and so on
  Some attributes, e.g., Max # of Nss, for the remaining AP may be changed and they needs to be announced
AP MLD
AP 1
AP MLD
AP 2
AP 1
Non-AP MLD A (No shared radio support)
STA A1
Non-AP MLD A (No shared radio support)
STA A1
STA B1
5GHz
5GHz/6GHz
5GHz
5GHz
5GHz/6GHz
6GHz
AP 2
5GHz
6GHz
4 antennas
2 antennas
2 antennas

## Slide 11: Considerations
The AP MLD or the non-AP MLD can initiate link switch operation for non-AP MLD
If some radios can be shared among frequency bands, link switch operation can be used adequately
  In this case, legacy/single-link devices may not be supported due to the switched band
To support the legacy/single-link devices, a subset of links may remain on the link where they existed
  To this end, some additional information can be included in addition to existing channel switching

## Slide 12: References
[1] 19/0822r9, “Extremely efficient multi-band operation”
[2] 19/1358r0, “Multi-link operation management”
[3] 19/1528r2, “Multi-link: Link management”

## Slide 13: Straw Poll 1
Do you agree to add the following text to the TGbe SFD?
  A non-AP MLD may send its associated AP MLD a frame to request to switch link to other link among enabled links of the AP MLD.

## Slide 14: Straw Poll 2
Do you agree to add the following text to the TGbe SFD?
  An AP MLD may send an non-AP MLD a frame to request to switch a link of the non-AP MLD to other link among enabled links of the AP MLD.

## Slide 15: Straw Poll 3
Do you agree to define the following?
  Single-link non-AP MLD: A non-AP MLD that transmits or receives frames to/from another MLD on a single link at a time