## Slide 1: Multi-link Operation: Per-link AID
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2020-01-09

## Slide 2: Overview
Several contributions [1-8] have discussed the topic of multi-link power-save and some have floated the idea of cross-link wake-up signaling
This contribution continues the discussion on power-save and proposes to extend existing PS mechanisms for cross-link ‘wake-up’ signaling

## Slide 3: Motivation
A non-AP MLD consumes power when monitoring a link
  The more links are monitored the more power is consumed
  In many cases not all Rx chains need to be enabled
Multi-link framework should provide a mechanism for a non-AP STA instance to save power when there is inactivity on its link
Further, the framework should provide a mechanism such that an AP MLD can signal wake-up of a non-AP STA on any or all of its links
  For example, when there is high volume of DL data, an AP MLD may signal a non-AP MLD to be available on more than one link

## Slide 4: Per-link power-save
In [3, 5, 6, 8] it was proposed that each STA instance of a non-AP MLD utilizes existing PS schemes to transition between doze/awake state for that link
  E.g., EOSP/More Data, PS-Poll, signaling on a link
In the following slides we propose cross-link signaling which enables an AP MLD to signal wake-up of a non-AP STA instances on any link
  The signaling builds on top of baseline TIM

## Slide 5: Traffic advertisement for all links
The TIM element in an AP’s beacon frame carries traffic indication for each non-AP STA
  11ax further extended this functionality (via OPS feature) to identify non-AP STA(s) that the AP can service (e.g., for DL or soliciting UL).
MLO framework can leverage the existing scheme
  i.e., an AP’s TIM indicates the link(s) it will service the client
A single AID for a non-AP MLD doesn’t meet the requirement
  Cannot identify the link(s) on which the AP MLD intends to serve the client
Therefore a scheme that clearly identifies each link is needed
  i.e., per-link AID: each non-AP STA of a non-MLD is assigned a unique AID

## Slide 6: Per-link AID
AP assigns an AID for each link that is setup between the entities
  Gives an AP-entity the ability to unambiguously identify link(s) that it intends to use to service a non-AP MLD
    A single TIM bitmap can identify all links, a subset of the setup links or a single link
The signaling scheme is compatible with existing framework and preserves legacy behavior
  Legacy STA are assigned a single AID
  Having multiple TIM elements (one per-link) in the same Beacon can confuse legacy STAs
  The scheme doesn’t require defining new element(s) for signaling per-link wake-up
Further, the scheme works for single radio ML capable clients
  Beacon on any link indicates the AP MLD’s intention
Existing AID-based features (such as OPS) would naturally work for multi-link without requiring any spec change
  E.g., An OPS AP MLD signals the link(s) on which it desires to ‘service’ a non-AP MLD

## Slide 7: Assignment of AIDs
During multi-link setup, the AP MLD assigns multiple AIDs to a non-AP MLD
  AID space common to APs of an MLD
    Similar to other features (e.g., security key, BA scoreboard etc)
  AID for the link where association is performed is provided via the AID field in the (Re)Association Response frame
    Existing / baseline
  AID for other link(s) conveyed along with link-specific parameters in (Re-)Association Response frame

## Slide 8
Example of wake indication:
  Non-AP STA sends a PS-Poll on link1 with AID of link1 to indicate its awake state for link1 and/or sends a PS-Poll on link1 with AID of link2 to indicate awake state of link2
  Other AID-based mechanisms possible to identify one or more links where the STA is in wake state
Example of wake signaling with per-link AID

## Slide 9: Summary
In this presentation, we describe
  The concept of per-link AID assignment
    A convenient way for identifying any link setup between the MLDs
    All AID based features can naturally be extended to multiple links
  An efficient cross-link signaling scheme that is compatible with existing framework
  A mechanism that facilitates per-link power-save for multi-link capable non-AP MLD

## Slide 10: SP #1
Do you support that the 802.11be amendment shall define a mechanism that enables the following:
  An AP MLD assigns a unique AID for each STA of a non-AP MLD during a multi-link setup
  Y:
  N:
  A:

## Slide 11: Appendix

## Slide 12: References
[1]: 11-19/1510 EHT Power saving considering multi-link (Jeongki Kim – LG Electronics)
[2]: 11-19/1526 Multi-Link Power-save (Abhishek Patil – Qualcomm)
[3]: 11-19/1528 Multi-Link Operation - Link Management (Abhishek Patil – Qualcomm)
[4]: 11-19-1536 Power Consideration for Multi-link Transmissions (Rojan Chitrakar – Panasonic)
[5]: 11-19/1544 Multi-link power save operation (Minyoung Park – Intel)
[6]: 11-19/1617 multi-link power save (Liwen Chu – NXP)
[7]: 11-19/1857 multilink power save followup (Liwen Chu – NXP)
[8]: 11-19/1904 MLO: Link Management (follow-up) (Abhishek Patil – Qualcomm)