## Slide 1: MLO: Efficient Paging
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-05-26

## Slide 2: Introduction
TID-to-link mapping feature allows each TID to be mapped to a separate link, or a set of links
  The set of links for each TID may be overlapping or disjoint
Non-AP MLD can retrieve data on subset of link(s) to which the TID is mapped
  by sending PS-Poll (or equivalent)
Non-AP MLD shall be able to get buffer unit (BU) indication on any link
  For power-save reasons, non-AP MLD can pick any one link to get notification about DL data
See appendix for related motions

## Slide 3: Potential solutions
Existing mechanism of traffic advertisement (single bit in TIM) works only when all TIDs are mapped to all or subset of links.
  However, when TID mapping is not fully overlapping, a non-AP MLD doesn’t know which TIDs the BU corresponding to and hence which link(s) to wake-up on to retrieve BUs
AP MLD needs to provide additional information to help non-AP MLD wake-up on the correct link(s)
Scheme 1: AP signals link information
  For example:
    Assign AID per link and set corresponding TIM bit to 1 [our initial approach]
    Explicit IE to provide link (or link set) information
Scheme 2: AP provides TID information
  For example, identify the TIDs for which the AP has BUs

## Slide 4: When does link based approach work?
Signaling link information (via per-AID based scheme or other) works under two extreme scenarios:
  Fully overlapped mapping (i.e., all TIDs map to subset or all links)
    In such case, AP provides the recommended link(s) and the non-AP MLD can pick all or subset to retrieve the BUs (for any TID)
  Disjoint mapping (i.e., one TID per link)
    In such case the recommended link clearly identifies the TID for the BUs
However, in practice, the set of links for each TID may be overlapping or disjoint
  In such case, providing a link recommendation doesn’t help and is ambiguous
    see example on next slide

## Slide 5: Problem with link-based indication (example)
Assume 3 links L1, L2, L3.
  Assume non-AP MLD is monitoring only L3
AP has BUs for a non-AP MLD corresponding to two TIDs
  TID 1 maps to L1 only
  TID 2 maps to both L1 and L2.
  AP wants to send an indication for BUs belonging to both TIDs.
AP recommends L1 & L2.
  Spec allows STA to pick any link. Therefore, STA picks L2.
  STA is unaware that BUs for TID 1 are stuck on L1.
  This may go on for a long time if AP has constant flow for traffic for TID 2.
One approach to address the above would be to fix the mapping for a set of TIDs to a set of links
  E.g., TID 0-3 maps to L1 and L2 and TID 4-7 maps to L3
  However, such approach would bring artificial restrictions to the protocol and take away some of the benefits of TID-to-link mapping

## Slide 6: Link based vs TID based
Initially we took an approach to solve the problem by assigning unique AIDs per link and identifying the link (via TIM bitmap)
However, as the spec development has progressed, we realized that link based signaling is ambiguous. Based on approved spec text:
    AP can signal BUs on any link [motion 52]
    TIDs can be mapped on overlapping or disjoint set of links [motion 54]
    STA can pick any enabled link(s) for a mapped TID to retrieve the BUs for that TID [motion 103]
    Non-AP MLD can operate on a subset of links to conserve power [motion 104]
    AP can recommend one or more link where it can serve the STA [motion 106]
  Based on the above, an AP MLD can recommend (#5) a set of links, but the ultimate choice lies with the non-AP MLD (#3) on which link(s) it wakes up to retrieve BUs.
Therefore, there is a need to signal the TID(s) for which APs has BUs
  Based on this, non-AP MLD would unambiguously know which link(s) it could wake-up on to retrieve the BUs

## Slide 7: Signaling TID information
TIM bit indicates BUs (of any TID) for a non-AP MLD
TID bitmap carried in the beacon indicates the TID(s) for which AP has BUs
  The field is carried only for the AIDs which had TIM bit set to 1
  TID bitmap is an 8-bit field, corresponding to each TID
The STA used TID to link mapping to decide which link(s) it should wake-up to retrieve the buffered MPDUs
0
0
1
0
AID:
1
1
0
0
1
0
0
1
0
0
1
0
0
…
…
…
…
…
…
12
28
35
57
77
0
TIM bitmap:
TID bitmap:
Size = 40 (5x8)
AID:12
AID:28
AID:35
AID:57
AID:77
11
13
27
34
56
76
29
36
58
78
255
1
0
0
0
1
0
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
Legacy

## Slide 8: Efficient TID signaling
Instead of signaling all TIDs (8-bits), the AP signals only 1 TID (3-bits)
  The TID that is signaled is based on certain criteria (TBD). Example:
    TID having the stricter latency requirement compared to other TIDs for which AP has BUs
    TID for which the AP has most amount of BUs
AP signals additional TIDs for which it has BUs via HE Control
  Define a new A-Control field (TID Control) to carry a bitmap consisting of 8-bits to signal each TID for which the AP has BUs
AP delivers MPDUs on the link where the STA wakes-up and the A-Control (TID Control) field of those MPDUs signals the additional TIDs for which AP has BUs
0
0
1
0
AID:
1
1
0
0
1
0
0
1
0
0
1
0
0
…
…
…
…
…
…
12
28
35
57
77
0
TIM bitmap:
AID:12
AID:28
AID:35
AID:57
AID:77
11
13
27
34
56
76
29
36
58
78
255
0
0
1
1
0
1
1
0
1
1
0
1
1
0
1
Legacy

## Slide 9: TID-mapping for R1
In order to keep things simple for R1, we recommend moving per-TID based mapping to R2
  i.e., in R1, all TIDs map to a subset of links
  By default, after ML setup, all TIDs map to all links

## Slide 10: Summary
This contribution provides an efficient mechanism to signal the TID(s) for which an AP MLD has BUs for a particular non-AP MLD
  Beacon (TIM) indicates BUs for a non-AP MLD
  Beacon also identifies a single TID for which the AP has BUs
  Additional TID(s) signaled via new A-Control field (TID Control)
The contribution also proposes to limit the scope of TID-to-link mapping for R1

## Slide 11: SP #1
Do you agree that in R1, all TIDs map to a subset of links?
  Note: By default, after ML setup, all TIDs map to all links
  Y:
  N:
  A:

## Slide 12: SP #2
Do you agree that 11be amendment shall provide a mechanism for a Beacon frame transmitted by an AP of an AP MLD to identify a single TID for which the AP has BUs for a non-AP MLD if the AP has indicated (via TIM element) that it has BUs for that non-AP MLD?
  Note: The TID that is signaled is based on certain criteria (TBD). Example:
    TID having the stricter latency requirement compared to other TIDs for which AP has BUs
    TID for which the AP has most amount of BUs
  Y:
  N:
  A:

## Slide 13: SP #3
Do you agree that 11be amendment shall provide a mechanism for individually addressed MPDUs transmitted by an AP of an AP MLD to a STA of a non-AP MLD to carry information of other TID(s) for which the AP has BUs?
  Y:
  N:
  A:

## Slide 14: SP #4
Do you agree that 11be amendment shall define a new A-Control field (TID Control) to carry a bitmap to identify each TID for which an AP has BUs?
  Y:
  N:
  A:

## Slide 15: Appendix

## Slide 16: References
[1]: 11-19/1955r0 Multi-link Operation: Per-link AID (Abhishek Patil, Qualcomm)
[2]: 11-19/1988 Power Save for Multi-link (Ming Gan, Huawei)
[3]: 11-20/066 Multi-link TIM (Young Hoon Kwon, NXP)
[4]: 11-20/084 Multi-link TIM design (Minyoung Park, Intel)

## Slide 17: Related Motions
802.11be defines a directional-based TID-to-link mapping mechanism among the setup links of a MLD.
  By default, after the multi-link setup, all TIDs are mapped to all setup links.
  The multi-link setup may include the TID-to-link mapping negotiation.
    TID-to-link mapping can have the same or different link-set for each TID unless a non-AP MLD indicates that it requires to use the same link-set for all TIDs during the multi-link setup phase.
      NOTE – Such indication method by the non-AP MLD is TBD (implicit or explicit).
  The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
    Format TBD.
      NOTE – When the responding MLD cannot accept the update, it can reject the TID-to-link mapping update.
  [Motion 54, [9] and [40]]
An AP of an AP MLD may transmit on a link a frame that carries an indication of buffered data for transmission on other enabled link(s).
  [Motion 52, [9] and [47]]
If a TID is mapped in DL to a set of enabled links for a non-AP MLD, then:
  The non-AP MLD can retrieve buffered BUs corresponding to that TID on any links within this set of enabled links
  The AP MLD can use any link within this set of enabled links to transmit data frames from that TID, subject to existing restrictions for transmissions of frames that apply to those enabled links.
    An example of restriction is if the STA is in doze state
  [Motion 103, [9] and [41]]
A non-AP MLD monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s).
  [Motion 104, [9] and [50]]
An AP MLD can recommend a non-AP MLD to use one or more enabled links.
  The AP’s indication could be carried in a broadcast or a unicast frame.
  [Motion 106, [9] and [48]]