## Slide 1: Multi-Link Device Instance & New Frame MAC Header
Date: 2019-11-07
Authors:
Name | Affiliations | Address | Phone | email
Huizhao Wang | Quantenna |  |  | hwang@Quantenna.com
Sigurd Schelstraete | Quantenna |  |  | 
Imran Latif | Quantenna |  |  | 
Debashis Dash | Quantenna |  |  | 

## Slide 2: Abstract
In this contribution we discuss the following topics for Multi-Link:
  Per SSID Multi-Link Device Instances & their Identities
  New Frame MAC header format for Multi-Link

## Slide 3: Multi-Link Device Instances & Their Identities (1)
Multi-Link Device entities will need to have their own IDs so that their IDs to be used in Multi-Link setup/teardown (association/disassociation), authentication exchange, management frame exchange, control frame & data frame exchange processes involved in Multi-Link.
Since association, authentication, security and QoS policies are binding to individual SSIDs (and SSIDs are usually applied to Multi-Link radios with the same profiles), for Multi-Link system, each unique SSID should have a corresponding Multi-Link Device instance ( or object) to represent the group of radio per Link Lower-MAC STAs which share the same SSID profile.
To differentiate multiple Multi-Link Device instances from each other, unique numeric ID values (range from {1, 255}) need to be assigned to Multi-Link Device instances. Optionally, unique MAC addresses can be assigned to Multi-Link Device instances as well.

## Slide 4: Multi-Link Device Instances & Their IDs (2)
Multi-Link
Device AP Instance
ID=1 for SSID1
Link1 AP
Lower-MAC
Link2 AP
Lower-MAC
Link3 AP
Lower-MAC
SSID1
SSID1
SSID1
Multi-Link
Device AP Instance
ID=2 for SSID2
Link1 AP
Lower-MAC
Link2 AP
Lower-MAC
Link3 AP
Lower-MAC
SSID2
SSID2
SSID2
Multi-Link
Device Instance
ID=N for SSID N
Link1 AP
Lower-MAC
Link2 AP
Lower-MAC
Link3 AP
Lower-MAC
SSID N
SSID N
SSID N
In an 802.11 AP or STA device, there can be one or more than one Multi-Link Device instances, each of the instances representing a unique SSID profile as the diagram showing here. The Multi-Link Device instancess are identified by their numeric ID numbers in the system.
The Multi-Link Device instances sometimes may need to have MAC address represented to Distribution System (DS) or Networking Stack, The Multi-Link Device instances can either reuse one of its Link’s Lower-MAC address or be assigned a unique MAC address by the network system admin.

## Slide 5: Multi-Link Frame MAC Header Format (1)
When a frame traverse through a Multi-Link system, its MAC header should contain information of transmitter Multi-Link Device Instance ID, receiver Multi-Link Device Instance ID, per Link Transmitter address (TA), per Link Receiver address (RA), frame’s source address (SA), and destination address (DA).
In order to carry the new information of transmitter Multi-Link Device instance ID and receiver Multi-Link Device ID, a new frame MAC header format is needed.
Different SSID profiles usually have different security policies, datapath forwarding rules and QoS policies. Using the new Multi-Link MAC header which contains the transmitter and receiver Multi-Link Device Instance IDs will help on:
  Per Link Lower-MAC can easily differentiate Multi-Link MPDU/MMPDU vs. regular MPDU/MMPDU.
  Forward the Multi-Link MPDU/MMPDU to Multi-Link Upper-MAC layer to process directly.
  At Multi-Link Upper-MAC layer, its processing logic can differentiate MMPDUs/MPDUs based on the transmitter/receiver Multi-Link Device instance IDs, and apply appropriated setup/teardown, security policies, datapath forwarding rules and QoS policies based on the SSID profile.

## Slide 6: Multi-Link Frame MAC Header Format (2)
Multi-Link Frame Format: red fields are new fields in MAC header, orange field is existing field with modified values to support Multi-Link Frame MAC header format: define Protocol version = 1 as indication of Multi-Link Frame MAC Header format is used:
Frame
Control
Duration
/ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
QoS
Control
HT
Control
CMMG
Control
MLE ID
1
MLE ID
2
MAC header
Frame
Body
FCS
Octets:
2
2
6
0 or 6
0 or 6
0 or 2
0 or 6
0 or 2
0 or 4
0 or 4
0 or 1
0 or 1
Protocol
version
Type
Subtype
To
DS
From
DS
More
Fragment
Retry
Power
Management
More
Data
Protected
Frame
+HTC
B0
B1
B2
B3
B4
B7
B8
B9
B10
B11
B12
B13
B14
B15
Bits:
2
2
4
1
1
1
1
1
1
1
1
Frame Control

## Slide 7: MLD Setup (Association) & Authentication Exchange Using Multi-Link MAC Header Format
STA Multi-Link
Upper-MAC Entity
Object
STA Link Lower-MAC
AP Multi-Link
Upper-MAC Entity
Object
AP Link Lower-MAC
Probe req (regular MAC header)
Probe rsp (regular MAC header + MLE Info)
Auth 1 (Multi-Link MAC header w/ MLE IDs)
Auth 2 (Multi-Link MAC header w/ MLE IDs)
Assoc req (Multi-Link MAC header w/ MLE IDs)
Assoc resp (Multi-Link MAC header w/ MLE IDs)
802.1x EAPOLs (Multi-Link MAC header w/ MLE IDs) (if 802.1x AKM is configured)

## Slide 8: MSDU Encapsulation Using Multi-Link Frame MAC Header (1)
In this proposal, Frame Control’s Protocol Version field with value 1 is defined to indicate the new Multi-Link frame MAC header is used
The two fields, MLD ID 1 and MLD ID 2, are used to identify the receiver side Multi-Link Device instance ID and the transmitter side Multi-Link Upper Device instance ID.
The encapsulation process of Multi-Link frame MAC header is depicted in below and the next page.
DA
type
SA
Payload
EtherType frame:
FC
Dur
RA
TA
DA
SC
SA
QC
HTC
SNAP+Type
Payload
RA: receiver per Link Lower-MAC addr
TA: transmitter per Link Lower-MAC addr
MLE ID1
MLE ID2
MLE ID1: receiver Multi-Link Device ID
MLE ID2: transmitter Multi-Link Device ID

## Slide 9: MSDU Encapsulation Using Multi-Link Frame MAC Header(2)
Multi-Link
Device AP instance
Multi-Link
Device STA instance
Link1 AP
Lower-MAC
Link2 AP
Lower-MAC
Link3 AP
Lower-MAC
Link1 STA
Lower-MAC
Link2 STA
Lower-MAC
Link3 STA
Lower-MAC
PC
PC
Upper layer Networking Stack
1. Packet originated from here:
With SA, DA, Type, QoS marking etc
In L2/L3 packet headers
2. Packets from the source device are encapsulated into
Multi-Link frame format with following fields assigned:
MLE ID1 = receiver Multi-Link Device ID
MLE ID 2 = transmitter Multi-Link Device ID
RA = receiver LinkX Lower-MAC address
TA = transmitter LinkX Lower-MAC address
DA = the packets’ DA
SA = the packets’ SA
TID = mapped from QoS marking
SN = the next SN of the TID from its Tx BA window
The results are MPDUs to be transmitted as S-MPDU, or
A-MPDU aggregation
3. Transmitter LinkX Lower-MAC assigns monotonic increase PN to each MPDUs and apply encryption on them.
4. Transmit as S-MPDU or A-MPDU
5. Receiver LinkX Lower-MAC receives each MPDUs
6. After CRC checking, decrypts the MPDUs, and conduct Rx replay checking on them
7. Pass the frames to the Multi-Link STA entity if they are Multi-Link frames
8. Multi-Link STA Entity sends BlockACK (partial state or full state)
8. Conduct Rx window reordering
9. Release the frames to the next stage of forwarding path, or to the Upper layer Networking Stack

## Slide 10: Conclusions
For 11be there are needs to define the framework of:
  Per SSID profile based Multi-Link Device Instance and its ID
  New Multi-Link frame MAC header format which contains transmitter/receiver Multi-Link Device IDs, which helps MLME and datapath to handle Multi-Link capable STAs and legacy STAs
  The use case of using the framework in Multi-Link system.

## Slide 11: SP 1
Do you agree that multiple instances of Multi-Link Device can exist in a 11be system?
Y/N/A

## Slide 12: SP 2
Do you agree that one Multi-Link Device instance represents one unique SSID profile?
Y/N/A
Note: a SSID profile contains: SSID string, RSN policy (or Open mode), datapath forwarding rules (optional), QoS policy (optional). An SSID profile can be applied to one or multiple Links.

## Slide 13: SP 3
Do you agree that each Multi-Link Device instance should have a unique ID (the ID can be a numerical value or MAC address) ?
Y/N/A

## Slide 14: SP 4
Do you agree that MMPDUs and MPDUs exchanges, in Multi-Link MLME and datapath, should optionally carry transmitter & receiver Multi-Link Device IDs, so that they can be properly dispatched to Multi-Link Device instances for processing?
Y/N/A

## Slide 15: SP 5
Do you agree that new Multi-Link MAC header format defined in page 6 should be included in 11be SFD?
Y/N/A

## Slide 16: References
IEEE 802.11-19-0773: Multi-Link Operation Framework
IEEE 802.11-19-0821: Multiple Band Operation Discussion
IEEE 802.11-19-1962: Multi-Link Security And Aggregation Operations