## Slide 1
Clarification on NGV indication
Date: 2019-11-11
Authors:

## Slide 2: Introduction
In 11bd SFD[1],
  “To transmit PPDU format up on request from upper layer, the PPDU format can be either 11p PPDU or 11bd PPDU.”
  “An 11bd STA shall indicate the NGV capability in MAC level, when transmitting an 11p PPDU.”
  “When an 11bd STA transmits an 11p group-addressed or unicast PPDU, the Duration/ID field of a frame in an 11p PPDU indicates that transmitter of the PPDU is an NGV capable STA.”
Since the decision of PPDU format is made by upper layer, current NGV indication scheme may cause legacy PPDU format propagation
In the July Session, this was discussed in MAC ad hoc but more discussion seems to be required.
  Y:6/N:4/A:many
In this contribution, current NGV indication scheme with upper layer consideration is investigated

## Slide 3: Recap: Indication of NGV Capability
To provide interoperability in coexistence case, 11bd devices indicate the NGV capability when it transmits 11p PPDU[2]
Case 2 causes 11p PPDU format propagation

## Slide 4: Is Case 2 allowed?  If “No”
If Case 2 is not allowed, no 11p PPDU format propagation.
However, this may cause backward compatibility issue with legacy STAs
  Since there is a time gap between the detection of legacy STA and the transmission of 11bd PPDU, legacy STAs may appear near the 11bd STA.

## Slide 5: Is Case 2 allowed?  If “Yes”
Case 2: Transmit 11p PPDU with 11bd capability after the reception of 11p PPDU with 11bd capability
  Current SFD allows Case 2: “To transmit PPDU format up on request from upper layer, the PPDU format can be either 11p PPDU or 11bd PPDU.”
However, there is no distinction of 11p PPDU from the first hop and the second hop, etc.
Since the detection range of 11bd is wider than 11p, propagation of 11p PPDU format would be fast.

## Slide 6: Is Case 2 allowed?  If “Yes”
In [4], timer based 11p STA detection was proposed but not accepted in SFD.
  Each time a NGV STA receives a 11p frame from a 11p STA, 11p neighbor timer is set to a threshold, e.g. 1000ms, and then counts down
    If no 11p frame from 11p neighbor is received until the timer becomes 0, the NGV STA assume no neighbor 11p STAs exist. It can transmit broadcast frames in NGV PPDUs.
This only applies to the first hop 11bd STA and the timer can not prevent the 11p PPDU format propagation.

## Slide 7: Is Case 2 allowed?  If “Yes”
Additional mechanism using timer and distance is required to prevent the unnecessary propagation of 11p PPDU transmission
Timer based legacy detection
  Once 11p PPDU with NGV capability is received, legacy detection timer is started.
  During the timer, if no 11p PPDU with NGV capability or 11p PPDU is received, STAs assume there is no 11p STAs.
Hop # information
  Hop # will tell the NGV STA how far the 11p STA is.
Combination of both timer and hop # will help upper layer to make a decision on PPDU format
  Hop # will prevent 11p PPDU with NGV capability propagation.
  Timer is used to go back to 11bd PPDU format

## Slide 8: Is Case 2 allowed?  If “Yes”
If 11bd OCB STA knows how far the legacy STA is away, upper layer can more proper decision.
Simple “Hop#” and “RSSI” information can help upper layer to choose proper PPDU format

## Slide 9: Additional Information to Help PPDU Format Decision
Hop # and/or RSSI can help 11bd devices to figure out how far the legacy device is.

## Slide 10: Conclusion
In this presentation, the transmission cases of 11p PPDU sent by 11bd devices are discussed
When 11bd detects 11p PPDU sent by 11bd device, it may use 11p PPDU format for robustness
  The PPDU format decision is made by upper layer
To prevent the unnecessary propagation of 11p PPDU transmission, more information on 11p device may be helpful for upper layer to make a correct decision on the proper PPDU format
  The information may include hop count, Rx RSSI, etc.

## Slide 11: Reference
[1] 19/0497r4 specification framework document
[2] 19/0018r0 NGV backward interoperability discussions
[3] 18/0861r9 IEEE 802.11 NGV SG Proposed PAR
[4] 19/0086r0 NGV Indication within Legacy 11p PPDU

## Slide 12: Straw poll 1
Do you agree with the following statement (Disable Case 2)?
  When an 11bd STA has only received 11p PPDU with NGV capability and has not received 11p PPDU from legacy STAs, it shall use 11bd PPDU format
Y/N/A

## Slide 13: Straw poll 2
[Case 2 is allowed]
Do you agree to add the following text into 11bd SFD?
  An 11bd STA shall indicate the hop number between the 11bd STA and the legacy device, when transmitting an 11p PPDU with NGV capability.
  The hop number is calculated by adding one hop to the hop number in the 11p PPDU with 11bd capability received from the previous 11bd STA.
    When STA’s hop number has not been decided, STA’s hop number is the received hop number +1.
    When STA’s current hop number is greater than the received hop number, hop number is updated to the received hop number +1.
  The hop number is indicated by adding a TBD additional value to the actual duration
Y/N/A

## Slide 14: Straw poll 3
Do you agree to add the following text into 11bd SFD?
  An 11bd STA shall indicate the RSSI of the previously received 11p PPDU, when transmitting an 11p PPDU with NGV capability.
Y/N/A