## Slide 1: 20MHz BW Operation Follow Up
Date: 2019-11-08
Authors:

## Slide 2: Recap: >10MHz Operation in NGV Channels
11bd allows 20MHz transmission in two continuous10MHz channels that legacy 11p STAs and 11bd 10MHz STAs exist.
  The medium access procedure should be defined to allow such operation.
>20MHz operation in 2.4/5/6GHz bands
  One 20MHz primary channel is defined, other 20MHz channels of the BSS operating channel are secondary 20MHz channels
  The backoff and NAV operation are based on:
    The Duration detected in the PPDU that covers the primary 20MHz channel.
    The PHY CCA detection in the primary 20MHz channel.
  The busy/idle detection in 20MHz channels other than the primary 20MHz channel is based on idle/busy checking within PIFS before the transmission.
  Several contributions in 11ac discussed the CCA improvement for legacy device coexistence, e.g. [1].

## Slide 3: PPDU BW Under 20MHz Operation
For a transmission between two NGV STAs that support 20MHz BW, the TXOP holder can decide whether 10MHz or 20MHz PPDU is used.
  When one of 10MHz medium is busy, the TXOP holder can use the idle 10MHz channel to transmit the frames to avoid delay.

## Slide 4: Primary Channel vs Secondary Channel
Within two continuous 10 MHz channels, one 10MHz channel is primary channel, another 10MHz channel is secondary 10MHz channel.
  The primary 10MHz channel is decided by up layer.
    Within 20MHz channel, All 20MHz STAs select the same 10MHz channel as the primary 10MHz channel.

## Slide 5: 20MHz Tx Backoff and Secondary Channel CCA
The PPDU which covers primary 10MHz channel is decoded based on CCA level -85dbm in primary 10MHz channel.
A 20MHz STA detects secondary 10MHz busy/idle per OFDM symbol detection (i.e. GI detection) with CCA level -85dbm.
A STA can do 20MHz PPDU transmission if the following condition are true:
  Option 1: Within the backoff procedure for the 20MHz transmission, both the primary 10MHz channel and the secondary 10MHz channel are idle when the backoff counter counts down.
Primary 10MHz channel
secondary 10MHz channel
Stop the backoff when primary 10MHz channel is busy.
Stop the backoff when secondary 10MHz channel is busy.
Bakoff procedure for 20MHz transmission
  Option 2: PIFS before the 20MHz transmission, the secondary 10MHz channel.

## Slide 6: Acknowledgement for 20MHz PPDU
In order to avoid EIFS recovery, 10MHz duplicate PPDU is defined to transmit the Ack/BA of 20MHz PPDU.
The tone rotation of secondary 10MHz is same as the tone rotation of secondary 20MHz of 802.11 baseline.
Primary 10MHz channel
secondary 10MHz channel
Stop the backoff when primary 10MHz channel is busy.
Stop the backoff when secondary 10MHz channel is busy.
Bakoff procedure for 20MHz transmission
QoS Data frame
Ack
Ack

## Slide 7: Straw Poll 1
Do you agree to add the following text to 11bd SFD:
  For a transmission from a NGV STA that support 20MHz BW, the transmitter can decide whether primary 10MHz or 20MHz PPDU is used after gaining channel access of 20MHz.

## Slide 8: Straw Poll 2
Do you agree to add the following text to 11bd SFD:
  Within a 20MHz channel, one 10MHz channel is OCB primary 10MHz channel, another 10MHz channel is OCB secondary 10MHz channel.
    The OCB primary 10MHz channel is decided by upper layer.
    Y: 16
    N: 0
    A: 7

## Slide 9: Straw Poll 3
Which one do you prefer:
  A STA can do 20MHz PPDU transmission if the following condition are true:
    Within the backoff procedure for the 20MHz transmission, both the primary 10MHz channel and the secondary 10MHz channel are idle when the backoff counter counts down.
  A STA can do 20MHz PPDU transmission if the following condition are true:
    The backoff counter in primary 10MHz channel becomes 0.
    PIFS before the 20MHz transmission, the the secondary 10MHz channel are idle.

## Slide 10: Straw Poll 4
Do you agree to add the following text to 11bd SFD:
  10MHz duplicate PPDU is defined to transmit the Ack/BA of 20MHz PPDU and the frames to protect 20MHz TXOP.
  The tone rotation of secondary 10MHz is same as the tone rotation of secondary 20MHz of 802.11 baseline.