## Slide 1: A-MSDU and A-MPDU
Date: 2019-11-08
Authors:

## Slide 2: Recap: A-MSDU/A-MPDU in 11bd SFD
11bd enables both A-MSDU and A-MPDU operation to work for unicast OCB and not to exceed the constraints on A-MSDU in A-MPDU as defined in 802.11ac.

## Slide 3: Recap: A-MSDU/A-MPDU in 11ac
A-MPDU related parameters of 11ac are from VHT Capabilities and HT Capabilities elements.
VHT Capabilities
HT Capabilities
A-MPDU Parameters

## Slide 4: A-MSDU, A-MPDU Support
We propose that all NGV STAs support A-MSDU and A-MPDU.
  Observation: all 11ac, 11ax devices implement these two features.
  As a relative new spec, there are no issues to support them.

## Slide 5: A-MSDU, A-MPDU Operation Options
Option 1: the parameters of A-MPDU and A-MSDU are defined by the spec where every NGV STAs support the same A-MSDU, A-MPDU operation parameters.
  Simple for inter-op between NGV STAs.
  No MAC data service interface change required.
  No BA negotiation is needed and BA operation is allowed.
Option 2: the parameters of A-MPDU and A-MSDU are announced by each NGV STA.
  Not good for inter-op.
  Provide some flexibility.
  Require MAC data service interface change to notify the peer STA’s parameters of A-MSDU/A-MPDU.
  No BA negotiation is needed and BA operation is allowed.
We prefer option 1.

## Slide 6: Fixed A-MSDU, A-MPDU Operation Parameters
Maximal MPDU Length: 7991 octets.
Maximal MPDU Start Spacing: 2us.
Buffer size: 32.

## Slide 7: MAC Data Service Change for A-MSDU/A-MPDU Parameters
With option 2, the up layer is used to acquire the A-MSDU/A-MPDU parameters.
The up layer needs to notify the MAC layer the peer STA’s A-MSDU/A-MPDU parameters for inter-op.
  Maximal MPDU Length.
  Maximal MPDU Start Spacing.
  Buffer size.

## Slide 8: Straw Poll 1
Which option do you prefer:
  Option 1: the parameters of A-MPDU and A-MSDU are defined by the spec where every NGV STAs support the same A-MSDU, A-MPDU operation parameters.
  Option 2: the parameters of A-MPDU and A-MSDU are announced by each NGV STA.