## Slide 1: Operation of Virtual BSS for Multi-AP Coordination
Date: 2019-11-05
Authors:

## Slide 2: Introduction
Multi-AP Coordination is a candidate feature being discussed in TGbe group
There are many categories of multi-AP coordination including joint processing, coordinate OFDMA, coordinated beamforming, AP selection, etc.
For the multi-AP coordination, cross-BSS operations (e.g. cross-BSS channel sounding) are often encountered
References [1-2] had proposed a virtual BSS architecture for multi-AP coordination
In this presentation, we further proposed two-level BSS implementation manner based on the virtual BSS architecture

## Slide 3: Virtual BSS Architecture for Multi-AP Coordination
  Multi-AP group setup procedure
  Multi-AP coordinator is the AP who initiates to set up a AP group.
    There is only one multi-AP coordinator in a AP group.
  Then the multi-AP coordinator will invite nearby APs to join in this AP group as member APs.
  Virtual BSS: An infrastructure BSS with a AP group.
  In the virtual BSS, temporal keys generated between STA and Coordinator. Coordinator performs data encryption/decryption and STA management
  Member APs served as a relay forwarding packets from coordinator and STA
Two-level BSS: A possible implementation manner is that, only when the link quality degrades to a certain threshold, then the STA will initiate to switch from the member BSS to the virtual BSS.
  Member BSSs are serving STAs that do not need the multi-AP coordinated transmission
    The reason is that the multi-AP coordinated transmission will introduce non-negligible signaling overhead
  The virtual BSS is serving STAs which need the multi-AP coordinated transmission, e.g.
    Frequently moving STAs, edge STAs, interfered STAs
Member AP
STA associated with virtual BSS
STA associated with member BSS
AP 1
(coordinator)
AP 2
AP 3
AP 4
BSS 1
BSS 2
BSS 3
BSS 4
Virtual BSS

## Slide 4: Benefits of Virtual BSS Architecture for Multi-AP Coordination
In virtual BSS, non-AP STA’s operation is almost identical to that of single BSS operation while getting benefit from multi-AP coordination [1-2].
  STA may receive packet from any AP within the virtual BSS
  Sounding procedure and beamforming feedback procedure is the same as single AP operation
  DL PPDU reception is the same as single AP PPDU reception
    Whether data is transmitted/beamformed by multiple APs or single AP is not important for data receive process
    Coordinated Beamforming PPDU is the same as downlink nulling
    Coordinated OFDMA PPDU is the same as OFDMA PPDU
    Joint Processed PPDU is the same as downlink MU-MIMO PPDU
Hence, under the virtual BSS architecture, the multi-AP coordination transmission can exploit existing signaling indication and sounding/feedback procedure, rather than redesign a new protocol

## Slide 5: Summary
In this presentation, a virtual BSS architecture is proposed for multi-AP coordination which can greatly reduce the change of current protocol
Two-level BSS implementation manner can efficiently avoid the signalling overhead introduced by multi-AP coordination

## Slide 6: References
[1] 11-19/1019, “Virtual BSS for Multi AP Coordination”
[2] 11-19/1451, “Virtual BSS for Multi-AP Coordination Follow-up”

## Slide 7: Straw Poll
Do you agree that the virtual BSS architecture should be adopted for multi-AP coordination?
  Yes
  No
  Abstain