## Slide 1
DMG in OCB environment
Date: 2019-11-12
Authors:

## Slide 2: Introduction
In 11bd SFD[1], OCB mode for DMG STAs has been agreed
  “11bd defines MAC sublayer functions and MLME extensions for DMG STAs in which dot11OCBActivated is true.”
Since there is no BSS concept in OCB environment, the operation in DMG STA needs modification
  Including the Beacon Interval concept and the sector sweep operation
  Considering non-applicable contention process for DMG STAs
In this contribution, considerations on the modification points of DMG operation in OCB mode are discussed

## Slide 3: Recap: Beacon Interval(BI) in DMG STAs
The basic operation in DMG STAs is performed by periodic BIs
  The sector sweep operation is done in BHI, initiated by multiple Beacon frame transmissions

## Slide 4: Recap: Beam training operation by Beacon frame
Beam training initiated by Beacon frame[2]:
  Beam training operation is initiated by multiple transmissions of Beacon frames in Beacon Header Interval
  Other STAs respond with sector sweep (SSW) frames in association beamforming training (A-BFT) period
DBcn
DBcn
DBcn
DBcn
Discovery Mode = 1
A STA
Peer STA1
SSW
SSW
Peer STA2
SSW
SSW
SSW-FB
SSW-FB
time
SSW
SSW
A peer STA sweeps sectors using SSW frames
Another peer STA sweeps sectors

## Slide 5: Selection procedure of initiator of Beam training operation
The role of beam training initiator cannot be decided by a contention process in 60 GHz because of hidden node problem
  Due to LOS characteristics of 60GHz, there are many hidden nodes as shown in the figure
  Using 5.9 GHz signal is one of ways to resolve such hidden node problem

## Slide 6: 60 GHz Scenarios (V2I, V2V)
In the proposed 60 GHz use cases, static STA can act as an AP
  In V2I scenario: RSU can act as an AP
  In V2V scenario: Header STA may act as an AP
    How to form a V2V communication group and select a header STA is done at application layer level.
The proposed use cases, static environment is assumed
  Static position of infrastructure in V2I transmission
  Static relative positions of vehicles in V2V transmission

## Slide 7: The use of 5.9 GHz transmission to support 60 GHz transmission
To help 60 GHz transmission, 11bd device may transmit information of 60 MHz transmission using 5.9 GHz band
  In V2V scenario, the leader vehicle may manage the 60 GHz communication using 5.9 GHz signal
    E.g., Beamforming training initiation time

## Slide 8: The use of 5.9 GHz transmission to support 60 GHz transmission
To help the 60 GHz transmission, 11bd device may transmit information of 60 MHz transmission using 5.9 GHz band
  In V2I scenario, the transmitter of 60 GHz signal may broadcast the information using 5.9 GHz signal
    E.g., Beamforming training initiation time

## Slide 9: Conclusion
In this contribution, the transmission procedure of DMG OCB STAs is presented
Without the concept of BSS, the decision method for beamforming training operation and initiator selection are needed
  The contention-based operation in 60 GHz is not recommended in OCB environments
5.9 GHz signals may help to address and initiate 60 GHz transmission
  Detailed information carried over 5.9GHz is TBD

## Slide 10: Reference
[1] 19/0497r4 specification framework document
[2] 19/1162r2 OCB for 60GHz

## Slide 11: Straw poll
Do you agree to use 5.9 GHz signal to indicate 60 GHz transmission and relative parameters?
Y/N/A