## Slide 1: Power Save for Multi-link
Date: 2019-11-11
Authors:

## Slide 2: Background
Multi-link feature not only increases the throughput[1], but also can improve latency performance by duplicate transmission[2]
However, power consumption issue[3] becomes more serious when multi-link feature is implemented at the STA, especially for the battery powered non-AP STA
  More than one link operate concurrently
  More than one link maintenance work, such as DL traffic delivery, BSS or link parameters update
  In this work, we focus on power save mechanisms for multi-link, including
  The necessity for primary link
  DL traffic delivery
  BSS or link specific parameters update and TWT setup

## Slide 3: Primary link
In 802.11 ax, we have (D)TIM, (U)-APSD, WNM, TWT, intra-PPDU and so on.
For the multi-link device (MLD), the above features could be implemented at each link
However, the power consumption increases linearly with the number of links
  Take beacon reception shown in the following figure for an example, the power consumption is doubled
STA based primary link is proposed to address the above issue
  The STA MLD does not need to receive the beacon on a non-primary link with the aid of primary link
Link 1
Link 2
Beacon
Beacon
Link 1
Link 2
AP
STA
PM =1 for Link 1&2
awake
awake
Beacon
Beacon
awake
awake
skip
skip

## Slide 4: Primary link
Before the primary link selection, the AP MLD will broadcast the set of primary links candidates through the beacon frame
  Based on the set of primary links candidates, each STA could choose its own primary link
  Primary link selection could be done in the phase of association or could be changed after the association
  The power consumption for the non-primary link could be reduced if the following work could be done in the primary link
  DL traffic delivery notification
  BSS or link specific parameters update notification
  Note: the above activities could be done without primary link
AP1/ 2.4G
AP2/ 5G
AP4/ 6G
STA1/ 2.4G
STA2/ 5G
STA/ 2.4G
STA1/ 5G
STA2/ 6G
Primary link 1
MLCD STA 2
MLCD STA 3
Primary link 2
Primary link 3

## Slide 5: DL traffic delivery
DL traffic delivery notification for a non-primary link is proposed to be sent on the primary link
  DL traffic includes group addressed MSDUs/MMPDUs and individual addressed MSDUs/MMPDUs
To support the above DL traffic delivery notification for a non-primary link , we propose to reuse the existing TIM element
  Use the same Partial Virtual Bitmap field in the TIM element to indicate whether there are buffered BUs for the primary link and non-primary link
  Assign another AID to a STA in non-AP MLD on non-primary link, corresponding to one bit in Partial Virtual Bitmap field
  For a STA in Non-AP MLD on non primary link，the buffered BUs could either be individual addressed BU or both two kinds buffered of BU
  Moreover, there may exist two options to notify the DL traffic buffered at the AP for a STA in non-AP MLD on non-primary link
  A unified notification for both group addressed BUs and individual addressed BUs, no necessity to separate them because of the same target-wake up the non-primary link
  Have two notifications for group addressed BUs and individual addressed BUs, respectively

## Slide 6: DL traffic delivery
Regarding group addressed BU delivery, there may exist divergence
  Opt1: deliver the group addressed BUs on the related link, no any change for the route of this kind of traffic (prefer)
  Leave it to implementation specific at AP side
  but need provide group addressed BUs notification for one link through another link
  Note: this scheme does not require the non-AP MLD to have a primary link, but with overhead notification instead
  Opt2: AP duplicates the group addressed BUs on all the links [4] and sends them on a or some links
  The non-AP MLD is required to have a primary link
  However, it will increase power consumption for some STAs on the primary link
  The transmission time for the group addressed BU on the primary link will increase significantly
  The duplicated group addressed BUs from the non-primary link may not be needed for some STAs on this primary channel, such as single link STA and legacy STA

## Slide 7: Link specific parameters update and TWT setup
Besides the DL traffic delivery notification in the primary link, link/BSS specific parameters update for non-primary link could also be done in primary link
  No need to wake up the non-primary link frequently to receive the new link specific parameters
  BSS parameter update could be done by follows
  Opt1: Provide the detailed updated parameters
  Opt2：Provide the BSS parameter update notification like Check Beacon field in TIM Broadcast (prefer)
TWT setup could be done in one link for another link [5]
To support both the peak throughput and power save, the same TWT parameters could be applied for more than one link
  Target Wake time (assume the same TSF for all the links, could have a further discussion on it)
  Nominal Minimum TWT Wake Duration
  TWT Wake Interval Exponent and TWT Wake Interval Mantissa
Link 1
Link 2
STA
awake
awake
awake
awake
awake
awake
TWT SP
TWT SP

## Slide 8: Summary
Power save mechanism is proposed based on primary link
  Primary link is STA based
  DL traffic delivery notification could be sent on one link for another link
  The STA on non-primary link in a Non-AP MLD does not need to receive its beacon frame if there is primary link
  An AP in an AP MLD shall provide BSS specific parameters update for another AP in the same AP MLD
  TWT setup could be done in one link for another link，and the same TWT parameters could also be applied for more than one link

## Slide 9: References
[1] IEEE 802.11-19/1291r3 Performance aspects of Multi-link operations
[2] IEEE 802.11-19/1101r1 Conditional Packet Duplication in Multiple Link System
[3] IEEE 802.11-19/1231r3 Multiband and Multichannel Operation in IEEE 802.11be
[4] IEEE 802.11-19/1526r0 multi-link power save
[5] IEEE 802.11-19/1510r0 power saving considering multi-link

## Slide 10: SP 1
Do you agree that not every STA operating in PS mode in a non-AP MLD is required to receive the beacon frames periodically
  This is an exemption besides the existing ones, such as individual TWT agreement, WNM sleep mode and NonTIM mode

## Slide 11: SP 2
Do you agree that an AP in an AP MLD shall provide BSS specific parameters update for another AP in the same AP MLD
  The detail for BSS specific parameters update is TBD

## Slide 12: SP 3
Do you agree that an AP in an AP MLD shall provide DL traffic notification for another AP in the same AP MLD
  The detail for DL traffic notification is TBD

## Slide 13: SP 4
Do you agree that the a TWT could be set up between a AP MLD and a non-AP MLD for more than one setup link?

## Slide 14: SP 5
Do you agree that each non-AP MLD should select one primary link to monitor DL traffic indication and BSS parameter update

## Slide 15: SP 6
Do you agree that the AP MLD assigns an AID to each STA of the non-AP MLD in the phase of association?