## Slide 1: Broadcast Demonstration
Date: 2019-11-12
Authors:

## Slide 2: Abstract
This presentation introduces an implementation and demonstration of the concept of eBCS.

## Slide 3: Notes
This implementation is just a technical proof of concept.
The TGbc features and technologies are under discussion.
The features and technologies might be adjusted in the TGbc amendment.
Although TGbc discusses Downlink (AP->STA) and Uplink (STA->AP) broadcasting, this implementation addresses only Downlink broadcast streaming.
Service discovery and scanning are not implemented.
  Channel is pre-configured
Although this demonstration uses only 100 STAs, the system can support thousands of STAs without additional airtime occupation.

## Slide 4: Introduction of TGbc
Scope of the project (PAR)
  This amendment specifies modifications to the IEEE 802.11 medium access control (MAC) specifications that enable enhanced transmission and reception of broadcast data both in an infrastructure BSS where there is an association between the transmitter and the receiver(s) and in cases where there is no association between transmitter(s) and receiver(s).
  This amendment introduces origin authenticity protection for broadcast data frames.

## Slide 5: TGbc Use Case 1: Stadium Video Distribution (11-19/268r5)
Stakeholders
  Stadium system operators
  Stadium audience, coaches and referees
  Broadcasters, e.g., Live TV
  Manufacturers of semiconductor, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reuse existing technology while reducing cost and implementation complexity
Service scene
  An eBCS AP provides eBCS for videos to a large number of densely located STAs, which may be mobile devices.
  An eBCS AP provides multiple eBCSs for multiple video streams, e.g.:
    live video feed/Video Highlights Replay
    Videos from different angles of the game (e.g., in soccer)
    Videos of different sport activities that take place in parallel (e.g., athletics)
Required function
Providing enhanced Broadcast Services (eBCS) for videos to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be STAs that do not transmit.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 6: A Part of Requirements of TGbc (11-19/151r5)
The 802.11bc amendment shall provide origin authenticity protection for broadcast data frames.
The 802.11bc amendment shall support modes of operation:
  a) in an infrastructure BSS where there is an association between the transmitter and the receiver(s)
  b) in cases where there is no association between transmitter(s) and receiver(s).

## Slide 7: Expected Functions of eBCS AP (11-19/850r0)
An eBCS AP receives contents stream and transmits them by eBCS protocol.
  An eBCS AP may receives multiple contents streams from single or multiple servers and transmits them.
  An eBCS AP should decide which contents to be broadcasted by eBCS according to the contents identifier.
  An eBCS AP should treat all contents streams equally.
An eBCS AP should advertise contents information such as human readable contebnts title, contents identifier, etc.
AP
Multicast Frames
eBCS Frames
Multicast Frames
Multicast Frames
Server
Server
Server

## Slide 8: Existing 802.11 vs This Implementation
 | Existing 802.11 | This Implementation
Association | Required | No association
STA transmission | Required (at least Authentication / Association) | No transmission
Frame authentication | GTKSA Insufficient for public use (11-19/451r5) | Digital Signature with TESLA Sufficient for public use (11-19/451r5)

## Slide 9: Frame Sequence (11-19/451r5)
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
  eBCS Info frame includes
  Ks,N (where s is the seq num of eBCS Info)
  Ks-1,L (where L is the last used key index)
  Ks-1,L+1 (if d = 2)
  Timestamp
  TI
  TK
  d
  eBCS Info sequence number
  Public key with CA signature
  Signature by the sender’s private key
Sender generates one-way key chain before
generating each eBCS Info frame
(Ks,N, Ks,N-1, Ks,N-2, …, Ks,0)
  eBCS Data frame includes
  Ks,i+2 (where s is the seq num of eBCS Info, d=2)
  As,i (Authenticator generated by the key K’s,i)
  Key index: i
  eBCS Info seq num: s

## Slide 10: Demonstration System
Broadcast
bcstx
bcsap
IP multicast
Broadcast AP
bcssta
bcsrx
Storage
nginx
bcsplay
Web server
Broadcast STA
Storage
nginx
bcsgenci
IP multicast
Scope of TGbc
HTTP server
HTTP server
Write contents information
(Title, Dst IP addr/port, File list…)
Camera
TESLA key generation
Add TESLA authenticator (eBCS Data frame)
Generate eBCS Info frame
Serialize, compress contents and divide into packets
LDPC-Triangle for redundancy (RFC5170)
Transmit packets as IP multicast
Receive frames through PCAP
Process eBCS Info frame
Authenticate eBCS Data frame
Transmit packets as IP multicast
Poll contents
Display contents
Reconstruct contents
Write to the storage
HTTP Live
Streaming
(unicast)
HTTP Live
Streaming
(unicast)

## Slide 11: Parameters
WLAN
  2.4GHz
  20MHz bandwidth (Ch11)
  IEEE 802.11n (HT) MCS3 for eBCS Data
  IEEE 802.11n (HT) MCS1 for eBCS Info
eBCS
  Digital signature: RSA2048
  Hash for TESLA: SHA256
  eBCS Info interval (TI): 1s
  TESLA Key Change Interval (TK): 100ms
Application Layer
  LDPC-Triangle
  Code rate: 2/3
  Packet transmission interval: 1ms

## Slide 12: Demonstration Video

## Slide 13: Brief Evaluations
Airtime occupation
  6Mbps (Data 4Mbps, Parity 2Mbps)
  25%
  We used HT MCS3 by hardware and regulatory restrictions
  Higher rate will make lower occupancy.
Security
  Confirmed that the following frames were dropped
    Wrong timestamp
    Wrong signature (eBCS Info)
    Wrong authenticator (eBCS Data)

## Slide 14: References
11-18/825r9, A PAR Proposal for BCS
11-18/826r9, A CSD Proposal for BCS
11-19/151r5, 802.11bc Functional Requirements Document
11-19/268r5, TGbc use case document
11-19/451r5, eBCS Frame Authentication Proposal
11-19/850r0, Expected Total System Architecture
11-19/1802r1, TESLA Improvement
IETF RFC5170, Low Density Parity Check (LDPC) Staircase and Triangle Forward Error Correction (FEC) Schemes
HTTP Live Streaming (HLS), https://developer.apple.com/streaming/