## Slide 1: Revisit DMG multi-band discovery forwarding
Date: 2019-11-11
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony |  |  | kazuyuki.sakoda(at)sony.com
Mohamed Abouelseoud | Sony |  |  | Mohamed.Abouelseoud(at)sony.com

## Slide 2: Agenda
Recap: why we are talking about this feature
Recap: what is DMG multi-band discovery assistance
What is the problem and what is missing in D5.0
Our previous discussion
New direction/activities
Discussion

## Slide 3: Motivation
802.11ay introduces DMG multi-band discovery assistance feature to ease forming opportunistic network, i.e., 60GHz mesh network, while maintaining low-latency and robust communication
However, the current DMG multi-band discovery assistance requires association to an AP per a request for discovery assistance
It is preferable to extend the assistance coverage beyond the AP to find neighbor DMG STAs efficiently
TGay had discussions if we should extend the feature, but did not come to the conclusion to include it
This presentation revisits the DMG multi-band discovery extension once again, and suggest to reconsider extending the feature

## Slide 4: Recap: why we are talking about this feature (1)
High-bandwidth, low-latency, and robust communication is a key to high quality VR type of application [1]
Ideally, the latency should be bounded < 3~10 msec over the air in order to satisfy system requirements [2]
There are many other application that benefits low latency capability
However, 802.11ad/ay DMG Beacons / exhaustive SSW could occupy the airtime continuously beyond the latency boundary
Big chunk of BHI should be eliminated

## Slide 5: Recap: why we are talking about this feature (2)
We also think that multi-AP type of network configuration is helpful to enhance range and robustness of the 60GHz network
Potentially introduce multi-hop communication on top of the 802.11ay MAC/PHY
Even if the routing and forwarding resides on layer 3, 802.11ay should provide tool set to enable such operation on layer 2, such as efficient neighbor discovery and opportunistic link establishment
  The same concept as DN-DN link for fixed wireless access use case with TDD DMG STA

## Slide 6: Recap: why we are talking about this feature (2)
Source
(DN)
DN
Sink
(DN)
Source
(DN)
Sink
(DN)
DN
DN

## Slide 7: Recap: why we are talking about this feature (3)
What we thought:
  It is preferable to make DMG beaconing (SSW beaconing) flexible enough not to block streaming data transfer, i.e., make it on-demand fashion
  Assume that typical DMG STA is dual/triple band capable, and collocates with STA operating at lower band such as 2.4/5GHz
  A new STA wishing to get onboard a neighboring 60GHz network should be able to find neighbor DMG STAs greedily, even if the neighboring DMG STAs are not performing exhaustive SSW beaconing all times
  Use lower band link to help new STA discovering neighboring DMG STA and joining a DMG BSS
   Motivation for DMG multi-band discovery assistance

## Slide 8: Recap: what is DMG multi-band discovery assistance
5GHz AP1 announce its discovery assistance capability (DA Enabled) in Muti-band element in its Beacon/Probe Response frame on lower band. DEV5 (5GHz STA5) recognizes that AP1 has collocated DMG AP1.
DEV1: Existing Device
DEV5: New Device wishing to onboard
DEV1
DEV5
DMG AP1
5GHz AP1
DMG STA5
5GHz STA5
DA Enabled
DA Enabled

## Slide 9: Recap: what is DMG multi-band discovery assistance
DEV5 (5GHz STA5) wishes to join the network, and joins the 5GHz BSS of AP1
DEV1: Existing Device
DEV1
DEV5
DMG AP1
5GHz AP1
DA Enabled
Association
Association
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5

## Slide 10: Recap: what is DMG multi-band discovery assistance
DEV5 (5GHz STA5) requests discovery assistance on 60GHz. DEV1 (5GHz AP1) recognizes the request and schedule DMG AP1’s SSW on 60GHz
DEV1: Existing Device
DEV1
DEV5
DMG AP1
5GHz AP1
DA Enabled
Association
FST Setup Req. /w DA
FST Setup Req. /w DA
Schedule SSW on 60GHz
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5

## Slide 11: Recap: what is DMG multi-band discovery assistance
DEV1 (5GHz AP1) respond with assistance agreement and let DEV5 know of the SSW schedule on 60GHz. DEV5 recognizes when and which channel to scan 60GHz channel
DEV1: Existing Device
DEV1
DEV5
DMG AP1
5GHz AP1
DA Enabled
Association
FST Setup Resp. /w DA
FST Setup Resp. /w DA
FST Setup Req. /w DA
Schedule SSW on 60GHz
Schedule scan on 60GHz
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5

## Slide 12: Recap: what is DMG multi-band discovery assistance
DMG AP1 performs TXSS at the designated time. If DMG STA5 can receive the signal, it will start communication with DMG AP1 over 60GHz channel.
DEV1: Existing Device
DEV1
DEV5
DMG AP1
5GHz AP1
DA Enabled
Association
FST Setup Resp. /w DA
FST Setup Req. /w DA
Schedule SSW on 60GHz
Schedule scan on 60GHz
TXSS
Communication
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5
TXSS
Communication

## Slide 13: What is the problem? (1)
We envision that multi-AP type of network configuration is helpful. It is preferable that the newly joining DEV5 can find multiple neighbor STAs
To ask for a discovery assistance, the DEV5 needs to associate to all of its potential neighbor DEVs one by one
DEV1: Existing Device
DMG AP1
5GHz AP1
DMG STA2
5GHz STA2
DMG STA3
5GHz STA3
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5
DEV2: Existing Device
DEV3: Existing Device

## Slide 14: What is the problem? (2)
It will be time consuming to repeat asking for discovery assistance one AP after another
There is no guarantee that all the existing DEV in its neighborhood operate 5GHz AP. Some of them might be STA associating to an AP
At the time of scanning, some Wi-Fi driver software may filter duplicate SSID and report back selected AP only to its application (Your laptop and phone only report on SSIDs (not each AP) responding to the scan request)

## Slide 15: What is missing in D5.0 (1)
It would be great if DEV5 can collect all potential neighbor’s SSW information via DEV1 so DEV5 (5GHz ST5) only needs to associate to an AP, and the AP will coordinate the discovery assistance request to its neighbor STAs
DEV1: Existing Device
DMG AP1
5GHz AP1
DMG STA2
5GHz STA2
DMG STA3
5GHz STA3
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5
DEV2: Existing Device
DEV3: Existing Device

## Slide 16: What is missing in D5.0 (2)
Upon reception of DA request, DEV1 forwards the request info to its neighbor STAs, and let them schedule the SSW to ease discovery from DEV1. AP1 respond back aggregated response to STA5.
DEV1: Existing Device
DMG AP1
5GHz AP1
DMG STA3
5GHz STA3
DEV5: New Device wishing to onboard
DMG STA5
5GHz STA5
DEV3: Existing Device
DEV1
DEV5
DA Enabled
Association
FST Setup Resp. /w DA
FST Setup Req. /w DA
TXSS
DEV3
DA Req. Forwarding
DA Req. Response
TXSS
Schedule SSW on 60GHz
Schedule scan on 60GHz
Schedule SSW on 60GHz

## Slide 17: Our previous discussion
This problem and suggested solution have been discussed in TGay [3][4], and even normative text was ready for review [5]
However, the group did not come to the conclusion to accept the proposal, probably because people thought the use case and the requirements are rare case…
But, wait! We started to see some new directions/activities in 802.11 community and beyond.

## Slide 18: New direction/activities (1)
Real time communication:
  RTA TIG walked through requirements on real time applications. It is recognized that low latency communication should be an important KPI in new application space. This argument is definitely valid to 60GHz technology as well.
  Looking into telecom world, low latency capability is getting to be one of the most compelling value proposition of 5G, a.k.a. URLLC.
  DMG discovery assistance and its proposed extension is all about low latency, high throughput, and robustness. TGay should provide enough tools to design a system meeting the requirements

## Slide 19: New direction/activities (2)
Probably, OOB discovery is going to be more popular:
  Some people may think multi-band/out-of-band discovery is not going to be useful or popular. At least in history, it was.
  However, 802.11ax is also talking about OOB discovery and they started to take it more serious these days [6][7]
  We do not need to be shy to leverage OOB discovery in 802.11. Rather, TGay should define complete set of OOB discovery features

## Slide 20: New direction/activities (3)
Wi-Fi sensing, 60GHz, multi-static radar:
  SENS TIG has been kicked off. One of the candidate technology/application is 60GHz multi-static radar [8]
  The use case assumes multiple DMG STA deployment in a neighborhood at consumer spaces, which is pretty similar to what [1] envisions
  It is possible that multi-AP type of deployment will be even more popular together with the use of 60GHz Wi-Fi sensing technology

## Slide 21: New direction/activities (4)
TGay is going to specify more details on management functions to design DN/CN with TDD mode [9]
  It sounds to be reasonable, as TGay will be providing more complete set of tools to form opportunistic networks over 802.11ad/ay devices

## Slide 22: Discussion
Should TGay consider to define a bit more complete set of tool to make multi-band discovery efficient?

## Slide 23: References
[1] 802.11-18/194r1 “Distribution network use case for consumer devices,” Kazuyuki Sakoda, et.al.
[2] 802.11-18/2009r6 “IEEE 802.11 Real Time Applications TIG Report,” Kate Meng, et.al.
[3] 802.11-19/19r1 “Proposed resolution of CID 3518”, Mohamed Abouelseoud, et.al.
[4] 802.11-19/868r0 “Multi-band comments resolution”, Mohamed Abouelseoud, et.al.
[5] 802.11-19/20r0, “Proposed resolution of CID 3518 text”, Mohamed Abouelseoud, et.al.
[6] 802.11-18/1922, “Considerations on 6GHz Discovery,” Thomas Derham, et.al.
[7] 802.11-18/1966, “6GHz – Out-of-band discovery discussion,” Laurent Cariou, et.al.

## Slide 24: References
[8] 802.11-19/1551r1 “Wi-Fi sensing in 60GHz band,” Alecsander Eitan, et.al.
[9] 802.11-19/1517r0, “TDD beamforming configuration,” Payam Torab, et.al.