## Slide 1: Broadcast Ack Operation
Date: 2020-01-12
Authors:
Onn Haran, Autotalks

## Slide 2: Is Broadcast Needed? Only Groupcast?
  Groupcast assures delivery within group: platooning, negotiation
  Groupcast (many-to-many) ≠ Multicast (one-to-many)
  Broadcast assured delivery is valuable as well, for example:
  Left Turn Assistance: A vehicle driving straight would benefit from assured delivery to a vehicle on opposite road about to turn left
  Crossing pedestrian: Assured delivery of cooperative perception message to vehicles approaching the pedestrian
  New 5.9GHz bandplan in US may limit 11bd to operate only when shared with WiFi. Reliability is decreased due to increased channel usage, hence Broadcast protection is essential

## Slide 3: Setup and Teardown Should be Eliminated to Scale to All-to-All Negotiation
X
X

## Slide 4: Pre-agreed Parameters
Parameter | Possible values | Pre-agreed value
Policy | Immediate / Delayed | Single recipient message (BlockAck): Immediate Multi-recipient message (if added): Sequenced
Buffer size | 0-1023 | 1 Only content of most recent message is relevant. No reason to acknowledge older messages
The same parameters should be applied by all supporting devices without negotiation

## Slide 5: Capability Support
  Alternative #1: Mandatory
  All NGV devices would be required to respond to BlockAckReq
  Delivery can be always assured
  Alternative #2: Optional
  A bit in NGV MAC header indicates BlockAckReq support
  Flexible
Alternative #2 is recommended

## Slide 6: Naming Convention
  A unique name should represent the dedicated messages
  Block is a bad term since only a single message is acknowledged
  Suggesting BroadcastAck
  BroadcastAckReq
  BroadcastAck

## Slide 7: Multiple Requests
  Multiple requests are sent to the stations
  Reminder: stations are identified by upper layer
  Retry when a single station failed to acknowledge
  After retry: No need to send requests to stations previously acknowledged
Broadcast / Groupcast data
BroadcastAckReq
Originator
Recipient #1
Recipient #2
BroadcastAck
BroadcastAck
BroadcastAckReq
Broadcast / Groupcast data
Retransmission

## Slide 8: BroadcastAckReq Format
Frame control
Octets
2
Duration
2
RA
6
TA
6
BAR control
2
BA information
2
Ack policy
1
Multi-TID
1
Compressed
1
GCR mode
2
Reserved
7
TID
4
Bits
Value
0
0
0
10
0
0
Unused combination
FCS
4
Fragment number
4
Starting sequence number
8
0

## Slide 9: BroadcastAck Format
Frame control
Octet
2
Duration
2
RA
6
TA
6
BAR control
2
BA information
3
FCS
4
Value
As in BlockAckReq
Starting sequence number
2
Bitmap
1
Octet
1 bit reports last message from TA, either Broadcast or Groupcast

## Slide 10: Adjustment to Requested Feedback from Multiple Recipients
Multiple changes are needed across the specification, but all are minor
For example, 10.24.3 “Data and acknowledgement transfer using immediate block ack policy and delayed block ack policy”
If an immediate block ack policy is used, the recipient shall respond to a Basic BlockAckReq frame with a Basic BlockAck frame. If the all recipients sends the Basic BlockAck frame, the originator updates its own record and retries any frames that are not acknowledges in the Basic BlockAck frame, either in another block or individually

## Slide 11: On Using Regular ACK
  Common BlockAck usage (acknowledging many messages at once) is overkill for BroadcastAck usage (acknowledging a single message)
  Regular ACK is simpler, and would have been suggested to this task, had it worked
  ACK frame follows the data frame. Deferred polling of ACK isn’t supported
A modification of Regular ACK might have fit the needs, but that theoretical modification becomes very similar to BlockAck
In summary, we recommend to base the solution on BlockAck

## Slide 12: Straw Poll #1
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall allow Broadcast and Multicast reception feedback based on BlockAck. Upper layer initiates the request and selects the recipients.”
Y:
N:
A:
January 2020
Onn Haran, Autotalks