## Slide 1: Multiple RU Support for 11be
Date: 2020-01-09
Authors:

## Slide 2: Introduction
In the September 2019 meeting, 11be task group has approved that 11be shall allow more than one RUs to be assigned to a single STA [1].
In [2] and [3], dividing RU sizes into small {26,52,106} and large {242,484,996} was discussed.
In this contribution, we address the four possibilities of multiple RU allocation.

## Slide 3: Options of Multiple RU Allocation
Considering that the multiple RUs should be supported to enhance the spectral efficiency with increasing complexity as little as possible, we can sequentially think the following options of multiple RU allocation for 11be.
    Option 1: new RU type
      Defines the new RU sizes (e.g. RU26+RU52 becomes 78-tone RU)
      Coding across multiple RUs
    Option 2: RU aggregation
      Aggregation of contiguous or non-contiguous RUs
      Coding across multiple RUs using new module like RU parser
    Option 3: multiple independent RUs to a single STA
      Combinations of contiguous or non-contiguous RUs
      Independent coding for each RU
    Option 4: puncturing

## Slide 4: Option 1: New RU Type
We consider only contiguous RU allocation in this option.
The new RU type is defined by combining multiple RUs.
  For example, RU26+RU52 becomes 78-tone RU.
Need to define BCC inter-leaver as well as LDPC tone mapper for new RU size
In order to reduce the complexity increase in defining the new RU type, the following things should be considered.
  The number of RUs that can be combined should be limited.
    In order to reduce the number of possible RU combinations
    For example, RU combinations of RU26+RU26+RU26 is not useful because AP can allocate RU52+RU26 to that STA.
  The number of RU combinations should be limited.
    In order to reduce the scheduling and signaling complexity
    For example, the combinations of contiguous RUs within each 20MHz can be introduced.
    For example, RU26+RU484 can not be applicable because it does not increase the spectrum efficiency much.
Therefore, balancing between complexity and the number of supported RU combinations is important.
This option can reuse the existing signaling method in 11ax by expanding RU Allocation subfield.

## Slide 5: Option 2: RU Aggregation
Contiguous or non-contiguous RUs are aggregated.
Option 2 can reuse the existing transmitter procedure excepting that this needs new module like RU parser after encoding.
In terms of de-interleaving and decoding latency, Option 1 and Option 2 are not so different because PHY will typically do the following two stage mapping:
  From RU allocation, find out which RU or RUs are allocated the receiving STA
  From RU indices, find out subcarriers indices
However, in terms of signaling, Option 2 increases the latency because we either need multiple mapping engine (then we need to know what's the maximal aggregation order) or do it sequentially for aggregated RUs.
Parser
PSDU
RU 1
RU N
Encoder

## Slide 6: Option 3: Multiple Independent RUs to a Single STA
The bits are distributed into multiple RUs before encoding or there are multiple PSDU corresponds to each RU. Then, the bits in each RU are encoded independently.
Similar to Option 2, Option 3 also needs new module like RU parser before encoding or changes in MAC (multiple PSDUs).
It provides higher flexibility (regarding MCS) than Option 2. But, there is no frequency diversity gain among multiple RUs due to separated encoding.
Parser
Encoder 1
PSDU
Encoder N
RU 1
RU N
Encoder 1
Encoder N
RU 1
RU N
PSDU 1
PSDU N
or

## Slide 7: Pros and Cons of Options 1, 2 and 3
 | Pros | Cons
Option 1: new RU type | Low complexity increase Similar signaling method in 11ax | Limited flexibility of combinations Need to define new inter-leaver and LDPC tone mapper
Option 2: RU aggregation | Flexibility of aggregations Fully utilizes the diversity gain | Higher complexity than Option 1 Higher signaling overhead than Option 1 which may increase latency Needs new module like RU parser Significantly increases the number of RU combinations
Option 3: multiple independent RUs to a single STA | Full flexibility regarding aggregations and MCS | Highest complexity increase Needs new module like RU parser or changes in MAC (multiple PSDUs) Higher signaling overhead than Option 1 Full diversity gain is not achieved.

## Slide 8: Option 4: Puncturing
Option 4 is for combining RUs by allowing RU/RUs to be punctured.
This option is suitable for large size RUs because introducing preamble puncturing of <20MHz in 11be will have coexistence issue with legacy devices [4].
In terms of signaling, this option can utilize the existing signaling method in 11ax to indicate the assigned multiple RUs of large size.
  For example, Bandwidth field to tell which 20MHz is punctured and use RU size by RU Allocation subfield which includes entire RU/BW, punctured and non-punctured RUs
    Bandwidth field == 4 (puncturing secondary 20MHz from 80MHz) + RU Allocation subfield == 208 means that 996 tone RU with secondary 20MHz is punctured (RU combination of RU242+RU484).

## Slide 9: Summary
Four options of 11be for support of assigning one or more RUs to a single STA in EHT MU PPDU are addressed.
    Option 1: new RU type
    Option 2: RU aggregation
    Option 3: multiple independent RUs to a single STA
    Option 4: puncturing
Pros and cons of Option1, 2 and 3 have been discussed.
For small size RUs, Option 1 is preferred because it provides not only the better performance with full diversity gain but also implementation convenience.
For large size RUs, Option 4 is preferred due to the signaling and implementation convenience.

## Slide 10: Straw Poll 1
Do you support that small-size multiple RUs can be combined and assigned to a single STA as a new RU type?
  Small-size RUs: RU26, RU52, RU106

## Slide 11: Straw Poll 2
Do you support that large-size multiple RUs can be combined and assigned to a single STA by allowing RU/RUs to be punctured?
  Large-size RUs: RU242, RU484, RU996

## Slide 12: Reference
[1] 11-19/1262r6, Specification Framework for TGbe.
[2] 11-19/1907r0, Multiple RU Combinations for EHT.
[3] 11-19/1908r0, Multi-RU Support.
[4] 11-19/1869r0, Preamble Puncturing and RU Aggregation.