## Slide 1: Considerations of FCC NRPM on 11bd
Date: 2020-1-12
Authors:
Onn Haran, Autotalks

## Slide 2: Enabling WiFi in U-NII-4 is FCC’s Prime Target
  FCC plans to allocate lower 45MHz to unlicensed WiFi
  FCC doesn’t plan to conclude WiFi sharing study
  If plan would be accepted, dedicated V2X Spectrum will be squeezed to 30MHz
  No room for future V2X services, needed for safety enhancement: Cooperative perception (sensor sharing) / Pedestrian / Platooning bandwidth needs cannot be ignored
Automotive industry consensually asks to maintain 75MHz for V2X

## Slide 3: Proposal: Add a Mode of 11bd Sharing in U-NII-4
11bd is based on the assumption of full 75MHz V2X usage
We propose to add a mode of operation in case 40MHz will be taken by FCC
  Other countries (Japan / EU) aren’t impacted
  In that unfortunate scenario, sharing can mitigate stakeholders aspiration
  FCC: Fast approval of exclusive WiFi usage
  Automotive: Protected V2X operation
  802.11bd PAR: 2x throughput requirement using 20MHz
  Proposal: 802.11bd shall develop and validate a sharing scheme
  Tiger team study can be used as a baseline

## Slide 4: No Legacy 10MHz V2X Channels Would Exist in Band Taken from V2X
  Sharing 20MHz channels is the only possible option if FCC takes the 40MHz band
  10MHz channels wouldn’t exist in that case
  Proposal: 802.11bd shall add a new mode for 20MHz operation, without considering 10MHz legacy channels
  Header: plain 11a header (no duplicated 10MHz header)
  Mask: no need for 10MHz channel compliant mask
  Channel access: no need to check for 10MHz activity
  Other V2X technology is more challenged to share band with WiFi
167
175

## Slide 5: V2X should be Prioritized if Shared with WiFi
  Multiple options can be considered, such as:
  Option A: Detect-and-Vacate
  WLAN stops using V2X channels for certain period after detecting 11bd header
  Option B: Raising V2X channel access priority
  For example, shorter DIFS or higher CCA for non-V2X
  Option C: Minimizing non-V2X traffic in V2X preferred channels
  For example, 173 / 177 cannot be primary channels
167
175

## Slide 6: Wide V2X Channels should be Considered
  A wider V2X channel is better for WiFi when sharing
  V2X would send messages in shorter time
    Unlicensed 160MHz channel degrades to 80MHz regardless if V2X uses 20, 40 or 80MHz
  A wider V2X channel serves better V2X
  Higher positioning accuracy
  Simpler management of V2X services (less channels)
  Simpler V2X hardware (less radios)
  Proposal: Define 40/80MHz V2X channels
171
167
175
163

## Slide 7: Straw Poll #1
Do you agree that 802.11bd shall add 20MHz channel operation mode, without co-existence with legacy 10MHz?
Y:
N:
A:
January 2020
Onn Haran, Autotalks

## Slide 8: Straw Poll #2
Do you agree that 802.11bd shall define and validate WiFi sharing scheme?
Y:
N:
A:
January 2020
Onn Haran, Autotalks

## Slide 9: Straw Poll #3
Do you agree that 802.11bd shall define wider channels (40/80MHz) for effective WiFi sharing?
Y:
N:
A:
January 2020
Onn Haran, Autotalks