## Slide 1: Proposed Corrections to Channel Access Issues in 802.11
Date: 2020-01-05
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari |  |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  |  |  | matthew.fischer@broadcom.com

## Slide 2: Abstract
This presentation discusses the following channel access issues in 802.11 which if fixed will help 802.11 performance as well as its coexistence with other wireless technologies.
Resetting the Contention Window Size (CWS) of AC_VO after transmission of 802.11 beacons.
Multiplexing of data of secondary ACs of lower priority along with the primary AC in DL and UL OFDMA in 802.11ax.

## Slide 3: Discussion: Issue 1
CWS for a given Access Category (AC) determines the random wait time for accessing the channel by traffic of that AC.
  Feedback regarding transmission failure is used to double the CWS, assuming that transmission failure is caused by collisions which would be reduced by doubling the CWS and increasing the random wait time.
  Feedback regarding transmission success is used to reset the CWS to CWmin, in order to reduce the random wait time and increase transmission efficiency.
802.11 beacons use exponential backoff with AC_VO (except when they contain CSA or TIM broadcast).
  However, beacons do not have feedback on transmission success/failure. So, beacons cannot double the CWS but whenever transmitted they reset the CWS.
The issue arises when beacons are transmitted along with traffic that has error feedback and uses AC_VO.
  Such traffic can double the CWS depending upon error feedback. However, the CWS will be reset on beacon transmission.
  This would amount to ignoring information about congestion/collision even when they are available.
There are other unlicensed technologies where management traffic is transmitted more frequently and has flexible mapping of such management traffic to AC.
If these technologies adopt the same principle, transmission of management traffic will lead to resetting the CWS of any AC.
This would mean that all traffic irrespective of the AC and availability of error feedback will mostly use the minimum CWS for that AC. This would defeat the principle of updating the CWS based on information about congestion/collision.

## Slide 4: Discussion: Issue 1 (continued)
Hence, it is proposed to not reset the CWS following the transmission of an 802.11 beacon i.e. the CWS for AC_VO shall not be reset following the transmission of a beacon.
Note:
  This procedure doesn’t mean that 802.11 beacons will be forced to use a higher CWS long after transmission of data traffic with error feedback that used AC_VO and may have increased the CWS. This is because the CWS can be reset to CWmin after a configurable number of retries at a given CWS or at CWmax.
  The same principle of CWS update for transmission of data without error feedback has been agreed in 3GPP for NR-U ([1]).

## Slide 5: Discussion: Issue 2
Traffic multiplexing rules in 802.11ax do not state any restrictions on the priority of traffic that can be transmitted in a TXOP acquired by a certain AC.
In contrast, in 802.11ac, multiplexing of traffic of different ACs is allowed only for MU-MIMO and with the following restriction: “The inclusion of secondary AC traffic in a VHT MU PPDU shall not increase the duration of the VHT MU PPDU beyond that required to transport the primary AC traffic ”
The same rule is not extended to 11ax, where it is merely stated (in 10.23.2.7) that the TXOP limit of the primary AC shall not be exceeded: “The inclusion of secondary AC traffic in an HE MU PPDU shall not cause the TXOP limit of the primary AC to be exceeded.”
In contrast, the ETSI-BRAN harmonized standard for 5 GHz ([2]) puts restrictions on the priority of traffic transmitted in a TXOP acquired using a certain access category : “4.2.7.3.2.6 Initiating Device Channel Access Mechanism: 6) The Channel Access Engine may start transmissions belonging to the corresponding or higher Priority Classes.”.
Similar restrictions have been put on 3GPP LAA (sections 5.7.0 and 5.7.2 of [3]) and NR-U.
Hence, the same principle of fairness, coexistence with other technologies including 802.11ac and abidance to regulations should be followed in 802.11ax and 802.11be.

## Slide 6: Proposals
Proposal 1:
  The CW for AC_VO shall not be altered following the transmission of an 802.11 beacon.
Proposal 2:
  The traffic multiplexing rules in 802.11be and 802.11ax shall require that for both DL and UL, for triggered as well as contention-based modes and for SU as well as MU-MIMO/MU-OFDMA transmissions, the following rule is followed:
    The duration of transmission shall not be longer than the minimum required to transmit the traffic of equal or higher priority relative to the access category that was used to obtain access to the channel (i.e. the primary AC).

## Slide 7: References
[1] 3GPP RAN1 #99, Chairman’s notes, Section 7.2.2.2.1
[2] ETSI EN 301 893 V2.1.9
[3] 3GPP TS 36.300 V15.7.0