## Slide 1: Consideration on 240/160+80 MHz and Preamble Puncturing
Date: 2020-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In the November F2F meeting, TGbe decided to support 240/160+80 MHz transmission
  240/160+80 MHz consists of three 80MHz channels including primary 80MHz and the tone plan of each 80MHz is the same as the 11ax 80MHz tone plan
One of the remaining issues on 240/160+80 MHz transmission is how to determine three 80MHz channels
  Fixed case by defining 240MHz channelization
  Flexible case by MAC indication
  Flexible case by PHY indication
We discuss this issue and also deal with a bandwidth indication method including preamble puncturing in SU and MU PPDU

## Slide 3: 240/160+80 MHz Channel (1/4)
Fixed case – 240MHz channelization
  240MHz channelization can be defined similar to 20/40/80/160 MHz
  This approach is reasonable in consideration of the current band plan in 5GHz and 6GHz
    In some bands (e.g., UNII8), contiguous 240MHz can be supported but contiguous 320MHz is not possible
    Since different regulation applies to each band, it may not be feasible to make a wide bandwidth across multiple bands
    Regardless of the 320/160+160 MHz channel, the 240/160+80 MHz channel can be defined, i.e., 240MHz BSS can be defined
  We don’t need any additional mechanism to determine and indicate three 80MHz channels
  The gain may be less than using flexible 240/160+80 MHz channel in terms of efficiency
  Additional hardware requirements may need to be defined
 Static 240/160+80 MHz channel

## Slide 4: 240/160+80 MHz Channel (2/4)
Flexible case – MAC indication (e.g., Beacon)
  AP determines three 80MHz channels (i.e., one 160MHz channel and one 80MHz channel) used for 240/160+80 MHz transmission and indicates it via a management frame
    It may be performed in 320MHz BSS
    Before PPDU transmission, STAs acquire the exact channel information for 240/160+80 MHz
    PHY signaling may be simple
  The mechanism to select three 80MHz channels is required but it is performed on a long-term basis
  It may be less flexible than the PHY indication case
 (semi-) Static 240/160+80 MHz channel

## Slide 5: 240/160+80 MHz Channel (3/4)
Flexible case – PHY indication (e.g., U-SIG, EHT-SIG)
  If 240/160+80 MHz PPDU is transmitted, the exact channel information is indicated in the PHY signaling field
    Several fields can be considered which contain bandwidth information, preamble puncturing pattern information or RU information
    The PHY signaling overhead may be high
  It is the most flexible method in terms of the channel availability because several types (maybe three types) of 240/160+80 MHz are possible
  The 240/160+80 MHz channel depends on the 320/160+160 MHz channel
    240/160+80 MHz transmission is possible only in 320MHz BSS
    240/160+80 MHz can be even indicated as one of the 320/160+160 MHz bandwidth modes
 Dynamic 240/160+80 MHz channel

## Slide 6: 240/160+80 MHz Channel (4/4)
Summary
  For a simple PHY signaling and low PHY overhead, we slightly prefer (semi-) static channel cases, i.e., fixed case with 240MHz channelization or flexible case with MAC indication
    Efficiency can be sufficiently enhanced by preamble puncturing or multiple RU aggregation already defined in 11be
 | Pros | Cons
Fixed case with channelization (Static channel) | 240MHz BSS possible No need for any additional mechanism to determine the channel Simple PHY / MAC signaling | Less gain in terms of efficiency Additional hardware requirements may be required
Flexible case with MAC indication ((semi-)Static channel) | Simple PHY signaling Receiver knows the exact 240/160+80 MHz channel in advance | MAC needs a mechanism to determine the channel Relatively less gain in terms of efficiency
Flexible case with PHY indication (Dynamic channel) | Most flexible in terms of channel availability Better gain in terms of average throughput | Complex PHY signaling Receiver needs to acquire the exact 240/160+80 MHz channel information from the PHY signaling field

## Slide 7: Bandwidth and Preamble Puncturing Indication for SU PPDU (1/4)
We propose the following fields to indicate the bandwidth and the preamble puncturing pattern for SU PPDU
  Bandwidth field in the version dependent field of U-SIG
    Modification of the 11ax bandwidth field
  Preamble puncturing field in the version dependent field of U-SIG
  Preamble puncturing pattern field in EHT-SIG

## Slide 8: Bandwidth and Preamble Puncturing Indication for SU PPDU (2/4)
We propose the following bandwidth field which is in the version dependent field of U-SIG for both static and dynamic channels
The exact channel information of 240/160+80 MHz can be indicated in the bandwidth field for the dynamic channel case as in [1]
  If the bandwidth field doesn’t have this different mode information, the receiver needs to acquire the exact 240/160+80 MHz channel information from the preamble puncturing pattern field
  0: 20MHz
  1: 40MHz
  2: 80MHz
  3: 160MHz and 80+80MHz
  4: 240MHz and 160+80MHz
  5: 320MHz and 160+160MHz
  6~7: reserved
  0: 20MHz
  1: 40MHz
  2: 80MHz
  3: 160MHz and 80+80MHz
  4: 240MHz and 160+80MHz mode 1
  5: 240MHz and 160+80MHz mode 2
  6: 240MHz and 160+80MHz mode 3
  7: 320MHz and 160+160MHz

## Slide 9: Bandwidth and Preamble Puncturing Indication for SU PPDU (3/4)
Whether preamble puncturing is applied to the PPDU can be also indicated in the bandwidth field as shown below
As an alternative way, a certain 1 bit field (i.e., preamble puncturing field) can be defined in the version dependent field of U-SIG
By doing so, the preamble puncturing pattern field described in the next slide can be used for other purposes or just dropped when preamble puncturing is not applied
  Of course, if preamble puncturing is not indicated early, the preamble puncturing pattern field is always required
  Note that the dynamic channel case still needs the preamble puncturing pattern field if the exact 240/160+80 MHz channel information is not indicated in the bandwidth field although preamble puncturing is indicated early
0: 20MHz
1: 40MHz
2: 80MHz non-preamble puncturing mode
3: 160MHz and 80+80MHz non-preamble puncturing mode
4: 240MHz and 160+80MHz non-preamble puncturing mode
5: 320MHz and 160+160MHz non-preamble puncturing mode
6: preamble puncturing in 80 MHz
7: preamble puncturing in 160 MHz or 80+80 MHz
8: preamble puncturing in 240 MHz or 160+80 MHz
9: preamble puncturing in 320 MHz or 160+160 MHz
10~15: reserved

## Slide 10: Bandwidth and Preamble Puncturing Indication for SU PPDU (4/4)
The preamble puncturing pattern field can be defined in EHT-SIG
  Even in SU PPDU, 20MHz based preamble puncturing can be applied by reusing the minimum CCA bandwidth resolution defined in the conventional Wi-Fi
  In this case, a simple bitmap method can be employed
    E.g., 1 bit per 20MHz can be used except for primary 20 (0: punctured, 1: used for transmission)
  Depending on the bandwidth, the total number of bits can be different
    3, 7, 11 and 15 bits can be used for 80MHz, 160/80+80 MHz, 240/160+80 MHz and 320/160+160 MHz, respectively
    For the dynamic channel case, 240/160+80 MHz transmission needs 15 bits if the exact 240/160+80 MHz channel information is not indicated in the bandwidth field
  We can further reduce the bit size by limiting possible preamble puncturing patterns

## Slide 11: Bandwidth and Preamble Puncturing Indication for MU PPDU (1/4)
We propose the following fields which are obtained by modifying the corresponding 11ax fields to indicate the bandwidth and the preamble puncturing pattern for MU PPDU
  Bandwidth field in the version dependent field of U-SIG
  RU allocation and Center 26-tone RU fields in the common field of EHT-SIG
  User field in the user specific field of EHT-SIG

## Slide 12: Bandwidth and Preamble Puncturing Indication for MU PPDU (2/4)
We propose the bandwidth field which has the following descriptions and those in the bandwidth field of 11ax and this field is contained in the version dependent field of U-SIG
  240MHz and 160+80MHz non-preamble puncturing mode
  320MHz and 160+160MHz non-preamble puncturing mode
  preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
  preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
  preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
  preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
Note that we assume that the EHT-SIG structure is the same as HE-SIG-B and if we decide to use a different EHT-SIG structure, the descriptions can be changed

## Slide 13: Bandwidth and Preamble Puncturing Indication for MU PPDU (3/4)
The descriptions in the previous slide can be used for both static and dynamic channel cases but the descriptions may mean different patterns between static and dynamic channel cases
  The fixed case and flexible case with MAC indication (i.e., static channel case) have the same patterns because only one 240/160+80 MHz channel is possible
  While in the flexible case with PHY indication (i.e., dynamic channel case), the patterns can be slightly different from the static channel cases since three modes are possible for 240/160+80 MHz channel
  In Appendix, the detailed non-preamble puncturing and preamble puncturing patterns are described for both static and dynamic channels
For the dynamic channel case, different modes of 240/160+80 MHz can be indicated in the bandwidth field to reduce the overhead for RU allocation and user fields

## Slide 14: Bandwidth and Preamble Puncturing Indication for MU PPDU (4/4)
RU allocation and user fields indicate the RU plan of each 20MHz channel and user information assigned to each RU, respectively, and they can be defined in EHT-SIG (common and user specific fields, respectively)
  By using these field, the preamble puncturing pattern can be also identified at receivers if preamble puncturing is applied
  According to the bandwidth, the total number of bits for the RU allocation field can be different because this field exists in each 20MHz channel
  For the dynamic channel case, if exact 240/160+80 MHz channel information is not indicated in the bandwidth field, the RU allocation field for 240/160+80 MHz also requires the same amount of bits used in 320/160+160 MHz

## Slide 15: Conclusion
We have discussed how to determine 240/160+80MHz channel
  Fixed case with channelization
  Flexible case with MAC indication
  Flexible case with PHY indication
  We slightly prefer the static channel case
We have also proposed some fields to indicate the bandwidth and preamble puncturing patterns in SU and MU PPDU
  SU PPDU
    Bandwidth field in the version dependent field of U-SIG
    Preamble puncturing field in the version dependent field of U-SIG
    Preamble puncturing pattern field in EHT-SIG
  MU PPDU
    Bandwidth field in the version dependent field of U-SIG
    RU allocation and Center 26-tone RU fields in the common field of EHT-SIG
    User field in the user specific field of EHT-SIG
 Static channel
 Dynamic channel

## Slide 16: Straw Poll #1
Which option do you prefer for the 240/160+80 MHz channel?
  Option 1: Fixed case with 240MHz channelization
  Option 2: Flexible case with MAC indication (e.g., Beacon frame)
  Option 3: Flexible case with PHY indication (e.g., U-SIG, EHT-SIG)
Option 1/Option 2/Option 3/A: ///

## Slide 17: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to SU, the bandwidth field having 3 bits is contained in the U-SIG as one of the version dependent fields and has the following descriptions
    0: 20MHz
    1: 40MHz
    2: 80MHz
    3: 160MHz and 80+80MHz
    4: 240MHz and 160+80MHz
    5: 320MHz and 160+160MHz
    6~7: reserved
Y/N/A: //

## Slide 18: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to SU, the preamble puncturing field having 1 bit is contained in the U-SIG as one of the version dependent fields and has the following descriptions
    0: Preamble puncturing is not applied to the PPDU
    1: Preamble puncturing is applied to the PPDU
  Note: The field name can be changed
Y/N/A: //

## Slide 19: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to SU, the preamble puncturing pattern field having TBD bits is contained in EHT-SIG
    Detailed descriptions are TBD
    Note: The field name can be changed
Y/N/A: //

## Slide 20: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to MU, the bandwidth field having TBD bits is contained in the U-SIG as one of the version dependent fields and has the following descriptions as well as the descriptions of the bandwidth field for HE MU PPDU
    240MHz and 160+80MHz non-preamble puncturing mode
    320MHz and 160+160MHz non-preamble puncturing mode
    preamble puncturing in 80 MHz, where in the preamble only the secondary 20 MHz is punctured
    preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
    preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
    preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
    preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
  Other descriptions are TBD
Y/N/A: //

## Slide 21: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to MU, the RU allocation and Center 26-tone RU fields having TBD bits are contained in the common field of EHT-SIG
    The RU allocation and Center 26-tone RU fields indicate the RU plan similar to that used in HE MU PPDU
    Detailed descriptions are TBD
Y/N/A: //

## Slide 22: Straw Poll #7
Do you agree to add the following text to the TGbe SFD?
  For the PPDU transmitted to MU, the User field having TBD bits is contained in the user specific field of EHT-SIG
    The User field indicates user information assigned to each RU similar to that used in HE MU PPDU
    Detailed descriptions are TBD
Y/N/A: //

## Slide 23: References
[1] 802.11-19/1889r2 Discussion on 240MHz Bandwidth

## Slide 24: Appendix Non-Preamble Puncturing and Preamble Puncturing Patterns for MU PPDU

## Slide 25: Preamble Puncturing Patterns for Primary 80
In each description for preamble puncturing, P80 has the following preamble puncturing pattern
  preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
  preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble only the secondary 20 MHz is punctured
  preamble puncturing in 240 MHz or 160+80 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
  preamble puncturing in 320 MHz or 160+160 MHz, where in the primary 80 MHz of the preamble the primary 40 MHz is present, and at least one 20 MHz subchannel that is not in the primary 40MHz is punctured
:Punctured
P40
S40

## Slide 26: Static Channel (1/3)
We assume the following channel is used for 320MHz non-preamble puncturing
Then, for the static channel, one of the following three patterns can be used for 240/160+80 MHz non-preamble puncturing
  PPDU is transmitted by using P80, S80 and H80
  PPDU is transmitted by using P80, S80 and L80
  PPDU is transmitted by using P80, L80 and H80
Three patterns above can be simply classified into two cases, i.e., 240MHz with S80 and without S80
  E.g.,
Static 240MHz with S80
Static 240MHz without S80

## Slide 27: Static Channel (2/3)
For the static 240/160+80 MHz channel with S80, the following preamble puncturing patterns can be indicated as 240/160+80 MHz preamble puncturing
  At least one of the 20MHz channels in the 80MHz channel which is not in P160 is used for transmission regardless of whether any 20MHz channels in S80 are used for transmission
For the static 240/160+80 MHz channel with S80, the following preamble puncturing patterns can be indicated as 320/160+160 MHz preamble puncturing
  At least one of the 20MHz channels in the 80MHz channel which is not included in the 240/160+80 MHz channel is used for transmission
: at least one 20MHz channel is used for transmission
: don’t care whether any 20MHz channel is used for transmission or not

## Slide 28: Static Channel (3/3)
For the static 240/160+80 MHz channel without S80, the following preamble puncturing patterns can be indicated as 240/160+80 MHz preamble puncturing
  At least one of the 20MHz channels in the S160 is used for transmission
For the static 240/160+80 MHz channel without S80, the following preamble puncturing patterns can be indicated as 320/160+160 MHz preamble puncturing
  At least one of the 20MHz channels in S160 as well as at least one of the 20MHz channels in S80 is used for transmission
 If no 20MHz channel is used in S160, it is preamble puncturing in 160/80+80MHz

## Slide 29: Dynamic Channel (1/2)
For the dynamic channel, all of the following three patterns can be indicated as 240/160+80 MHz non-preamble puncturing
  PPDU is transmitted by using P80, S80 and H80
  PPDU is transmitted by using P80, S80 and L80
  PPDU is transmitted by using P80, L80 and H80

## Slide 30: Dynamic Channel (2/2)
For the dynamic channel, all of the following preamble puncturing patterns can be indicated as 240/160+80MHz preamble puncturing
  At least one of the 20MHz channels in only one of the 80MHz channels in S160 is used for transmission regardless of whether any 20MHz channels in S80 are used for transmission
  No 20MHz channel in S80 is used for transmission and at least one of the 20MHz channels in S160 is used for transmission
For the dynamic channel, the following preamble puncturing patterns can be indicated as 320/160+160MHz preamble puncturing
  At least one of 20MHz channels in each of S80, L80 and H80 is used for transmission