## Slide 1: MLA: Sync PPDUs
Date: 2020-03-14
Authors:

## Slide 2: Background
Motion #38
Move to add the followings to the 11be SFD:
A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
Note - The 2 links are on different channels
Note - Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.
Motion #46
Move to add the following to the 11be SFD:
Shall allow a multi-link device that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links?
  Signaling of this constraints is TBD

## Slide 3: Motivation
As a follow-up to Motions #38 and #46, we provide some considerations in this presentation
We focus on a very common scenario in this presentation:
  STR-AP with non-STR STA
MLO offers:
  Throughput gain by concurrent transmissions on multiple links at the same time
  Latency improvements by contending on multiple channels

## Slide 4: Terminology
STR (simultaneous Tx and Rx)
  An MLD that is capable of simultaneous Tx/Rx on multiple links for the given set of links
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on all links)

## Slide 5: Terminology: Sync PPDUs
  To achieve start time alignment, a modified EDCA can be used to access the 2nd link (see next slide)
  If start time alignment is not allowed: Start times may be different. End time is aligned
      + This mode is possible for DL (assuming AP is STR capable). AP counts down on each link independently
      + Not possible for UL, except for adding additional signaling
Two types of Sync PPDUs. Both have end-time aligned (within SIFS)

## Slide 6: Sync Mode EDCA Access – essentially EDCA with truncated countdown
On the 2nd link
  The link performs normal EDCA countdown. If the countdown is on-going at the time the TXOP is acquired on the 1st link, the countdown counter is set to 0 instantly to allow the STA to tx on the link
  In that way, PD/NAV on 2nd link will be honored i.e., don’t access if NAV is set on 2nd link. Disruption to the 2nd link is largely addressed
    Can add further rules to limit the access to the 2nd link if needed e.g., 2nd link access only if RBO < a TBD Threshold value (configurable by AP)
Compare to 80 + 80 access
  80 + 80 does not check NAV on the 2nd link
  SMEA can further limit the access on the 2nd link by setting some threshold on the RBO

## Slide 7: Pitfalls of No Sync PPDUs
11be protocol needs to be able to handle bi-directional traffic
However, when bi-directional traffic is present, the UL traffic would wipeout a significant portion of the DL
  This would bring down the overall system throughput as the medium time for the lost DL is wasted
  UL transmission can lead to full DL loss if the DL’s pre-amble is hit

## Slide 8: Pitfalls of No Sync PPDUs (Cont’d)
Neither option is good (Note BAs are not shown for simplicity)
Option 1: STA Tx on Link 2 while Rx on Link 1
Option 2: STA Holds on countdown on Link 2 while Rx on Link 1

## Slide 9: The Proper Solution – Sync PPDUs
Guarantees fair medium access between AP and STA and no Tx/Rx collisions between links

## Slide 10: How Sync PPDUs can work with STR AP + Non-STR STA
STA/AP gets access to L1 | UL | DL
L2 is IDLE and SMEA is used on L2 | L1+L2: Sync’ PPDUs See slide here. | L1+L2 : Sync’ PPDUs See slide here.
L2 is IDLE and SMEA is not used | L1: S1 sends PPDU1 to A1 L2: can be used for UL/DL for Sy. No constraints S2 cannot use until PPDU1-end-time UL: blocked due to CCA. See slide here. | L1: A1 sends PPDU1 to S1 L2: can be used for one of these: UL/DL for Sy. No constraints. See slide here. A2 sends DL for S2, with end-time same as PPDU1. S2 will not use L2 for UL. See slide here.
L2 is BUSY@PPDU1 start, but later became IDLE during PPDU1 |  | 
Multiple Primary channels allowed

## Slide 11: Conclusion
To take full advantage of MLO, Sync PPDUs should be used for STR-AP + Non-STR STA configuration
If a non-STR STA is associated with an AP that does not align the end times of the PPDUs, the following will suffer:
  Performance (i.e., throughput and latency. As shown in our simulation results (to be provided separately))
  Power consumption of the STA
To meet the Non-STR constraints, an STR-AP implements Sync PPDUs and this capability needs to be advertised

## Slide 12: What’s Needed in the Spec at a High Level
Even though currently agreed Async mode does not prohibit a transmitter from aligning the end times of the PPDUs, there is no guarantee an AP will do that
Therefore, we should let an AP advertise whether or not it will align the end times of the PPDUs
  So that a Non-STR STA can have a choice to associate only with those APs that can meet the Non-STR STA constraints

## Slide 13: What’s Needed in the Spec at a High Level (Cont’d)
AP MLD side:
  Signaling to indicate its capable of aligning the end times of the PPDUs
  Definition of the alignment of the end times of the PPDUs
    e.g., within SIFS
  If SMEA is used to access the 2nd link, define how to access the links other than the one that obtained the TXOP
    Honor PD/NAV on 2nd link. Don’t access if NAV is set on 2nd link (Disruption to the 2nd link is largely addressed)
    Can add more rules to limit the access to the 2nd link e.g., 2nd link access only if RBO < a TBD Threshold value (configurable by AP)
  If SMEA is not used, each link accesses the channels independently

## Slide 14: What’s Needed in the Spec at a High Level (Cont’d)
STA MLD side:
  Signaling to indicate the non-STR constraints
    Already motioned (refer to Motion #46)
  If SMEA is used, procedures of how to access the links other than the one that obtained the TXOP
    Same as those in the AL MLD side (see the previous slide)

## Slide 15: SP1
Do you agree to the following?
In R1 of the spec, supporting the following cases:
  STR AP MLD with STR non-AP MLD
  STR AP MLD with non-STR non-AP MLD
  Note: All the other cases are TBD

## Slide 16: SP2
Do you agree to the following?
Define signaling for an AP MLD to advertise whether it is capable of aligning the end of DL PPDUs that are sent simultaneously on multiple links to the same non-STR non-AP MLD, in such a way that the response to any of the PPDUs will not overlap with any of the DL PPDUs
If the AP MLD advertises this capability, it shall perform the time alignment mentioned above

## Slide 17: SP3
Do you agree to the make the following an optional or mandatory feature?
An AP MLD aligns the end of DL PPDUs that are sent simultaneously on multiple links to the same non-STR non-AP MLD, in such a way that the response to any of the PPDUs will not overlap with any of the DL PPDUs
Mandatory (no signaling needed):
Optional (will need to add capability signaling):
Neither:

## Slide 18: AppendiX

## Slide 19: UL: L2 is IDLE and SMEA is allowed on L2
Use -72dBm as the ED threshold for the second link to improve fairness

## Slide 20: UL: L2 Busy or SMEA NOT allowed on L2

## Slide 21: DL: L2 is IDLE and SMEA is allowed on L2
The start time and end time of the PPDUs are within SIFS

## Slide 22: DL: L2 is Busy or SMEA is NOT allowed on L2 A2 decides to serve Sy instead

## Slide 23: DL: L2 is Busy or SMEA is NOT allowed on L2