## Slide 1: Preamble Structure and SIG Contents
Date: 2020-01-11
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction (1/3)
Previously, the following motions have been passed [2]:
  There shall be a 2 OFDM symbol long, jointly encoded Universal-SIG (U-SIG) field in the EHT preamble immediately after the RL-SIG
  There shall be a variable MCS and variable length EHT-SIG, immediately after the U-SIG, in an EHT PPDU sent to multiple users.
  The EHT-SIG (immediately after the U-SIG) in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s)
  Further details of common field and user-specific field(s) is TBD

## Slide 3: Introduction (2/3)
The EHT-SIG format of an EHT PPDU sent to multiple users is shown below [3]
  EHT-SIG are divided into two sections: EHT Common field and EHT User Specific field
  The length of EHT-SIG is variable
  EHT-SIG Common needs to accommodate the overflow from the U-SIG.
Duplicate
Multiplexing
Multiplexing

## Slide 4: Introduction (3/3)
EHT PPDU types have not been determined. If there exists an SU PPDU, the most likely format is described as below [3]
  HE-SIG-A and U-SIG have the same length (2 symbol long)
  In 11be, some new fields are added to U-SIG, such as PPDU version. Therefore, it is not enough for a two-symbol U-SIG to contain both the newly added information and the similar information in HE-SIG-A. An EHT-SIG is needed to accommodate the overflow from the U-SIG.
Duplicate
In this contribution, we further discuss the EHT-SIG structures and contents of the EHT PPDU sent to one or multiple users.

## Slide 5: EHT-SIG Design for MU PPDU (1/2)
Duplicate
Multiplexing
Multiplexing
  Like 11ax, the beginning part of EHT-SIG could be duplicated to accommodate the overflow from the U-SIG. EHT-SIG Common Part A is used to denote this duplicated part.
    U-SIG and EHT-SIG Common Part A is similar as “HE-SIG-A” in 11ax
    Part A can be less than the length of one symbol
  EHT-SIG Common Part B is like the Common field of HE-SIG-B, which is divided into different content channels. RU Allocation subfields can be included in this field.
    Part A and Part B can be jointly encoded or separately encoded
MU PPDU: Opt 1:

## Slide 6: EHT-SIG Design for MU PPDU (2/2)
Multiplexing
Multiplexing
Multiplexing
The beginning of EHT-SIG for MU PPDU (Part A) can also have different content channels, i.e., have 2 CC at the beginning.
  Benefits
  Some information in content channel 1 can be moved to content channel 2 to save overhead when the bandwidth exceeds 20MHz
  Additional information needed when the bandwidth exceeds 20MHz could be contained in content channel 2.
  Exact details can be further discussed.
MU PPDU - Opt 2:

## Slide 7: EHT-SIG Contents for MU PPDU
Similar as 11ax, RU allocation and center 26-tone RU subfields can exist in EHT-SIG common part B.
For compressed mode of EHT MU PPDU, similar as 11ax, common part B can be omitted.
  Common Part A may still exist to account for the overflow of U-SIG
Similar as 11ax, user field will be similar as the user field of 11ax.
  Some fields may need larger bitwidth, e.g., NSTS

## Slide 8: EHT-SIG Contents for MU PPDU
Bit | Field
B0 | UL/DL
B1 | HE-SIG-B MCS
B2 | 
B3 | 
B4 | HE-SIG-B DCM
B5 | BSS Color
B6 | 
B7 | 
B8 | 
B9 | 
B10 | 
B11 | Spatial Reuse
B12 | 
B13 | 
B14 | 
B15 | Bandwidth
B16 | 
B17 | 
B18 | Number of HE-SIG-B Symbols Or MU-MIMO users
B19 | 
B20 | 
B21 | 
B22 | HE-SIG-B compression
B23 | GI+HE-LTF Size
B24 | 
B25 | Doppler
Bit | Field
B0 | TXOP
B1 | 
B2 | 
B3 | 
B4 | 
B5 | 
B6 | 
B7 | Reserved
B8 | Number of HE-LTF Symbols And Midamble Periodicity
B9 | 
B10 | 
B11 | LDPC Extra Symbol Segment
B12 | STBC
B13 | Pre-FEC Padding Factor
B14 | 
B15 | PE Disambiguity
B16 | CRC
B17 | 
B18 | 
B19 | 
B20 | Tail
B21 | 
B22 | 
B23 | 
B24 | 
B25 | 
HE-SIG-A1
HE-SIG-A2
Bit | Field | Number
B0 | Version Identifier | 4
B1 |  | 
B2 |  | 
B3 |  | 
B4 | BSS Color | 7?
B5 |  | 
B6 |  | 
B7 |  | 
B8 |  | 
B9 |  | 
B10 |  | 
B11 | TXOP | 8?
B12 |  | 
B13 |  | 
B14 |  | 
B15 |  | 
B16 |  | 
B17 |  | 
B18 |  | 
B19 | DL/UL | 1
B20 | Reserved | 1
B21 | PPDU Format | 3?
B22 |  | 
B23 |  | 
B24 | EHT-SIG DCM | 1
B25 | Reserved | 1
U-SIG1
U-SIG2
Bit | Field | Number
B0 | EHT-SIG MCS | 4
B1 |  | 
B2 |  | 
B3 |  | 
B4 | Number of EHT-SIG Symbols or MU-MIMO users | 5?
B5 |  | 
B6 |  | 
B7 |  | 
B8 |  | 
B9 | Bandwidth | 4?
B10 |  | 
B11 |  | 
B12 |  | 
B12 | Number of EHT-LTF Symbols And Midamble Periodicity | 4
B13 |  | 
B14 |  | 
B15 |  | 
B16 | CRC | 4
B17 |  | 
B18 |  | 
B19 |  | 
B20 | Tail | 6
B21 |  | 
B22 |  | 
B23 |  | 
B24 |  | 
B25 |  | 
Bit | Field | Number
B0 | Spatial Reuse | 4
B1 |  | 
B2 |  | 
B3 |  | 
B4 | LDPC Extra Symbol Segment | 1
B5 | STBC | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8 | PE Disambiguity | 1
B9 | Doppler | 1
B10 | GI+EHT-LTF Size | 2
B11 |  | 
B12 | Reserved/TBD (could be used by some new fields related to new features) | 4 or 14
B13 |  | 
B14 |  | 
B15 |  | 
B16 | CRC | 4 or 0
B17 |  | 
B18 |  | 
B19 |  | 
B20 | Tail | 6 or 0
B21 |  | 
B22 |  | 
B23 |  | 
B24 |  | 
B25 |  | 
EHT-SIG Common Part A

## Slide 9: EHT-SIG Design for SU PPDU (1/2)
Duplicate
  In 11ax, the contents of HE-SIG-A are duplicated in different channels.
  Like 11ax, if there exists an SU PPDU, the EHT-SIG of SU PPDU could be duplicated in different channels. The included information accommodates the overflow from the U-SIG.
SU PPDU - Opt 1:

## Slide 10: EHT-SIG Design for SU PPDU (2/2)
  The positions of available content channel 2 could be indicated by the information in U-SIG (like the Bandwidth field in HE-SIG-A in 11ax).
  Benefits
  The overhead could be reduced by half when the bandwidth exceeds 20MHz
  The information of preamble puncturing could be contained in content channel 2 (For example, a bitmap of preamble puncturing)
Multiplexing
Like EHT MU PPDU, the SU PPDU could also consider using different content channels in EHT-SIG.
SU PPDU - Opt 2:

## Slide 11: EHT-SIG Contents for SU PPDU
Bit | Field
B0 | Format
B1 | Beam Change
B2 | UL/DL
B3 | MCS
B4 | 
B5 | 
B6 | 
B7 | DCM
B8 | BSS Color
B9 | 
B10 | 
B11 | 
B12 | 
B13 | 
B14 | Reserved
B15 | Spatial Reuse
B16 | 
B17 | 
B18 | 
B19 | Bandwidth
B20 | 
B21 | GI+LTF Size
B22 | 
B23 | NSTS And Midamble Periodicity
B24 | 
B25 | 
Bit | Field
B0 | TXOP
B1 | 
B2 | 
B3 | 
B4 | 
B5 | 
B6 | 
B7 | Coding
B8 | LDPC Extra Symbol Segment
B9 | STBC
B10 | Beamformed
B11 | Pre-FEC Padding Factor
B12 | 
B13 | PE Disambiguity
B14 | Reserved
B15 | Doppler
B16 | CRC
B17 | 
B18 | 
B19 | 
B20 | Tail
B21 | 
B22 | 
B23 | 
B24 | 
B25 | 
HE-SIG-A1
HE-SIG-A2
Bit | Field | Number
B0 | Version Identifier | 4
B1 |  | 
B2 |  | 
B3 |  | 
B4 | BSS Color | 7?
B5 |  | 
B6 |  | 
B7 |  | 
B8 |  | 
B9 |  | 
B10 |  | 
B11 | TXOP | 8?
B12 |  | 
B13 |  | 
B14 |  | 
B15 |  | 
B16 |  | 
B17 |  | 
B18 |  | 
B19 | DL/UL | 1
B20 | Reserved | 1
B21 | PPDU Format | 3
B22 |  | 
B23 |  | 
B24 | Beam Change | 1
B25 | DCM | 1
U-SIG1
U-SIG2
Bit | Field | Number
B0 | Spatial Reuse | 4
B1 |  | 
B2 |  | 
B3 |  | 
B4 | MCS | 4
B5 |  | 
B6 |  | 
B7 |  | 
B8 | Bandwidth | 4?
B9 |  | 
B10 |  | 
B11 |  | 
B12 | NSTS And Midamble Periodicity | 4
B13 |  | 
B14 |  | 
B15 |  | 
B16 | CRC | 4
B17 |  | 
B18 |  | 
B19 |  | 
B20 | Tail | 6
B21 |  | 
B22 |  | 
B23 |  | 
B24 |  | 
B25 |  | 
Bit | Field | Number
B0 | GI+LTF Size | 2
B1 |  | 
B2 | Coding | 1
B3 | LDPC Extra Symbol Segment | 1
B4 | STBC | 1
B5 | Beamformed | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8 | PE Disambiguity | 1
B9 | Doppler | 1
B10 | Reserved/TBD (could be used by some new fields related to new features) | 6
B11 |  | 
B12 |  | 
B13 |  | 
B14 |  | 
B15 |  | 
B16 | CRC | 4
B17 |  | 
B18 |  | 
B19 |  | 
B20 | Tail | 6
B21 |  | 
B22 |  | 
B23 |  | 
B24 |  | 
B25 |  | 
EHT-SIG (CC1)
Puncturing signaling could be put in CC1 or CC2 (preferred).

## Slide 12: Summary
We have proposed to have more than one content channel in the EHT-SIG of MU PPDU. The beginning position of different content channels could be immediately after the U-SIG.
We have proposed to have more than one content channel in the EHT-SIG of SU PPDU, which could enable the signaling of preamble puncturing in SU PPDU.
Preamble and structure of other PPDU formats can be further discussed if we have made some progress for SU and MU PPDU.

## Slide 13: Straw Poll #1
Do you agree to have RU Allocation subfield in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users?
  Compressed modes are TBD
  Contents of RU allocation subfield are TBD
  33Y
  0N
  4A

## Slide 14: Straw Poll #2
Do you agree to have at least one compressed mode in which RU Allocation subfield doesn’t exist in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users?
  Signaling method is TBD
  18Y
  6N
  14A

## Slide 15: Straw Poll #3
Do you agree to have more than one content channel in the EHT-SIG field of an EHT PPDU sent to multiple users?
  Content channel’s concept is defined in 11ax
  Y
  N
  A

## Slide 16: Straw Poll #4
Do you agree to have more than one content channel in the EHT-SIG of an EHT PPDU sent to one user?
  Y
  N
  A

## Slide 17: Straw Poll #5
Do you agree to have the following subfields in U-SIG and/or EHT-SIG of an EHT PPDU sent to single user?
  MCS
  NSTS
  GI+EHT-LTF Size
  Coding

## Slide 18: Straw Poll #6
Do you agree to have the following subfields in EHT-SIG of an EHT PPDU sent to single user?
  Preamble puncture signaling, exact contents TBD

## Slide 19: Straw Poll #7
Do you agree to have the following subfields in U-SIG of an EHT PPDU sent to multiple user?
  EHT-SIG MCS
  Number of EHT-SIG Symbols
  34Y
  0N
  7A

## Slide 20: Straw Poll #8
Do you agree to have the following subfields in U-SIG or EHT-SIG an EHT PPDU sent to multiple user?
  GI+EHT-LTF Size

## Slide 21
[1] IEEE 802.11-19/1722r11 TGbe November 2019 Meeting Agenda
[2] IEEE 802.11-19/1262r6 Specification Framework for TGbe
[3] IEEE 802.11-19/1519r5 Forward Compatibility for WiFi Preamble Design
[4] IEEE 802.11-19/1870r4 Further Ideas on EHT Preamble Design
[5] IEEE 802.11-19/1516r4 11be Preamble Structure
[6] IEEE 802.11-19/1214r7 EHT Preamble Design
References

## Slide 22: Example of the Bandwidth field in EHT SU PPDU
We give a 4-bit indication method here. The bandwidth field can indicate the bandwidth and one available position of the CC that is not in P20 at the same time.
  Index 4 indicates S40-2 assuming P20 is with CC1. Otherwise, S40-2 would be changed to S40-1. The correct name should be the other 20MHz channel in S40 corresponding to the same content channel of the secondary 20MHz.
240MHz BW can also be considered.
Index | One available position of the CC that is not in P20 | Bandwidth
1 | - | 20MHz
2 | S20 | 40MHz
3 | S20 | 80MHz
4 | S40-2 | 80MHz
5 | S20 | 160MHz
6 | S40-2 | 160MHz
7 | S80-2 | 160MHz
8 | S80-4 | 160MHz
9 | S20 | 320MHz
10 | S40-2 | 320MHz
11 | S80-2 | 320MHz
12 | S80-4 | 320MHz
13 | S160-2 | 320MHz
14 | S160-4 | 320MHz
15 | S160-6 | 320MHz
16 | S160-8 | 320MHz