## Slide 1: Multi-link Block Ack Architecture
Date: 2020-01-10
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation | 202 Bedok South Avenue 1, #02-11 Singapore 469332 |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Overview
In our previous contribution, we shared our thoughts on some aspects of Multi-link block ack operations [1].
The following aspects related to Multi-link block ack have been added to the 11be SFD :
  A single block ack agreement is negotiated between two MLDs for a TID that may be transmitted over one or more links.
  Sequence numbers are assigned from a common sequence number space shared across multiple links of a MLD, for a TID that may be transmitted to a peer MLD over one or more links.
This contribution shares one possible architecture for Multi-link block ack. Other architectures are also possible and are discusssed in [2] and [3].

## Slide 3
Originator MLD

## Slide 4
Recipient MLD

## Slide 5
Scoreboard size
Different links may have different data rates (e.g. due to different bandwidths, # of antennas etc.). Consequently, the recipient MLD can expect to receive more MPDUs on the faster link and may need to negotiate different Per-link Scoreboard sizes for different links during the setup of block ack parameters between two MLDs. Else, the scoreboard size of a slower link may constrain a faster link’s throughput.
The size of the BA Bitmap of BAs may also get restricted by the scoreboard sizes.
Notes: E.g. Link 2 is 4 times faster than link 1. => Link 2 may maintain a buffer size that is 4 times bigger than Link1’s.
The size of the Receiver Reordering buffer >= Sum of scoreboard sizes of all enabled links.

## Slide 6
Example Recipient Implementation
Recipient MLD may also maintain a common scoreboard to keep a longer term record of received MPDUs (not limited by TXOPs). Per-link scoreboard may be implemented as partial-state, while common scoreboard may be implemented as full-state. The common Scoreboard is updated regularly with the content of the per-link Scoreboards (e.g. every time the Per-link scoreboard is updated, or at a very minimum at the end of each link’s TXOP).
Notes: common scoreboard may prevent the receipt status of a link being lost, for e.g. due to switch of TIDs between TXOPs.
The size of the Common Scoreboard >= Maximum scoreboard sizes among all enabled links.

## Slide 7
Conclusion
This contribution shared one possible architecture for Multi-link block ack operations.
We proposed that the block ack agreement for a TID that may be transmitted over multiple links be allowed to maintain different buffer sizes for different links.
We also proposed that a recipient MLD may maintain a common scoreboard to consolidate the receipt status of MPDUs of a TID received via different links.

## Slide 8: Reference
IEEE 802.11-19/1512r6 – Multi-link acknowledgment
IEEE 802.11-19/1575r0 – Multi-link BA Operation
IEEE 802.11-19/1856r0 – A-MPDU and BA

## Slide 9
Straw Poll 1
Do you support that an MLD maintains a common Receiver Reordering Buffer for a TID that may be received over one or more links?
  Y/N/A

## Slide 10
Straw Poll 2
Do you support that different scoreboard sizes may be negotiated for different links during negotiation of a block ack agreement for a TID that may be received over one or more links?
  Y/N/A

## Slide 11
Straw Poll 3
Do you support that an MLD may maintain a common scoreboard to consolidate the receipt status of MPDUs of a TID received via different links?
  Y/N/A