## Slide 1: Multi-Link TIM
Date: January, 2020
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Background
For a multi-link operation, mechanisms of indicating buffered frame information of one link by including the indication information on another link of an AP Multi-Link Device (MLD) [1][2].
In conventional 802.11 standard, TIM element within a Beacon frame works for indicating buffered frame information of associated STAs with a serving AP.
In this contribution, we propose possible ways of expanding conventional TIM mechanism to be used for indication of multiple link status.

## Slide 3: Requirements
Required information
  In case an AP MLD does not have buffered BU to transmit to a non-AP MLD:
    There’s only one bit information needed to indicate that there’s no buffered BU.
  In case the AP MLD has buffered BU to transmit to a non-AP MLD:
    The AP MLD needs to indicate which link the AP MLD has buffered BU to transmit, especially when different TIDs are mapped to different links.
Additional requirements
  It should be backward compatible.
    Legacy STAs, 11be single link STAs, and 11be multi-link STAs can be indicated without any confusion.
  Additional signaling overhead for indicating multiple link status should be minimized.

## Slide 4: Possible Approaches
TIM element(s) indicating buffered frame status of multiple links
  Multiple TIM indication
  Single TIM indication
Defining another element for indicating link mapping
  TIM + Link mapping

## Slide 5: Multiple TIM Indication
An AP MLD transmits separate version of TIM element for each link in a Beacon frame on a link.
  AID of a STA on a link and the AID of a STA on another link from same non-AP MLD can be the same.
  Each version of TIM may have a link identifier.
  At least the TIM element for the link that the Beacon frame is transmitted is backward compatible.

## Slide 6: Multiple TIMs Indication
Possible solution:
  The TIM element transmitted in the Beacon frame of a link indicates the buffered frames for STAs associated with the AP of the link.
  The TIM subelement in Slave Link Related element indicates the buffered frames for STAs associated with AP of the link identified by LinkID.
Element ID = 255
Length
Element ID Extension
Link ID
subelements
Subelement ID
Length
Information
Subelement 1
Slave Link Related element 2
Element ID = 255
Length
Element ID Extension
Link ID
subelements
Slave Link Related element 1
Subelement ID
Length
Information
Subelement n
255 octets
Subelement ID
Length
Information
Subelement n+1
Subelement ID
Length
Information
Subelement n+2

## Slide 7: Single TIM indication
The non-AP MLD has different AIDs in different links.
The TIM element in the Beacon of a link indicates the buffered frames for STAs associated with the AP of the link and the APs of other links.
  For a non-AP MLD associated with the AP MLD, different AID tells the buffered frame status of different link.

## Slide 8: TIM + Link Indication
Conventional TIM element is used as it is:
  For a non-AP MLD, TIM bit is assigned per non-AP MLD regardless of the number of links setup.
  TIM bit for a non-AP STA/MLD is set to 0 if the AP MLD does not have any buffered frame to transmit to a non-AP STA/MLD.
  TIM bit for the non-AP STA/MLD is set to 1 if the AP MLD has one or more buffered frames to transmit to the non-AP STA/MLD on any link to be used.
On top of conventional TIM element, another element is defined to indicate the buffered data to link mapping for each non-AP MLD that the TIM bit is set to 1

## Slide 9: TIM + Link Indication
Operation Example:
  A link mapping bitmap (LMB) is defined, where each bit within the LMB per AID indicates a designated link corresponding to the AID.
    Size and link mapping of LMB per AID will be indicated during association.
  On each incident of TIM element transmission, such as a Beacon frame transmission,
    For each AID, corresponding TIM bit is set to 1 if there’s a buffered data for the AID regardless of specific link of non-AP MLD mapped to the AID to be used.
    New element (e.g., Buffered data to link mapping (BLM) element) follows the TIM element.
      The BLM element includes a set of LMBs, where the size of the set equals to N_TIM * N_bitmap, where N_TIM denotes the number AIDs that corresponding TIM bit is set to 1 and N_bitmap denotes the size of LMB.
    The location of LMB for an AID in the set can be predefined:
      E.g., The set is listed in monotonically increasing order of LMB for those AIDs that TIM bit is set to 1.
    When a non-AP MLD identifies in TIM element that the TIM bit corresponding to the non-AP MLD’s AID is set to 1, the non-AP MLD further checks the LMB corresponding to the AID and identifies specific link(s) that the buffered traffic is mapped.

## Slide 10: TIM + Link Indication
Operation example
  There are 3 links that an AP MLD supports
    LMB per AID is composed of 3 bits
      1st/2nd/3rd link corresponds to 1st/2nd/3rd bit of the LMB per AID
  Out of 255 non-AP MLDs, there are 5 non-AP MLDs that the AP MLD has buffered data:
    Corresponding AIDs are 12/28/35/57/77.
  The size of a set of LMBs goes down to only 15 bits (5 STAs x 3 bit per STA)
0
0
1
0
AID:
0
1
0
0
1
0
0
1
0
0
1
0
0
…
…
…
…
…
…
12
28
35
57
77
0
TIM bitmap:
A set of LMB:
Size = 15 (5x3)
1
0
0
AID:12
0
1
1
AID:28
0
1
0
AID:35
0
0
1
AID:57
1
1
0
AID:77
11
13
27
34
56
76
29
36
58
78
255
Link 1
Link 2
Link 3

## Slide 11: TID mapping
Current agreements on TID mapping [3]
  802.11be defines a directional-based TID-to-link mapping mechanism among the setup links of a MLD.
    By default, after the multi-link setup, all TIDs are mapped to all setup links.
    The multi-link setup may include the TID-to-link mapping negotiation.
      TID-to-link mapping can have the same or different link-set for each TID unless a non-AP MLD indicates that it requires to use the same link-set for all TIDs during the multi-link setup phase.
      NOTE – Such indication method by the non-AP MLD is TBD (implicit or explicit).
    The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD.
      Format TBD.
      NOTE – When the responding MLD cannot accept the update, it can reject the TID-to-link mapping update.

## Slide 12: TID mapping
Basic principle
  In a typical multi-link operation scenarios, we expect that all TIDs are mapped to all links (default mode).
    If an AP MLD supports N links, TIM indication for N different links will be identical.
    Therefore, in either multiple TIMs method or single TIM method, we cannot avoid N times duplicated TIM indication overhead.
    It is better to have a per-MLD indication for TIM element.
  If there exists a separate TID-to-link mapping for each non-AP MLD:
    It is beneficial to have link indication only when there’s a buffered BU for a non-AP MLD.
Therefore, we believe that TIM + Link Indication is a better option among possible candidates.

## Slide 13: Summary
TIM indication methods for indicating buffered frame status of multiple links have been proposed.
  Multiple TIM indication
  Single TIM indication
  TIM + Link indication
TIM + Link indication is an efficient solution for multi-link TIM indication:
  For a BSS that all TIDs are mapped to all links, which is a default mode of operation, we only need a TIM element.
  Indication overhead can be reduced and controlled based on the TID-to-link mapping rule.

## Slide 14: SP 1
Do you agree to add the following to 11be SFD:
  A bit in a partial virtual bitmap of a TIM element that corresponds to a non-AP MLD is set to 1 if any individually addressed BUs for the non-AP MLD are buffered by the AP MLD.

## Slide 15: SP 2
Do you agree to add the following to 11be SFD:
  When a non-AP MLD made a multi-link setup with an AP MLD, one AID is assigned to the non-AP MLD across all links.

## Slide 16: References
[1] 11-19-1857r1 Multiple Link Power Save
[2] 11-19-1544r0 Multi-link power save operation
[3] 11-19-1262-08 Specification Framework for TGbe