## Slide 1
Authors:
Multi-Link Communication Mode Discussion
Date: 2020-01-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | sun.bo1@zte.com.cn
Nan Li | ZTE |  |  | li.nan25@zte.com.cn
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution intends to clarify terms used ML operation and proposes the definition of the terms to be used in 802.11be.

## Slide 3: Background
Multi-Link framework requirements
  ML framework requirements are proposed to support
    Dynamic selecting and switching an operating link to address the use cases of reducing access latency for fast connection, balancing loads, etc..
    Concurrent transmit or receive packets over multiple links to address the use cases of improving transmission reliability and increasing peak-throughput.
  However, there is no clear definition for “concurrent transmit or receive” packets over multiple links.

## Slide 4: Background
  Terms used in communication industry [1, 2, 3]
  Simplex communication: a communication channel that operates in one direction at a time, but that may be reversible.
  Half Duplex communication: a communication channel can operate in both directions, but only one direction at a time (not simultaneously).
  Full Duplex communication: a duplex communication channel requires two simplex channels operating in opposite directions.

## Slide 5: Issues on Terms
  Terms being used in 802.11be
  In SFD [7], some capability of MLD is described as
    A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
    802.11be shall allow the following asynchronous multi-link channel access:
      Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.
      Downlink and uplink frames can be transmitted simultaneously over the multiple links.
  Term used in some 802.11be contributions
    Simultaneous transmission and reception (STR) is used in [4, 5]
    Non simultaneous transmission and reception (non-STR) is used in [4, 5]
    Synchronous MLD in [6] seems referring to non-STR. And the asynchronous MLD in [6] seems referring to STR.
    Synchronous and asynchronous transmission mentioned in [5] seems referring to the timing synchronization in transmissions.
  We suggest to clearly define those terms for multi-link operation in SFD.

## Slide 6: ML Operation Definition
  STR: simultaneous transmission and reception
  STR Operation: is the operation of which a transmission on one link is independent to (i.e. non-interruptible on) the operation on another link.
  STR-constraint Operation: is the operation of which a transmission on one link will be constrained if causes the reception interruption on another link.

## Slide 7: ML Operation Definition
  Synchronous Transmission
  A MLD shall transmit on multiple links frames of which their transmission starting time are aligned within TBD micro-seconds.
Asynchronous Transmission
  A MLD may transmit on multiple links frames of which their transmission starting time may not be aligned within TBD micro-seconds

## Slide 8: Straw Poll (1)
Do you support to define the following in SFD ?
  STR: simultaneous transmission and reception
  STR Operation: is the operation of which a transmission on one link is independent to (i.e. non-interruptible on) the operation on another link.
  STR-constraint Operation: is the operation on a link may depend on the operation of another link.
      e.g. a transmission on a link may be constrained if it causes the reception interruption on another link, or a reception on a link may be constrained if a transmission is on anther link.
  STR-constraint links: A pair or group of links are in the STR-constraint Operation.
YES/NO/ABS

## Slide 9: Straw Poll (2)
Do you support to define the following in SFD ?
  Synchronous Transmission: A MLD transmits on multiple links frames that one or both of the following condition is true:
    The transmission starting times of the frames are aligned within TBD micro-seconds
    The transmission ending times of the frames are aligned within TBD micro-seconds
  Asynchronous Transmission: A MLD transmits on multiple links frames that has no alignment requirement on the transmission starting or ending time of the frames.
YES/NO/ABS

## Slide 10: References
The IEEE Authoritative Dictionary of Standard Terms, 7th Ed., 2000, Inst. of Electrical and Electronic Engineers, p.1053
https://en.wikipedia.org/wiki/Simplex_communication
https://en.wikipedia.org/wiki/Duplex_(telecommunications)
11-19-1917-01-00be-considerations-for-multi-link-channel-access-without-simultaneous-tx-rx-capability
11-20-0026-00-00be-mlo-sync-ppdus
11-20-0081-01-00be-mlo-synch-transmission
11-19-1262-07-00be-specification-framework-for-tgbe

## Slide 11
Thank you!