## Slide 1: Calibration for Implicit Feedback
Date: 2020-01-12
Authors:
Name | Affiliations | Address | Phone | email
Qinghua | Intel |  |  | 
Feng Jiang |  |  |  | 
Ziv Avital |  |  |  | 
Xiaogang Chen |  |  |  | 
Roya Doostnejad |  |  |  | 
Po-kai Huang |  |  |  | 
Assaf Gurevitz |  |  |  | 
Robert Stacey |  |  |  | 
Laurent Cariou |  |  |  | 

## Slide 2: Background (1/2)
Explicit feedback suffers from large overhead and high complexity for large antenna arrays
Implicit feedback reduces the overhead and draws significant attentions [1-3]
However, implicit feedback requires accurate calibration
  Chain response varies with gain setting
  DL MU-MIMO is sensitive to cross-talk
Two calibration types i.e. self-calibration and mutual calibration
Li, Jiang, et al., Intel

## Slide 3: Background (2/2)
Self-calibration
  Pros — Don’t need standard support
  Cons — Need additional hardware; Hard to achieve high accuracy
Mutual calibration (802.11n)
  Pros — No self-calibration hardware
  Cons — Incompatible with existing explicit feedback in terms of hardware and frame exchange sequence; Not adopted by the market
In [1], test results show that it’s possible to achieve -37dB@50% EVM for implicit channel estimation

## Slide 4: Remark
Implicit feedback requires Tx/Rx chain calibration at the transmitter
Channel matrix feedback was in 802.11n spec but not implemented
In contrast, compressed beamforming feedback using Givens angles is widely implemented
It is desirable to have a backward-compatible calibration scheme i.e. reusing the implemented compressed beamforming feedback

## Slide 5: Problem Statement
Want a simple calibration scheme for implicit feedback
  No self-calibration hardware
  Compatible to explicit feedback
  Low overhead

## Slide 6: Proposed Solution
Reuse the hardware and frame exchange sequence of existing compressed beamforming feedback for mutual calibration

## Slide 7: Recap of 11n Calibration
Beamformer obtains both DL and UL channels and compares them
Channel reciprocity:
AP
STA

## Slide 8: Calibration and Compensation
Downlink channel fed back by B
Uplink channel estimated by A
Compensation factor at A
AP
STA

## Slide 9: Remarks
Beamformer needs channel estimates of both forward and backward directions for estimating compensation factor
Beamformee only needs to feed back the channel estimates calculated from one of its receive antennas

## Slide 10: Channel Vector vs. Beamforming Vector
For an Nx1 MISO channel, a beamforming vector is just a normalized channel vector
Namely, for MISO channels, beamforming vector and channel vector only differ by a global factor, which doesn’t affect the beamforming
Power normalization factor

## Slide 11: Observation
The beamforming vector for the transmitter to beamform to a single receiver’s antenna preserves all the phases and amplitudes information required for calibrating the transmitter’s antennas
The existing feedback scheme i.e. the compressed beamforming feedback can be reused for feeding back the beamforming vector

## Slide 12: Reusing Beamforming Vector for Calibration
For NxM MIMO channel, beamformee selects one antenna out of M receive antennas, downgrades the channel to Nx1 MISO, and feeds back the beamforming vector of the MISO as the channel vector
Beamformer uses the fed back beamforming vector as the channel vector in estimating the compensation factors
Reuse Givens quantization. Don’t need new hardware

## Slide 13: Feedback Calculations
Proposed calibration feedback skips the SVD step
h1
hN
…
v
i , j
SVD of HM x N
HM x N
h1
hN
…
v
i , j
h1
Conventional beamforming feedback

## Slide 14: Explicit Feedback Sequence
Compressed beamforming report consists of quantized NxNSTS beamforming matrixes
Compressed beamforming report
Beamformer
Beamformee
NDPA
NDP

## Slide 15: Calibration Feedback Sequence
Reuse explicit beamforming feedback sequence
Compressed beamforming report consists of quantized Nx1 beamforming vectors for the selected beamformee antenna
Compressed beamforming report
NDPA
NDP
Beamformer
Beamformee

## Slide 16: Backward Sounding
Remember beamformer needs both forward and backward channels
The LTF of the calibration feedback frame itself can be used for backward sounding
Compressed beamforming report
LTF
NDPA
NDP
Backward channel sounding; implicit feedback; and channel training for demodulating payload
Beamformer
Beamformee
Nx1 vectors instead of NxNSTS matrixes, much smaller than conventional beamforming feedback

## Slide 17: Remarks
Both calibration feedback and implicit feedback can be all fit into one explicit sounding/feedback sequence
The overhead of calibration plus implicit feedback is still smaller that of the explicit beamforming feedback
Calibrations can be done for each STA group for compensating the transceiver variations e.g. different AGC/PA settings
To avoid impact of low quality CSI feedback, the AP may calculate the calibration parameter for each STA separately and apply each STA’s calibration parameter to its own DL channel estimation

## Slide 18: Simulation Settings (1/2)
DL MU-MIMO
  AP has 4 antennas and each STA has 2 antennas
  3 STAs each receiving 1 stream
Each Tx chain and each Rx chain response differ by a phase
Channel D, MCSs 7, 9
Two quantization schemes for calibration feedback
  Ideal quantization without quantization error
  802.11 (7, 9) bit quantization

## Slide 19: Simulation Settings (2/2)
AP solicits calibration feedbacks from 2 STAs
Each STA sends calibration feedbacks for one of its 2 antennas
AP combines the two compensation weight estimates
Calibration is done for 1 channel and the compensation weights are used for 5000 channels
  For 3 STA MU-MIMO, calibration is done with 1 STA’s 2 antennas
  For 4 STA MU-MIMO, calibration is done with all 4 STAs’ 8 antennas

## Slide 20: MCS 7, 3 Users
Less than 0.4 dB

## Slide 21: MCS 7, 4 Users
Less than 0.3 dB

## Slide 22: MCS 9, 3 Users
Less than 0.4 dB

## Slide 23: MCS 9, 4 Users
0.65 dB

## Slide 24: Lab Test Setup
Two 4-antenna 11ax devices: A and B
Antennas pairs are connected by cables
Measured several channels from device A to device B, and then measured several channels from device B to device A
Measurement results for 80MHz band and 2x LTF
The time interval between measurements is 5 seconds
A
B
DL
UL

## Slide 25: Lab Measurement Results (1/4)

## Slide 26: Lab Measurement Results (2/4)

## Slide 27: Lab Measurement Results (3/4)

## Slide 28: Lab Measurement Results (4/4)

## Slide 29: Performance Evaluation
(DL measurement 1) and (UL measurement 1) are used for calibration
(DL measurement 2) is estimated by compensating (UL measurement 2) using
EVM of ith channel element is calculated as [1]

## Slide 30: Simulation vs. Measurement

## Slide 31: Conclusions
Propose a calibration scheme with backward compatibility, simple implementation, and high efficiency
Achieve the performance of ideal calibration feedback
Enable implicit feedback without challenging self-calibration
Simulation results matched with lab test data

## Slide 32: Reference
[1] IEEE 802.11-19/1193r0, Calibration of Implicit Sounding, Nov. 2019
[2] IEEE 802.11-19/1934r0, Precoding Performance Using Implicit Channel Estimation, Nov. 2019
[3] IEEE 802.11-19/0767, Implicit Channel Sounding in IEEE 802.11 (Feasibility Study), July 2019

## Slide 33: Backup

## Slide 34: Fading Impact
Calibration signal can be in deep fade at some subcarriers
AP should solicit calibration feedbacks i.e. beamforming vectors for more than one STA antenna
Channel response
Freq
Signal in deep fade
Drop to zero and leave only noises

## Slide 35: Diversity Combing (1/2)
AP solicits beamforming vectors for M STA antennas
AP
STA

## Slide 36: Diversity Combing (2/2)
AP estimates the compensation weight using the beamforming vectors fed back for the M STA antennas
AP combines the estimates using the received uplink sounding strengths as the weighting factors
where is AP antenna index; is STA antenna index;
Uplink channel estimate
Downlink channel estimate, fed back and nomalized

## Slide 37: Calibration Error