## Slide 1: Performance of parameterized spatial reuse (PSR) with coordinated beamforming/null steering for 802.11be
Date: 2020-01-10
Authors:
Name | Affiliation | Address | Phone | Email
Adrian Garcia-Rodriguez | Nokia |  |  | adrian.garcia_rodriguez@nokia-bell-labs.com
David Lopez-Perez |  |  |  | 
Lorenzo Galati Giordano |  |  |  | 
Olli Alanen |  |  |  | 
Mika Kasslin |  |  |  | 
Eloise de Carvalho Rodrigues |  |  |  | 
Enrico Rantala |  |  |  | 
January 2020

## Slide 2: Introduction
As shown in [19/1594r2], the 802.11ax parameterized spatial reuse (PSR)* framework
  provides a good basis for coordinated beamforming/null steering, since it
  allows APs to altruistically—but coordinately—‘share’ an uplink transmission opportunity (TXOP) with other inter-BSS devices
    The performance gains of synchronous coordinated beamforming systems have been demonstrated in [19/0772r1] and [19/1212r2]
In this contribution, we
  briefly review the PSR framework with coordinated beamforming/null steering of [19/1594r2], and
  evaluate the performance of such scheme
  *referred to as spatial reuse parameter (SRP) in drafts D1.0 – D5.1
January 2020
*
Notes: Parameterized spatial reuse

## Slide 3: 802.11ax PSR framework with null steering: Practical operation
Standard PSR framework + coordinated null steering (see [19/1594r2])
ACK
TF
UL data
UL data
ACK
Contention
STA21
donor AP1
AP2
STA11
UL data
STA12
UL data reception
UL data reception
STA21 measures power, and identifies a spatial reuse opportunity (SRO)
TF advertises spatial reuse opportunity
NDP
TF
TF
NDP
NDP
NDP
NDPA
Transfer and return frames may be needed to coordinate AP1 and AP2 actions
NDP
NDP
NDP
NDP
Phase 1 – Coord.
Phase 2 – Implicit CSI acquisition
Phase 3 – Coordinated inter-AP DATA TX & ACK with nulls
CRequest
CResponse
Data transmission
Null steering
AP2 nulls
STAs 11 and 12
AP1 nulls
STA21
*Similar to 802.11ax, an alternative implementation could be based on AP2 sending the ACK while AP1 is still performing UL data reception
t
BSS1
BSS2
January 2020

## Slide 4: 802.11ax PSR framework with null steering: Key implementation benefits
Unsynchronized operation [19/0638r0]
  Since the interference suppression is performed through the application of a spatial filter during data reception, APs can suppress both
  the non-precoded PPDU preambles, and
  the guard interval signals
  from interfering devices, without requiring symbol-level synchronization
Easily adjusts to null steering impairments
  APs granting the spatial reuse opportunities with null steering may set their acceptable receiver interference level accounting for impairments
    If only 10 dB of interference suppression can be guaranteed through null steering, the UL Spatial Reuse field of the Trigger frame should be adjusted by that factor, when compared to the baseline PSR operation
January 2020

## Slide 5: System evaluation
We will compare the performance of the following three systems:
Baseline system without PSR
  Spectrum shared according to CSMA/CA
System with PSR
  When triggering uplink transmissions, APs may grant SROs to inter-BSS STAs
System with PSR and coordinated beamforming/null steering
  When triggering uplink transmissions, APs may a) steer radiation nulls, and b) grant SROs to inter-BSS STAs
January 2020
AP
2
AP
1
Time sharing
beam
Devices may listen to each other
BB
BB
BB
URLLC
BB
BB
BB
BB
URLLC

## Slide 6: System evaluation
We will compare the performance of the following three systems:
Baseline system without PSR
  Spectrum shared according to CSMA/CA
System with PSR
  When triggering uplink transmissions, APs may grant SROs to inter-BSS STAs
System with PSR and coordinated beamforming/null steering
  When triggering uplink transmissions, APs may a) steer radiation nulls, and b) grant SROs to inter-BSS STAs
January 2020
SRO not found
AP
2
AP
1
Power-based spatial reuse
BB
BB
BB
URLLC
Spatial reuse enabled when inter-OBSS devices can guarantee the acceptable receiver interference level set by the AP triggering uplink transmissions
beam
beam
SRO found
Contention lost
SRO not found
SRO found
Constrained TX power
AP1 triggered uplink
SRO not found

## Slide 7: System evaluation
Radiation null at reception
placed by AP
We will compare the performance of the following three systems:
Baseline system without PSR
  Spectrum shared according to CSMA/CA
System with PSR
  When triggering uplink transmissions, APs may grant SROs to inter-BSS STAs
System with PSR and coordinated beamforming/null steering [19/1594r2]
  When triggering uplink transmissions, APs may a) grant SROs, and b) steer radiation nulls to inter-BSS STAs
January 2020
SRO found
AP
2
AP
1
BB
BB
BB
URLLC
beam
beam
SRO found
Contention lost
SRO found
Contention lost
SRO found
Contention lost
Power-based spatial reuse
aided by null steering
      Devices are more likely to
      a) find spatial reuse opportunities, and
      b) access the medium with larger transmission powers
SRO not found
AP1 triggered uplink

## Slide 8: 802.11ax PSR framework with null steering: Performance evaluation
We consider a scenario with both
  uplink broadband traffic—modeled as a file transfer protocol (FTP) service—, and
  uplink low-latency traffic—modeled as an augment reality (AR) application
When triggering uplink, APs spatially multiplex as many STAs as possible of a class per TXOP
Our main objective with the remaining spatial degrees of freedom is to reduce the worst-case latencies of the STAs with low-latency traffic
  In our study, APs granting SROs will suppress interference only from neighboring low-latency STAs with the strongest average perceived interference
January 2020
Broadband (BB) FTP3 model [A]
File size = 0.5 MBytes
Offered traffic = 100 Mbps
Latency-sensitive (LS) AR model [B]
File size = 32 bytes
Constant arrival rate, frequency = 10 ms
time
Per STA traffic
time
Per STA traffic

## Slide 9: 802.11ax PSR framework with null steering: Intuition
ACK
Multiple short-packet transmissions may be performed within a long uplink-triggered transmission
January 2020
TF
UL data
UL data
ACK
STA21
(low-latency)
donor AP1
AP2
STA11
UL data
STA12
UL data reception
STAs 21 and 22 identify SROs
Phase 3 – Coordinated inter-AP DATA TX & ACK with nulls
Null steering (RX)
AP2 nulls
STAs 11 and 12
t
BSS1
BSS2
STA22
(low-latency)
Phases 1 and 2 – Coordination and CSI acquisition
(see slide 3)
ACK
UL data
Contention
UL data reception
UL data reception
AP1 nulls STAs 21 and 22
Null steering (TX)
This is the main benefit for latency-sensitive applications
Packet arrival to the queue

## Slide 10: Fundamental system model parameters*
January 2020
Frequency/Bandwidth | 5.18GHz/80MHz (1 channel)
AP deployment | 2 ceiling-mounted APs ¦ Inter-AP distance = 15 m ¦ AP height = 3 m
AP characteristics | 4x2 antenna array (0.5λ separation) ¦ AP max. Tx power = 24 dBm ¦ omni antenna element ¦ NF = 7 dB
STA deployment | 16 broadband STAs uniformly distributed at height = 1 m 8 low-latency STAs uniformly distributed at height = 1 m
STA characteristics | STA max. Tx power = 15 dBm ¦ 1 omni antenna ¦ NF = 9 dB
Channel model | 3D spatial channel model (3GPP TR38.901 – InH [C])
MAC layer conf. | Max. # radiation nulls = 4 ¦ IP/MAC header overhead considered ¦ No EDCA ¦ No RTS/CTS ¦ Max. TXOP = 4 ms ¦ SNR-driven MCS selection
PHY layer conf. | PHY header overhead considered ¦ Spatial filter = ZF (with and without nulls) ¦ Omni PLCP header ¦ 11ax MCSs
  *A complete description of the system model parameters can be found in the Appendix

## Slide 11: Performance of low-latency STAs
PSR with null steering: Interference suppression bias for computing the receiver acceptable interference per AP = 10 dB
The PSR-based system with null steering demonstrates a significant reduction of the worst-case delays due to
  the more aggressive spectrum access,
  the coordinated spectrum usage, and
  the inter-BSS interference mitigation
The 5%-worst delays are reduced by a factor of 2.3x w.r.t. the baseline system
  The power-based PSR of 802.11ax does not improve the worst-case delays in the dense scenario considered
Further lower latencies could be achieved through complementary techniques, e.g., reduced TXOP durations
January 2020

## Slide 12: Performance of low-latency STAs as a function of null steering accuracy
January 2020
PSR with null steering: Variation of the interference suppression bias for computing the receiver acceptable interference per AP
The worst-case latency benefits are also present when APs advertising SROs account for a limited interference suppression
  When compared to uncoordinated systems, these gains are due to 1) the interference suppression from the AP receiving the spatial reuse transmissions, and 2) the inter-AP coordination—which prevents some lengthy collisions
  The worst-case delays are reduced by a factor of 5x when APs advertising SROs estimate that the interference suppression bias provided by the spatial radiation nulls reaches 8 dB
  A larger number of low-latency inter-BSS devices find spatial reuse opportunities

## Slide 13: Performance of broadband STAs
January 2020
PSR with null steering: Interference suppression bias for computing the receiver acceptable interference per AP = 10 dB
The PSR-based system with null steering approximately preserves the throughput offered to the STAs with broadband traffic
The slight throughput decrease w.r.t. the baseline is mostly caused by
  1) the decision of providing spatial reuse opportunities and focusing the available spatial radiation nulls towards inter-BSS low-latency STAs, and
  2) the loss in AP receive beamforming gain due to the radiation null placement
  The power-based PSR of 802.11ax preserves the throughput of the broadband STAs w.r.t. the baseline in the dense scenario considered
  STAs with broadband traffic benefit from the spatial reuse opportunities offered by PSR

## Slide 14: Conclusions
In this contribution, we evaluated the worst-case latency benefits provided by a system implementing parameterized spatial reuse (PSR) with coordinated beamforming
  The considered protocol does not require a tight synchronization
    APs suppress interference through a receive spatial filter
  The considered protocol significantly reduces the worst-case delays in a scenario with mixed low-latency and broadband traffic
    This is mostly thanks to the more aggressive—albeit controlled—spectrum access
January 2020

## Slide 15: Straw poll #1
Do you believe that enhancing the parameterized spatial reuse (PSR) with coordinated beamforming capabilities is appealing and should be further explored within the 802.11be task group?
  Yes
  No
  Abstain
January 2020

## Slide 16: References
[19/0772r1] Roya Doostnejad (Intel), “Multi-AP Collaborative BF in IEEE 802.11”, 19/0772.
[19/1212r2] David Lopez-Perez (Nokia), “Performance of Coordinated Null Steering in 802.11be”, 19/1212.
[19/1594r2] David Lopez-Perez (Nokia), “Coordinated Beamforming/Null Steering in 802.11be”, 19/1594.
[19/0638r0] Sigurd Schelstraete (Quantenna), “Nulling and coordinated beamforming”, 19/0638.
[A] 3GPP TR 36.814, “Evolved Universal Terrestrial Radio Access (E-UTRA); Further advancements for E-UTRA physical layer aspects,” March 2017.
[B] 3GPP TR 38.824, “Study on physical layer enhancements for NR ultra-reliable and low latency case (URLLC),” March 2019.
[C] 3GPP TR 38.901, “Study on channel model for frequencies from 0.5 to 100 GHz,” June 2018.
January 2020

## Slide 17: Appendix
January 2020

## Slide 18: Baseline uplink 802.11ax PSR Framework Enables spatial reuse during uplink transmissions
Standard version
ACK
TF
UL data
UL data (constrained TX power)
ACK
Contention
UL data
UL data reception
UL data reception
STA21 measures power, and identifies a spatial reuse opportunity
TF advertises SRO
AP1 advertises the spatial reuse opportunity (SRO) in a trigger frame (TF), and provides information about
  AP1 transmit power
  AP1 acceptable uplink interference level
STA21 measures AP1 received power level, and determines whether using the SRO
  STA21 derives, e.g. its maximum transmit power, based on the above information
If STA21 finds an SRO, it contends while AP1 is receiving uplink data
  STA21 TXOP has to accommodate all transmissions within AP1 data reception
Data transmission
STA21
donor AP1
AP2
STA11
STA12
t
BSS1
BSS2
January 2020

## Slide 19: Complete list of system model parameters
January 2020
Simulation length | 20 drops of 2 seconds each
Frequency/Bandwidth | 5.18GHz/80MHz (1 channel)
Scenario size | 35 meters x 20 meters
AP deployment | 2 ceiling mounted APs at (10 m, 10 m) and (25 m, 10 m) ¦ AP height = 3 m
STA deployment | 16 broadband STAs ¦ 8 low-latency STAs ¦ 2D uniform distribution ¦ STA height = 1 m ¦ Minimum inter-STA 2D distance = 0.1 m ¦ Minimum AP-STA 2D distance = 0.5 m ¦
Channel model | 3D spatial channel model (3GPP TR38.901 – InH [C])
AP/STA MAC layer conf. | IP/MAC header overhead considered ¦ No EDCA ¦ No RTS/CTS ¦ Max. TXOP = 4 ms ¦ SNR-driven MCS selection
AP MAC layer conf. | Max. number of spatially multiplexed STAs = 8 ¦ Uplink-triggered transmissions active ¦ Scheduling logic = No joint multiplexing of broadband and low-latency STAs, priority to low-latency STAs, Round Robin scheduling policy ¦ Uplink power control logic = Min. RSS to achieve selected MCS + 6 dB of margin ¦ PSR safety margin value for calculating the acceptable receiver interference level = 3 dB (Eq. 26-7, 802.11ax D6.0) ¦ Perfect channel state information acquisition ¦ Max. number radiation nulls = 4 ¦ Inter-BSS device null steering selection method = Low-latency STAs generating the strongest perceived interference ¦ Max. estimated interference suppression per radiation null = 10 dB (considered when calculating the PSR acceptable interference level)
STA MAC layer conf. | PSR minimum Tx power to find spatial reuse opportunity = 3 dBm
AP/STA PHY layer conf. | PHY header overhead considered ¦ 11ax OFDM numerology with cyclic prefix duration = 0.8 us ¦ AP/STA sensitivity = - 90 dBm ¦ Spatial filter = ZF (with and without nulls) ¦ Omni PLCP header ¦ 11ax MCSs with target PER = 10%
AP PHY layer characteristics | AP max. Tx power = 24 dBm ¦ 4x2 array (0.5λ separation) ¦ Omni antenna elements ¦ NF = 7 dB
STA PHY layer characteristics | STA max. Tx power = 15 dBm ¦ 1 omni antenna ¦ NF = 9 dB