## Slide 1: Multi-RU support for OFDMA
Date: 2020-01-10
Authors:

## Slide 2: Introduction
It has been agreed in principle to support multiple RUs for a single STA in 11be
Open questions:
  How many simultaneous RUs?
  Any restrictions on the combination of RUs?
  Any restrictions on the locations of the RUs?

## Slide 3: Use cases
There are several use cases for support of multiple RUs:
  Non-OFDMA
    Motivation:
      Use OFDMA with multiple RUs assigned to one STA as an implementation of preamble puncturing for SU
  OFDMA
    Motivation:
      Increased efficiency
      More equitable spectrum assignment for multiple users

## Slide 4: Preamble puncturing
Sometime called “non-OFDMA”
  Still uses OFDMA format, but all RUs assigned to the same user
Essentially an implementation of preamble puncturing for single user
Specific constraints linked to preamble puncturing:
  Remove a sizeable (≥ 20 MHz) part of the spectrum from transmission
  Coarse granularity of RUs
  Mostly concerned with large RUs sizes

## Slide 5: OFDMA considerations
Considerations for (true) OFDMA may be different
  This submission will focus on the OFDMA case
One observation is that the current single-RU structure is mostly optimized for 2, 4, 8, 16 users (assuming equal rates)
  11ax RU allocation is inflexible and sometimes inefficient for other cases
Multi-RU support could allow more efficient support for other values of the number of users
See examples on next slides

## Slide 6: OFDMA for 2, 4 and 8 users
Fairly efficient
Minimal inefficiencies in spectrum
Easy to allocate equal BW to all users

## Slide 7: OFDMA for three users
Without multiple RUs:
One RU has double the BW as the other two
  Provided total BW is used efficiently
Use multi-RU to improve flexibility in spectrum allocation

## Slide 8: Possible allocations with multi-RU
More even distribution of spectrum
Contiguous/near-contiguous allocation
Max 2 RUs
Further improved distribution of spectrum
non-contiguous allocation
Max 2 RUs
Further improved distribution of spectrum
Contiguous/near-contiguous allocation
Max 3 RUs

## Slide 9: OFDMA for five users
Without multiple RUs:
Three RUs have double the BW as the other two
  Provided total BW is used efficiently

## Slide 10: Possible allocations with multi-RU
More even distribution of spectrum
Contiguous/near-contiguous allocation
Max 2 RUs
Some minor inefficiencies
Further improved distribution of spectrum
Contiguous/near-contiguous allocation
Max 3 RUs
Inefficiencies reduced

## Slide 11: OFDMA for six users
Without multiple RUs:
Two RUs have double the BW as the other four
  Provided total BW is used efficiently

## Slide 12: Possible allocations with multi-RU
More even distribution of spectrum
Contiguous/near-contiguous allocation
Max 2 RUs
Some minor inefficiencies
Further improved distribution of spectrum
non-contiguous allocation
Max 3 RUs
Inefficiencies reduced

## Slide 13: Conclusions
Multi-RU support provides more flexibility in equitable distribution of spectrum for any number of users
Efficiency depends on number of RUs allocated per user

## Slide 14: Contiguous vs. non-contiguous RUs
It is preferred to have one encoder per user and distribute the codes bits over the RUs
Modulating/demodulating the bits is not made more complex by RUs being contiguous or not
However, channel feedback is provided in contiguous blocks
  Large gaps between RUs will lead to inefficiencies there
  Small gaps won’t have much impact
Contiguous allocation is not a must from implementation complexity point of view, but having multiple RUs in tight clusters is preferred for cases with precoding

## Slide 15: How many RUs?
When trying to provide more equal spectrum for multiple users, major improvement can be achieved with 2 RUs
  NOTE: this submission only considered OFDMA cases
Having 3 RUs allows for further optimization in both overall BW efficiency and spectrum split

## Slide 16: Restrictions on RU sizes
For the examples shown, clear gains can be achieved by the following combinations of RUs:
  RU242 + RU106
  RU106 + RU52
Additional improvement are achieved by adding the following combinations:
  RU242 + RU52
  RU106 + RU26
  RU106 + RU52 + RU26
  RU106 + RU26 + RU26
  RU106 + RU106 + RU26
  RU106 + RU106 + RU52

## Slide 17: Conclusions
We have considered multi-RU requirements for the OFDMA case
Focus on improving spectrum split for number of users different from 2, 4, 8, 16
Propose to allow up to 3 RUs to be sent to a single user
Propose to allow at least the following combinations:
  RU242 + RU106
  RU106 + RU52
  RU242 + RU52
  RU106 + RU26
  RU106 + RU52 + RU26
  RU106 + RU26 + RU26
  RU106 + RU106 + RU26
  RU106 + RU106 + RU52
Multiple RUs should be “close together”, but being strictly contiguous placement is not required

## Slide 18: Straw Poll 1
Do you agree that multi-RU for OFDMA shall support up to three RUs to be sent to same user?
Y/N/A:

## Slide 19: Straw Poll 2
Do you agree that multi-RU for OFDMA shall support at least the RU combinations listed on Slide 17?
Y/N/A:

## Slide 20: Straw Poll 3
Do you agree that multi-RU for OFDMA shall support both contiguous and non-contiguous RU combinations?
Y/N/A:

## Slide 21: References
[1] Preamble puncturing and RU aggregation, IEEE 802.11-19/1869r0
[2] Multiple RU Combinations for EHT, IEEE 802.11-19/1907r0
[3] Multi-RU Support, IEEE 802.11-19/1908r0