## Slide 1: 11be preamble and forward compatibility
Date: 2020-01-10
Authors:

## Slide 2: Summary
Several agreements have been reached on 11be preamble
11be preamble design is intended to secure forward compatibility with future 802.11 generations (post-11be)
Forward compatibility of 11ax with 11be preamble was also discussed
  No agreement
  Several existing agreements may actually preclude this option for now
Intention of this submission is to present an 11be preamble design that allows forward compatibility with 11ax

## Slide 3: 11be preamble status
Tentative structure:
Agreed that:
  RL-SIG is present
  Mod(L_LENGTH, 3) = 0
  U-SIG BPSK modulated
  U-SIG has “Version-independent” bits and “Version-dependent” bits
    Including TXOP and BSS Color
  Version-independent bits are followed by Version-dependent bits
  U-SIG followed by EHT-SIG for MU format
  Other fields TBD

## Slide 4: Comparison with other preamble types

## Slide 5: Issues with proposed structure
11ax receive state machine not forward compatible with 11be preamble as currently proposed
  No access to TXOP or BSS Color in 11be preamble
No early PHY termination during auto-detect
  11be packets will be classified as 11a by 11ax receiver

## Slide 6: Discussion of forward compatibility
[3] proposes “forward compatibility” as a requirement for 11be preamble
One of the stated goals is:
  “Better coexistence than just L-SIG based deferral among future generations of 802.11 through universal fields”
    Presumably refers to knowledge of e.g. TXOP and BSS Color
Great Idea, however:
  Of limited value if only available for Wi-Fi generations after 11be
    2027? 2028?
  Renewed effort should be made to achieve the stated goal for 11ax instead

## Slide 7: Forward compatibility (2)
Attempts were made to extend forward compatibility to 11ax ([5])
  Significant number of bits can not be reused
  Concerns about changes in reserved bits
We believe forward compatibility can be achieved starting from 11ax, with minimal changes in the agreed design

## Slide 8: Design constraints
To achieve forward compatibility while addressing concerns expressed during earlier discussions, we should design a preamble that meets the following requirements:
11ax systems can process 11be preamble
  Preferably without ending in error indication
Maintain backwards compatibility with systems that don’t tolerate changes in reserved bits
TXOP and BSS Color can be extracted from 11be preamble by 11ax systems (without changes to 11ax)
11ax systems can terminate packet early after processing relevant parts of the 11be preamble
11be systems can distinguish between 11ax and 11be early enough to prepare for field following HE-SIG-A/U-SIG

## Slide 9: Proposal
The design constraints can be met with the following choices for the 11be preamble (L-SIG, U-SIG):
  Set L_LENGTH field in L-SIG such that L_LENGTH%3 = 1
  Set B0 of U-SIG1 equal to 0
  Use B1-B6 of U-SIG1 for BSS Color
  Set B23 of U-SIG1 equal to 1
  Use B0-B7 of U-SIG2 for TXOP
  Use remaining bits at will

## Slide 10: How it works: 11ax receiving 11be preamble (1)
11ax device recognizes the frame as an HE TB PPDU packet
  Based on L-SIG and FORMAT (B0 of HE-SIG-A1 equals 0)
  Will parse for bits of HE-SIG-A (for HE TB PPDU)
11ax device will process U-SIG as if it was HE-SIG-A

## Slide 11: How it works: 11ax receiving 11be preamble (2)
Reserved bit (B23 of HE-SIG-A) has the correct value
BSS Color (B1-B6 of HE-SIG-A1) and TXOP (B0-B7 of HE-SIG-A2) can be extracted
Since the device didn’t hear any Trigger frame, none of the SR information is relevant to the device – SR bits will be ignored
B7-B15 of HE-SIG-A2 can take any value since they are set by the Trigger frame – bits will be ignored
At this point the device also knows this packet is not intended for itself
  The device did not send a Trigger frame to solicit this packet
  Device can gracefully exit after processing HE-SIG-A
End Result:
  TXOP and BSS Color are available to 11ax device
  device terminates processing after U-SIG (without error condition)
  Forward compatibility achieved respecting the stated design constraints

## Slide 12: How it works: 11be system receiving 11ax preamble
If format is HE SU, HE ER SU or HE MU PPDU, process the appropriate 11ax format
If format is HE TB PPDU and 11ax Trigger was detected preceding packet, process as 11ax TB PPDU
If format is HE TB PPDU and 11ax Trigger was not detected:
  Extract TXOP, BSS Color
  Continue to process as 11be and confirm later whether or not this is correct
    E.g. EHT-SIG or other yet-to-be-designed part of preamble
    Whatever happens, correct processing is not required if the frame is 11ax instead of 11be (“orphaned” TB PPDU)

## Slide 13: How it works: 11be system receiving 11be preamble
The device recognizes the packet as 11ax TB PPDU, but without Trigger frame preceding it
  Decode as an 11be packet (i.e. assume U-SIG follows RL-SIG)
  This will be explicitly confirmed later during further preamble processing (e.g. EHT-SIG)
Extract TXOP and BSS Color
Parse the rest of the version-dependent bits
  Drop packet if invalid values are found or later part of preamble indicates an error, otherwise proceed as 11be
  If by chance the packet was in fact an 11ax TB PPDU responding to hidden node AP, no further processing is required beyond extraction of TXOP and BSS Color

## Slide 14: Addressing earlier concerns
During earlier 11ax forward compatibility discussion, a number of concerns were raised
  Backwards compatibility with non-compliant devices
  Clean design
  Timely auto-detection information

## Slide 15: Backwards Compatibility with deployed devices
During discussion, reference was made to deployed devices that don’t support changing of reserved bits
  Issue was never clearly explained
  We need to understand the limitations to be able to evaluate design options
  What is the failure?
    Packet dropped? Device crash?
What is backwards compatibility anyway?
  It’s important to not cause issues with already deployed devices
  It’s OK if some deployed devices miss out on new functionality, while other fully compliant devices are able to use it
Proposed solution does not expose devices to packets that can not already encountered in the field

## Slide 16: Comment on “Clean design”
It has been argued that having Version-independent bits interspersed with Version-dependent bits was not as “clean”
Everything else being equal, clean design is preferred
However, major functionality should not be sacrificed in the name of “clean design”
  Choose “useful” over “clean”
  Forward compatibility is important enough
Other examples of “useful” over “clean” design
  L-SIG based packet length signaling
  BW signaling in non-HT

## Slide 17: Early availability of FORMAT bit
B0 of U-SIG1/HE-SIG-A1 is essential in distinguishing between 11ax/11be formats
It appears that FORMAT bit (B0 of U-SIG1/HE-SIG-A1) is only available after full processing of U-SIG/HE-SIG-A
The field following U-SIG/HE-SIG-A may be different depending on the actual format (HE/EHT)
  Early availability of the format information may be needed for timely change in the state machine
In reality, the FORMAT bit is the first bit out of the encoder and first bit out of the deinterleaver
  Can be available well before the end of U-SIG/HE-SIG-A

## Slide 18: Conclusion: forward compatibility should include 11ax
As currently defined, forward compatibility won’t be available until the next major update after 11be
  First 11be deployed ~ end 2023
  First post-11be deployed ~ end 2027?
That’s a long time to wait for a feature that was deemed to be an important design criterion
No guarantee what the next generation will look like
  Will it need/use forward compatibility?
No guarantee that deployed non-compliant systems will allow full use of the functionality
Without inclusion of 11ax, forward compatibility as currently defined is mostly academic and of little practical value

## Slide 19: A plea for real forward compatibility
11be preamble should be designed such that 11ax is forward compatible with 11be preamble
  Only this achieves meaningful forward compatibility
Will make a stronger case for forward compatibility for subsequent generations
  “setting a good example”

## Slide 20: Straw Poll
Do you agree that 11be preamble should be designed such that 11ax is forward compatible with the 11be preamble?
NOTE: “forward compatible” means having access to at least TXOP and BSS COLOR from the 11be preamble
Y/N/A:

## Slide 21: References
[1] Further discussion for 11be preamble, IEEE 802.11-19/1486r9
[2] 11be Preamble Structure, IEEE 802.11-19/1516r4
[3] Forward Compatibility for WiFi Preamble Design” , IEEE 802.11-19/1519r0
[4] EHT Preamble Design, IEEE 802.11-19/1540r7
[5] Preamble Design Consideration for 11be follow-up, IEEE 802.11-19/1569r1
[6] Further Ideas on EHT Preamble Design, IEEE 802.11-19/1870r4
[7] 802.11be Preamble and Auto-Detection Analysis and Comparison, IEEE 802.11-19/1883r0