## Slide 1: Multi-Link Feature Candidates For Release 1
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | email
Huizhao Wang | Quantenna, a division of ON Semi |  |  | huizhao.wang@onsemi.com
Sigurd Schelstraete |  |  |  | 
Abhishek Agrawal |  |  |  | 
Debashis Dash |  |  |  | 

## Slide 2: Introduction (1/2)
Contribution [1] recommends 11be to adopt phased releases to address time to market concern. And it proposes Release 1 of 11be to have following key features:
  320 MHz bandwidth
  4K QAM
  Multiple RUs to a single STA
  Multi-link operation
We support the phased release and the key feature set of Release 1.
For MLO, we propose that Release 1 to focus on basic functionalities, basic performance enhancements, basic power save modes, and basic non-STR constrains (STR AP to non-STR non-AP STA only)

## Slide 3: Introduction (2/2)
Proposed basic features to be included for Release 1:
  Multi-link discovery, setup & teardown, Security Association (authentication, PTK, GTK key-exchange)
  TID binding options: allow MPDUs from the same TID to be sent on:
    All TIDs are allowed on all the setup links by default
    All TIDs are mapped to a subset of links
  BlockACK agreement with buffer size up to 1K
  Support AP MLD is STR capable, non-AP MLD can be STR or non-STR capable
  STR AP MLD communication with non-STR non-AP MLD:
    DL PPDUs on the multiple links aligned at the END time with TBD time margin
    Avoid DL transmission on one (or more links), and trigger UL transmission on another link(s)
    Links of STA MLD conducts either independent EDCA channel access, or truncated EDCA channel access provided it will be compliant to RF regulatory requirements
    Allow alignment for Uplink PPDUs across multiple links at start time and ending time
  Power save mode:
    Power save state signaling on per link using existing mechanisms
    MLD level TIM
Note: Demonstrate performance gain over multiple link operation without MLD

## Slide 4: Straw Poll 1
Do you agree with the selected features in page 3 for MLO Release 1?
Y/N/A

## Slide 5: References
[1] IEEE802.11-19/2153r0, “Adopting a release framework to meet 802.11be timeline”