## Slide 1: EHT-LTFs Design
Date: 2020-01-20
Authors:
Name | Affiliations | Address | Phone | email
Dandan Liang | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | Dandan.liang@huawei.com
Ming Gan |  |  |  | 
Wei Lin |  |  |  | 

## Slide 2: Abstract
This contribution proposes the EHT-LTFs design methods for 320MHz and 240MHz.

## Slide 3: Introduction
In 11ax, one of three HE-LTF types is applied in the HE-LTF field of an HE PPDU: 1x HE-LTF, 2x HE-LTF, 4x HE-LTF [1].
The 1x HE-LTF, 2x HE-LTF and 4x HE-LTF sequences are defined for 20/40/80/160/80+80MHz.

## Slide 4: Introduction
11be Tone plan Motions have been passed [2]:
  320MHz/160+160MHz transmission
    11be reuses 11ax tone plan for 20/40/80/160/80+80MHz PPDU
    For 320MHz and 160+160MHz PPDU, 11be uses duplicated HE160 for both OFDMA and non-OFDMA tone plan
996 + 5DC /
994 + 7DC
996 + 5DC /
994 + 7DC
12 Edge
11 Edge
996 + 5DC /
994 + 7DC
EHT 320MHz/160+160MHz Tone Plan
23
Null
996 + 5DC /
994 + 7DC
23
DC
23
Null

## Slide 5: Introduction
11be Tone plan Motions have been passed [2]:
  240MHz/160+80MHZ transmission
    11be 240/160+80 MHz transmission consists of 3x80MHz segments while the tone plan of each 80MHz segment is the same as HE80 in 11ax
    Whether 240/160+80 MHz is formed by 80MHz channel puncturing of 320/160+160 MHz is TBD
996 + 5DC /
994 + 7DC
12 Edge
11 Edge
996 + 5DC /
994 + 7DC
EHT 240MHz/160+80MHz Tone Plan
11+12
Null/DC
996 + 5DC /
994 + 7DC
11+12
Null/DC

## Slide 6: Introduction
Recommend that 11be LTFs reuses 11ax LTFs in 20/40/80/160/80+80MHz PPDU for considering backward compatibility.
For 320/160+160/240/160+80MHz, low PAPR and low overhead are two main metrics for designing EHT-LTFs, some EHT-LTFs design considerations were discussed in [3-6].
  Low PAPR [3]
  Reducing EHT-LTFs overhead: small symbol duration[3], orthogonal mapping in frequency domain [4] and tone-interleaved LTFs[5]

## Slide 7: Introduction
In this contribution, the EHT-LTFs are proposed based on defined tone plan for 320/160+160MHz and 240/160+80MHz.
  Design considerations:
    Low PAPR:
      all sizes of RUs
      26, 52, 106, 242, 484, 992, 2x996, 3x996, 4x996 tones RU
    Low Overhead:
      Methods are as 11ax -- 1x, 2x symbol duration
      1x symbol duration: 6.4 µs excluding GI
      2x symbol duration: 12.8 µs excluding GI
      4x symbol duration for EHT-LTFs: open-minded
  Potential design methods:
    Option 1: Repeat 11ax 160MHz LTF sequences, apply the coefficient value on the second 160MHz part.
    Option 2: Repeat 11ax 80MHz LTF sequences, apply the coefficient value on the second - fourth 80MHz part.

## Slide 8: Simulation Parameters
EHT-LTFs type: 1x, 2x symbol duration
RU size: 26, 52, 108, 242, 484, 996, 2x 996, 3x 996 and 4x 996 tones
P matrices of dimension: 16x16
Pilot position: same as 11ax 80MHz/160MHz

## Slide 9: EHT-LTFs of 320MHz/160+160MHz

## Slide 10: 320MHz 2x EHT-LTF
Option 1: Repeat 11ax 160MHz LTF sequences and apply the coefficient value on the second 160MHz part.
6.23 (80MHz) | 6.69 (80MHz) | 6.23 (80MHz) | 6.69 (80MHz)
6.72 (160MHz) |  | 6.72 (160MHz) | 
8.9783 (240MHz) |  |  | 
 | 8.9935 (240MHz) |  | 
9.3908 (320MHz) |  |  | 
Worst PAPR (dB) of proposed 2x EHT-LTF @320MHz
EHT LTF320MHz_2x = [LTF160MHz_2x, 023, LTF160MHz_2x ]

## Slide 11: 320MHz 2x EHT-LTF
Option 2: Repeat 11ax 80 LTF sequences and apply the coefficient value on the second - fourth 80MHz part.
6.23 (80MHz) | 7.00 (80MHz) | 6.93 (80MHz) | 7.25 (80MHz)
6.53 (160MHz) |  | 6.7287 (160MHz) | 
7.50 (240MHz) |  |  | 
 | 7.55 (240MHz) |  | 
7.55 (320MHz) |  |  | 
EHT-LTF320MHz_2x = [LTF80MHz_part1_2x, LTF80MHz_part2_2x, LTF80MHz_part3_2x, LTF80MHz_part4_2x, LTF80MHz_part5_2x, 023, LTF80MHz_part1_2x, LTF80MHz_part2_2x, -LTF80MHz_part3_2x, -LTF80MHz_part4_2x, -LTF80MHz_part5_2x, 023, -LTF80MHz_part1_2x, LTF80MHz_part2_2x, -LTF80MHz_part3_2x, LTF80MHz_part4_2x, -LTF80MHz_part5_2x, 023, LTF80MHz_part1_2x, LTF80MHz_part2_2x, LTF80MHz_part3_2x, -LTF80MHz_part4_2x, LTF80MHz_part5_2x],
Worst PAPR (dB) of proposed 2x EHT-LTF @320MHz
here HE-LTF80MHz_2x = [LTF80MHz_part1_2x, LTF80MHz_part2_2x, LTF80MHz_part3_2x, LTF80MHz_part4_2x, LTF80MHz_part5_2x ].

## Slide 12: 240MHz 2x EHT-LTF
Whether 240/160+80 MHz is formed by 80MHz channel puncturing of 320/160+160 MHz is TBD [2]
Open-minded for designing 240 EHT-LTF sequences.

## Slide 13: Conclusion
Recommend that EHT-LTFs reuses HE-LTFs in 20/40/80/160/80+80MHz PPDU for considering backward compatibility.
Propose that design methods of EHT-LTFs for 320/160+160/240/160+80MHz PPDU.

## Slide 14: Appendix: 160MHz 2x HE-LTF
4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.37 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46
4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 | 
5.42 |  |  |  |  | 5.41 |  |  |  | 5.42 |  |  |  |  | 5.41 |  |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  | 
5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  | 
6.15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.01 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.37 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46
4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 | 
5.42 |  |  |  |  | 5.41 |  |  |  | 5.42 |  |  |  |  | 5.41 |  |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  | 
5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  | 
6.23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.69 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Worst PAPR (dB) of proposed 2x HE-LTF @160MHz

## Slide 15: Appendix: 80MHz 2x HE-LTF
4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.37 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46 | 4.46
4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 |  | 4.69 |  | 4.69 |  |  | 4.69 |  | 4.69 | 
5.42 |  |  |  |  | 5.41 |  |  |  | 5.42 |  |  |  |  | 5.41 |  |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  |  | 5.41 |  |  |  |  | 5.42 |  |  | 
5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  |  | 5.58 |  |  |  |  |  |  |  | 
6.15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6.23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6.01 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Worst PAPR (dB) of proposed 2x HE-LTF @80MHz

## Slide 16: Straw Poll #1
Do you agree to add the following text into SFD?
-EHT-LTFs sequences are same as HE-LTFs sequences in 20/40/80/160/80+80MHz PPDU

## Slide 17: Straw Poll #2
Do you agree to include 4x EHT-LTF for 320MHz/160+160MHz/240MHz/160+80MHz?

## Slide 18: Reference
[1] <Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications>, 802.11-2016.
[2] Alfred Asterjadhi, <Tgbe Novermber 2019 Meeting Agenda>, IEEE 802.11-19/1722r11.
[3] Jinmin Kim, et al, <Consideration of EHT-LTF>, IEEE 802.11-19/1925r0.
[4] Dandan Liang, et al, <EHT P matrices discussion>, IEEE 802.11-19/1980r0.
[5] Junghoon Suh, et al,<Orthogonal Sequences based Reference Signal for LTF Reduction>, IEEE 802.11-19/1585r0.
[6] Sameer Vermani, et al, <Performance Comparisons for LTF Designs for EHT>, IEEE 802.11-19/1867r0.