## Slide 1: A BAR Variant For Multi-Link Operation
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook |  |  | chunyuhu@fb.com

## Slide 2: Background
Multi-link operation supports A-MPDU of one BA session over multiple links
The sequence number of A-MPDU transmitted over each link can have gap due to missing numbers are transmitted over the other link(s)
Consider scenario in next slide

## Slide 3: Holes in Local Rx Reorder Buffer
The MLO STA may have local rx buffer before forwarding to the common recorder buffer
There should be a signaling to allow reorder-buffer @ STA1/MAC-SAP2 to forward MPDUs to global one ASAP.
  Avoid any time-out delay
  Avoid the global recorder buffer management to poll local rx buffer status

## Slide 4: Proposed Solution
Define a new BAR variant (L-BAR) that notifies the A-MPDU responder that it skipped transmitting a sequence number range or numbers set in a bitmap; and it avoids moving the BA window start SN
Allow it to be aggregated with DATA frames
  A-MPDU3 can include an L-BAR
  Doesn’t require an immediate BA if aggregated within an A-MPDU
For example: repurpose bit4 to indicate this new type

## Slide 5: Straw Poll 1
Do you agree to define a new type of BAR used in the multi-link operation that allows to notify the A-MPDU responder that it has skipped a range of sequence numbers and/or a subset of sequence numbers?
Y
N
A

## Slide 6: Straw Poll 2
Do you agree that the new BAR defined in straw poll 1 can be aggregated with DATA frames in an A-MPDU?
Y
N
A