## Slide 1: Channel Sounding for Multi-AP CBF
Date: 2019-01-10
      Jan. 2020

## Slide 2: Introduction
Multi-AP coordinated beamforming (CBF) and joint transmission (JT) are interesting topics under study in 11be [1-6]
CSI information is critical for the multi-AP CBF and JT
  Requires CSI info between AP and in-BSS STA and OBSS STA
  CSI between AP and OBSS STA (challenging and require new design)
  CBF and JT require different levels of CSI info
    Separate sounding sequences can be designed for JT and CBF
This submission discusses design considerations for channel sounding in multi-AP CBF
  Focus on sequential channel sounding and explicit CSI feedback
  Enable AP to obtain CSI from OBSS STA
  Align with 11ax sounding protocol
      Jan. 2020

## Slide 3: Recap: Passed Motion for Multi-AP Sounding
The following motion has been passed in IEEE TGbe, Nov. 2019 [7]
  “802.11be shall provide a joint NDP sounding scheme as optional mode for multiple-AP systems.
  Sequential sounding scheme that each AP transmits NDP independently and sequentially without overlapped sounding period of each AP can also be used in multi-AP systems.”
      Jan. 2020

## Slide 4: Recap: 11ax Sounding Sequence
11ax sounding protocol with more than one STA
SIFS
HE
NDPA
HE
NDP
AP
STA1
STA2
…
STAN
Compressed Beamforming/CQI 1
BFRP
Trigger
SIFS
SIFS
Compressed Beamforming/CQI 2
Compressed Beamforming/CQI N
…
One or more sequences
Sounding
Announcement
NDP
Transmission
CSI Feedback
      Jan. 2020

## Slide 5: Multi-AP Channel Sounding
Several contributions in TGbe discussed multi-AP channel sounding [8-10]
In general multi-AP channel sounding with explicit CSI includes three parts:
  Channel sounding announcement
  NDP frames transmission
  CSI report feedback
      Jan. 2020

## Slide 6: Channel Sounding Announcement
The multi-AP channel sounding can be announced by one or more NDPA frame(s) from master AP and/or slave AP
The sounding announcement frame(s) should include
  The parameters of the following NDP frame(s)
  The info of Slave APs that participate in the sounding sequence
  ID info of STAs that will join this channel sounding (possibly from different BSSs)
  STA’s CSI feedback format (quantization, spatial stream number, frequency segment)
      Jan. 2020

## Slide 7: NDP Frame Transmission
In CBF, the CSI between AP and OBSS STA is needed for spatial domain interference mitigation
Transmission and reception of the join NDP frame set higher bars for AP and STA
In channel sounding for CBF, NDP frames from multi-AP can be transmitted sequentially for implementation simplicity:
  Different AP sequentially transmits its own NDP frame
  Each AP’s PHY NDP frame can be P-matrix multiplexed
  Reuse legacy channel estimation and CSI report preparation
      Jan. 2020

## Slide 8: CSI Report Feedback
CSI report carries CSI info of NDP listened by STA
  Compressed beamforming feedback matrix/CQI
  Different AP’s CSI info is identified by BSSID/color or other ID
Multi-AP can use trigger frame to solicit CSI report for high efficiency
  Each AP can solicits CSI from STAs in its own BSS or in OBSS
    The STA that has measured PHY NDP of OBSS AP will respond to the BFRP sent by the OBSS AP
      Jan. 2020

## Slide 9: Sounding Sequence for CBF
For CBF-only multi-AP scenario, an example sounding sequence with two APs is:
  Reuse 11ax sounding sequence
  STA11 to STA1N associate with AP1, STA21 to STA2N associate with AP2
  NDPA1 and NDPA2 includes ID info of STAs in both AP1’s and AP2’s BSS
  In AP1’s sounding sequence, CSI report includes CSI info for NDP1
  In AP2’s sounding sequence, CSI report includes CSI info for NDP2
CSI
report
SIFS
NDP1
Master: AP1
Slave: AP2
STA11
STA1N
SIFS
NDPA2
NDP2
STA21
STA2N
BFRP
Trigger
SIFS
CSI
report
CSI
report
BFRP
Trigger
SIFS
SIFS
…
…
CSI
report
NDPA1
SIFS
      Jan. 2020

## Slide 10: Conclusions
A sequential channel sounding sequence is proposed for multi-AP CBF
The proposed sounding sequence reuses the 11ax sounding protocol and includes three parts:
  Multi-AP Channel sounding announcement(s)
  NDP frame(s) transmission
  Explicit CSI report feedback(s)
      Jan. 2020

## Slide 11: Backup
The following motion has been passed in IEEE TGbe, Jan. 2020 [13]
“11be shall define a mechanism to determine whether an AP is part of an
AP candidate set and can participate as a shared AP in coordinated AP
transmission initiated by a sharing AP.”
      Jan. 2020

## Slide 12: Reference
IEEE 802.11-19/0772 Multi-AP Collaborative BF in IEEE 802.11
IEEE 802.11-19/0103 AP Coordination in EHT
IEEE 802.11-19/0071 Coordinated Multi-AP Transmission for EHT
IEEE 802.11-18/1982 Consideration on multi-AP Coordination for EHT
IEEE 802.11-18/1510 AP Coordinated Beamforming for EHT
IEEE 802.11-19/0094 Joint Processing MU-MIMO
IEEE 802.11-19/0094 Specification Framework for TGbe
IEEE 802.11-19/0448 Multi-AP Transmission Procedure
IEEE 802.11-19/1593 Joint Sounding for Multi-AP Systems
IEEE 802.11-19/1535 Sounding for AP Collaboration
IEEE 802.11-19/1097 Sounding procedure in AP collaboration
IEEE 802.11-19/1134 Consideration of Multi-AP Sounding
IEEE 802.11-20/0566 Compendium of straw polls and potential changes to the Specification Framework Document
      Jan. 2019

## Slide 13: SP#1
Do you support that multiple APs can sequentially use an 11ax-like sounding sequence to collect CSI from the in-BSS STAs and OBSS STAs?
  Each AP’s sounding sequence is similar to the 11ax sounding protocol with multiple STAs (NDPA + NDP + BFRP TF + CSI report).
Y: 81 N: 4 Abstain: 43
      Jan. 2020

## Slide 14: SP#2
In sequential channel sounding sequence for multi-AP, do you support that the NDPA frame and BFRP TF frame will include ID info for OBSS STA?
  The details of the NDPA, BFRP TF and the ID info are TBD.
Y: 75 N: 9 Abstain: 45
      Jan. 2020

## Slide 15: SP#3
In sequential channel sounding sequence for multi-AP, do you support:
  STA processes the NDPA frame and the BFRP Trigger frame received from OBSS AP
  If polled by the BFRP trigger frame from OBSS AP, the STA responds with the corresponding channel state information (CSI) to OBSS AP
  Note 1: the details of CSI report are TBD.
  Note 2: the OBSS AP belongs to the multi-AP set serving the STA and the details regarding formulation of the multi-AP set are TBD.
Y: N: Abstain:
      Jan. 2020