## Slide 1: Further Discussions on Preamble Puncturing and SIG-B (EHT-SIG) Signaling
Date: 2020-04-08
Authors:
Name | Affiliations | Address | Phone | email
Sanghyun Kim | WILUS, Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0524 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Apr 2020
Sanghyun Kim (WILUS), et al.

## Slide 2: Introduction
EHT supports wider bandwidth operation
  EHT includes support for 320 MHz bandwidth [1]
  However, it is hard to expect the whole 320 MHz channel to be idle in dense environments
  EHT needs to enhance the utilization of non-contiguous channel access method [2][3]
In our previous contribution [4], we evaluated the performance of the various content channel structures in terms of puncturing flexibility
  Recently, [5][6] introduced different EHT-SIG information per 80/160 MHz
  In this contribution, we further evaluate puncturing performances along with the different EHT-SIG per 80 MHz segment
We evaluate two EHT-SIG signaling methods for STAs parked in non-primary segments, and analyze puncturing performances

## Slide 3: Two EHT-SIG content channels per 80 MHz segment
[5][7] proposed the preamble design that allows different signaling information conveyed on different 80 MHz segment
This contribution considers the followings as a starting point for discussion
  EHT-SIG per 80 MHz segment conveys different contents
  EHT-SIG per 80 MHz segment has two content channels similar to HE-SIG-B
Receiving two EHT-SIG content channels in non-P80 segment
  11be STA parked in a non-P80 segment has no dedicated P20 channel to receive puncturing information, therefore the locations of non-punctured content channels are unknown to the STA
1
2
1
2
5
6
5
6
7
8
7
8
3
4
3
4
80 MHz
Segment #4
80 MHz
Segment #3
80 MHz
Segment #2
80 MHz
Segment #1
(P80)
Content channel structure
of 320 MHz PPDU

## Slide 4: Considerations on the signaling of non-primary segment
There may be two methods to ensure preamble signaling reception for the STAs parked in non-P80 segments
  Method 1) Set virtual P20 for each non-P80 segments
    STAs parked in a non-P80 segment decode U-SIG in the virtual P20
    Similar complexity to 11ax on the STA-side
    A virtual P20 channel cannot be punctured when its non-P80 segment has non-punctured channels
    If a virtual P20 channel is punctured, its non-P80 segment is also punctured
  Method 2) Parallel decoding of four 20 MHz sub-channels
    STAs parked in a non-P80 segment decode all four 20 MHz sub-channels to detect non-punctured sub-channels of the segment
    It requires improved processing capability to 11be STAs compared to 11ax STAs

## Slide 5: Available puncturing patterns per 80 MHz segment
Method 1: Set virtual P20 for each non-P80 segments
  Available puncturing patterns per segment are the same with 11ax P80’s puncturing patterns
Method 2: Parallel decoding of four 20 MHz sub-channels
  More flexible puncturing patterns are available if two different content channels are present within the segment
Idle
Busy
Idle or
Busy
Available puncturing patterns
of Method 2
(per segment)
Assumption 1. Content channel structure per segment is similar to 11ax (1, 2, 1, 2)
Assumption 2. Puncturing patterns per 80 MHz segment are individually determined
-Even if only P20 is IDLE within P80 channel, non-P80 segment can utilize preamble puncturing
Available puncturing patterns
of Method 1
(per segment)
Busy
Busy
Busy
Busy
(Virtual)
P20
(Virtual)
P20
(Virtual)
P20
Busy
(Virtual)
P20

## Slide 6: Simulation results
Throughput results of method 1 and method 2 compared with 11ax design
  Simulation setup in appendix
Method 1 shows lower TPUT performance than 11ax design
  For the heavy loaded OBSS case, the method 1’s virtual P20 limitation incurs 20 % lower TPUT performance than 11ax design
Method 2 increases TPUT performance in the light loaded OBSS case
  However, for the heavy loaded OBSS cases, the method 2 also shows slight performance drop than 11ax design
Chart: Throughput (Mbps)
| 11ax content channel design (1, 2, 1, 2) | METHOD 1 (Set Virtual P20) | METHOD 2 (Decode 80 MHz)
OBSS Load: 10 Mbps | 468.27 | 457.4 | 499.67
OBSS Load: 50 Mbps | 181.8 | 157.25 | 178.98
-2.5 %
TPUT
-20 %
TPUT
+6.5 %
TPUT
-1.5 %
TPUT
Baseline
performance

## Slide 7: Performance Analysis
Method 1 and 2 have difficulty in utilizing non-P80 segments due to limited puncturing patterns
  Non-primary 80 MHz channel status rarely matches the available puncturing patterns
    For the P80 segment, one of two content channels is always present in the P20, but non-P80 segments have no dedicated channel to receive one of the two content channels
  STAs parked in non-P80 segment are relatively hard to be served
  For the different EHT-SIG per 160 MHz, a similar phenomenon may occur at the secondary 160 MHz
We need to consider ways to improve the signaling success probability on the non-primary segments
Never punctured
P20
VP
20
VP
20
VP
20
Non-P80 segments have no P20-like channel that never punctured
P80
non-P80#1
non-P80#2
non-P80#3
Idle
Busy
Idle or
Busy
Chart: OBSS Load: 50 Mbps
| 1 (P20) | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
11ax content channel design (1, 2, 1, 2) | 54.827 | 37.993 | 17.369 | 14.978 | 21.999 | 17.54 | 14.648 | 15.745 | 14.565 | 18.908 | 18.819 | 16.34 | 18.666 | 17.387 | 13.044 | 17.832
METHOD 1 (Set Virtual P20) | 54.824 | 37.95 | 17.423 | 14.747 | 17.395 | 13.58 | 6.0933 | 5.7204 | 15.934 | 12.658 | 6.5451 | 6.9689 | 15.363 | 13.133 | 4.8038 | 6.31
METHOD 2 (Decode 80 MHz) | 54.352 | 37.633 | 16.925 | 14.338 | 17.409 | 15.354 | 15.684 | 15.31 | 15.596 | 15.035 | 15.914 | 16.11 | 14.823 | 15.37 | 14.13 | 15.477
Chart: OBSS Load: 10 Mbps
| 1 (P20) | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
11ax content channel design (1, 2, 1, 2) | 81.161 | 70.546 | 57.818 | 55.962 | 50.393 | 48.559 | 48.642 | 47.535 | 48.435 | 48.448 | 49.834 | 48.793 | 48.856 | 49.394 | 47.408 | 49.727
METHOD 1 (Set Virtual P20) | 80.705 | 70.3 | 57.769 | 55.702 | 49.505 | 44.151 | 38.133 | 37.048 | 48.241 | 43.356 | 37.861 | 37.193 | 48.336 | 44.325 | 35.996 | 37.769
METHOD 2 (Decode 80 MHz) | 80.509 | 69.897 | 57.495 | 55.63 | 48.941 | 47.824 | 48.563 | 47.404 | 47.19 | 47.05 | 48.76 | 48.146 | 47.338 | 48.082 | 46.819 | 48.535

## Slide 8: Necessities of improving content channel structure
Signaling success probability is highly dependent on the content channel structure
  Our previous contribution concluded that two-content channel structure has good balance in terms of channel accessibility and signaling overhead, and single-content channel structure has the best channel accessibility (puncturing flexibility) [4]
11ax-like two-content channel structure may not be the best structure for EHT-SIG of the non-primary segment
Different channel accessibility of each segments can cause fairness issue between STAs parked in the primary segment and STAs parked in non-primary segments
We need to consider new content channel structures to enhance signaling success probability to improve puncturing flexibility

## Slide 9: Summary
We showed two signaling methods for the non-primary segments and analyzed puncturing flexibility of the two methods incorporating different EHT-SIG per 80 MHz segments
  Signaling failure on the non-P80 segments degrades puncturing flexibility and causes fairness issue between STAs parked in the P80 segment and the non-P80 segments
We propose to further study new content channel structures of EHT-SIG

## Slide 10: Straw Poll 1
Which option do you prefer for preamble decoding in the non-primary segment?
  Opt. 1 : Set virtual P20 for each non-P80 segments
    A virtual P20 channel cannot be punctured when its non-P80 segment has non-punctured channels
  Opt. 2 : Parallel decoding of four 20 MHz sub-channels
    STAs parked in a non-P80 segment decode all four 20 MHz sub-channels to detect non-punctured sub-channels of the segment

## Slide 11: References
[1] 11-19-1262-08-00be-specificication-framework-for-tgbe
[2] 11-19-1242-00-00be-wider-bandwidth-channel-access-in-eht
[3] 11-19-1190-00-00be-improved-preamble-puncturing-in-802-11be
[4] 11-19-1606-00-00be-preamble-puncturing-and-sig-b-signaling
[5] 11-20-0439-00-00be-efficient-eht-preamble-design
[6] 11-20-0020-02-00be-consideration-for-eht-sig-transmission
[7] 11-20-0380-00-00be-u-sig-structure-and-preamble-processing

## Slide 12: Appendix: Simulation Setup
Investigate performances of different preamble puncturing options in OBSS environments
EHT BSS
  1 BSS operating BW: 320MHz
  1AP-1STA, DL only, full buffer
  MCS 7 fixed, A-MPDU (10 MPDUs per non-punctured 20 MHz), 1 MPDU=1500 Bytes
  PPDU BW: P20, P40, P80, P160, P320, and preamble puncturing BW based on its CCA results and the method 1/2
  Assume EHT-SIG field overhead of 4 symbols (16 us) required per 20MHz in PPDU BW
OBSS
  Among 320MHz channels, 3 OBSSs exist per each 80MHz segment
  Each OBSS’ operating BW: 80MHz / 40MHz / 20MHz each
  Primary channel is randomly chosen within each 80MHz segment
  PPDU BW: P20, P40, or P80 based on CCA results (no puncturing)
  Each OBSS has 1AP-1STA, DL only, CBR 10Mbps or CBR 50Mbps
  MCS 7 fixed, A-MPDU (Max 64 MPDUs), 1 MPDU=1500 Bytes

## Slide 13: Appendix: Simulation Setup (OBSS example)
P20
EHT BSS
(320 MHz)
OBSS 1
(80 MHz)
OBSS 2
(40 MHz)
OBSS 3
(20 MHz)
Fixed P20
location
3 OBSS per 80MHz segment
random P20 location for each OBSS
80 MHz
320 MHz