## Slide 1: Discussion on eBCS Service Info Format
Date: 2020-01-12
Authors:

## Slide 2
Abstract
In this contribution, we discuss the preference on how to design eBCS Service Discovery Info.

## Slide 3: Introduction
An eBCS AP needs to indicate its eBCS service information
eBCS Service Information may be needed in several frames including:
  Beacon
  eBCS Info frame
  eBCS Service Discovery frame
The format may benefit from a more modular design of the eBCS Service Information
  E.g., in the form of a information element

## Slide 4: eBCS Service Info
The eBCS Service Info included in eBCS Info frame is [3]
The eBCS Service Info included in eBCS Service Discovery frame is [4]
Similar eBCS Service Info is expected in the beacon
 | Category | Public Action | Sequence Number | Fragmentation Control | eBCS Advertisement Interval | Contents Information Number | Contents Information 1 | … | Contents Information N
Octets: | 1 | 1 | 8 | 1 | 1 | 1 | variable |  | variable

## Slide 5: Proposed Update to the SFD
Define a eBCS Service Information element and include it in all of the frames:
  Beacon
  eBCS Info frame
  eBCS Service Discovery frame
  Probe Response frame

## Slide 6
References
[1] IEEE 11-19/1429r2, 802.11bc Specification Framework Document, November 2019
[2] IEEE 11-19/1001r1, Functional Requirements Document Proposed Update, January 2020
[3] IEEE 11-19/2159r0, Draft Text for 9.6.7 eBCS Info Frame, January 2020
[4] IEEE 11-20/135r0, Draft Text for 9.6.33 eBCS Service Advertisement Frame, January 2020

## Slide 7: Straw Poll
Do you agree that TGbc should define a eBCS Service Information element and include it in all of the following frames:
  Beacon frame
  eBCS Info frame
  eBCS Service Discovery frame
  Probe Response frame