## Slide 1: EPD and LPD Terminology Misalignment in IEEE Std 802.1 and 802.11
Date: 2020-01-28
Authors:

## Slide 2: Abstract
Inconsistencies in EPD and LPD Terminology between IEEE Std 802.1 and IEEE Std 802.11 are highlighted.

## Slide 3: Summary
  EtherType protocol discrimination (EPD) and LLC protocol discrimination (LPD) are discussed in IEEE Std 802, IEEE Std 802.1AC, IEEE Std 802.1Q, and IEEE Std 802.11.
  Overall, the descriptions are imprecise, inconsistent, and confusing.
  It’s a problem for various reasons, particularly because new standards are supposed to support EPD, but we don’t really know what that means.
  The conflict in definitions should be resolved.

## Slide 4: Background Contributions
  • R. Marks, “What are EPD and LPD?”
  maint-Marks-epd-lpd-0719-v02.pdf
  • N. Finn, “Why the EPD/LPD information in IEEE 802, IEEE 802.1AC, and 802.1Q must be fixed”
  maint-finn-epd-lpd-errors-0919-v02.pdf
  • R. Marks and N. Finn, “Clarifying EPD and LPD”
  maint-Marks-Finn-hlpde-1119-copyright
  Files available at:
  http://www.ieee802.org/1/files/public/docs2019/

## Slide 5: EPD and LPD, per IEEE Std 802
EPD and LPD were (to my knowledge) originally specified in IEEE Std 802-2014.
EPD… uses the EtherType value made available to the LLC sublayer through the MSAP
LPD… uses the addresses defined in ISO/IEC 8802-2, including the Subnetwork Access Protocol (SNAP) format
  LLC using DSAP/SSAP is LPD
  SNAP carrying an EtherType is also LPD (uses 802.2 addresses)
    IEEE Std 802 specifically refers to “LPD-based SNAP identifier mechanism”
IEEE Std 802.3 is capable of natively representing the EtherType within its MAC frame format, which is used to support EPD
IEEE Std 802.3 natively supports ISO/IEC 8802-2 LPD (over a limited range of frame sizes)
  If the Type/Length field is <1501, then it represents a Length <1501 and we have LPD; this can include SNAP carrying an EtherType
In other IEEE 802 networks, such as for IEEE Std 802.11™, LPD is also achieved using SNAP
…an LPD PDU…
“In either of these techniques, the EtherType is effectively being used as a means of identifying an LSAP that provides LLC sublayer service to the protocol concerned.”
Ethernet-like Type/Length coding is not EPD; it is a system to make allow support for both EPD & LPD
LPD can use either EtherType or DSAP/SSAP as the actual protocol identifier.

## Slide 6: Rough Terminology Map

## Slide 7: MAC Requirements
  MAC needs to support LLC (DSAP/SSAP) identifiers
    EPD does not support these
    therefore MAC must support LPD
  MAC needs to support EtherType identifiers
    It can do this with LPD
    It can optionally support EPD too
  Per IEEE Std 802, going forward, MACs need to “support EPD.” This means:
    Enabled to carry both EPD and LPD frames.
    Enabled to differentiate EPD and LPD frames.
  Ethernet does this
    Differentiates by Type/Length field encoding
    At the IEEE 802 level, we shouldn’t care how the differentiation per frame is conveyed.
  So, MACs use either:
    LPD encoding: supports LPD only
    EPD encoding: supports LPD and EPD; differentiates EPD and LPD frames.

## Slide 8: Problematic aspects of IEEE 802.11
  “There are two LLC sublayer protocols used (see IEEE Std 802); LLC Protocol Discrimination (LPD) (see ISO/IEC 8802-2:1998) and EtherType Protocol Discrimination (EPD) (see IEEE Std 802.3-2012).”
    But IEEE Std 802.3 does not refer to EPD or LPD.
    Minor issue
  “As specified in IEEE Std 802, EPD encoding always starts with a Length/Type field that is either a 2-octet length or a 2-octet Ethertype while LPD encoding always starts with an LSAP octet. There is no indication in a Data frame as to whether EPD or LPD MSDU encoding is in use.”
    IEEE Std 802 doesn’t say that Length/Type encoding is EPD; it says that Ethernet uses Length/Type coding to support both EPD and LPD.
    Major issue, reflected throughout IEEE Std 802.11.

## Slide 9: Rough Terminology Map

## Slide 10: Possible Ways Forward
  Fix apparent errors, as noted above.
  Change IEEE Std 802.11 to refer to “Type/Length encoding” instead of “EPD encoding”; or
  Clarify in IEEE Std 802.11 that “EPD encoding” includes EPD and LDP; or
  Do nothing to address inconsistency; or
  Amend IEEE Std 802 to change definitions of EPD and LDP; or
  Other.