## Slide 1: [MLLE MAC addresses]
Date: 2019-01-15
Authors:

## Slide 2: Recap: MLLE AP with multiple MAC addresses
Legacy STA1
Legacy STA2
MLLE AP
M1
M2
L1
L2
MAC-SAP
MLLESTA
Full flexibility:
MLLE STA can use one, more, or all of the MLLE AP links
Each link could operate as an independent BSSs
  Legacy STAs may be able to connect to either link of the MLLE AP
MAC-SAP address could be one of the link addresses or a separate one (with some usage constrains).
MAC-SAP address was proposed to facilitate MLLE SA setup.
Cons:
Internal MAC address translation M1/M2 <-> MAC-SAP
Retransmitting a frame on a different link may not be possible, depending on the number of MLLE STA MAC addresses

## Slide 3: When the number of MAC addresses on MLLE-AP and MLLE STA do not match
Problem: the same Nonce value will be reused to encrypt different data (a security flaw) if all of the following are true:
  The A2 of two different links are the same (allowed by the MLA architecture)
  A frame is retransmitted on another link using the same A2 and same PN (PN remains the same across retransmissions to avoid out-of-order PN received after SN re-ordering)
  The A1 of two different links are different (allowed by the MLA architecture) <- different AAD data gets re-encrypted using the same Nonce

## Slide 4: Recap: retransmission issue
Legacy STA1
Legacy STA2
MLLE AP
M1
M2
L1
L2
MAC-SAP
If:
M1≠M2 and m1≠m2, or
M1=M2 and m1=m2,
then frames can be retransmitted on either link
However, M1=M2 may introduce backward compatibility issues in existing STA population (alter passive scanning alg).
If:
m1=m2, but M1≠M2, then retransmission on a different link is only possible if the CCMP encryption is modified
Designing a solution which requires m1≠m2 is way too limiting.
A solution which requires modification to the encryption engine is cumbersome: the AP will need to support both the current and the newly defined CCMP encryption.
Is there a solution which does not require m1≠m2 or modification to encryption engine for retransmission, and does not break backward compatibility?
MLLE STA
m1
m2
mac-sap

## Slide 5: MLLE AP with only one MAC address
Legacy STA1
Legacy STA2
MLLE AP
M
M
L1
L2
MAC-SAP
MLLESTA
- If MLLE AP has only one MAC, then only one of the links should be usable by legacy STAs, to avoid backward compatibility issues
- MLLE STA can still use one, more, or all of the MLLE AP links
- Cons: L2 may become unused, if only legacy STAs are associated with the AP
STA MAC addresses:
- Only one MAC address for the MLLE STA

## Slide 6: Hybrid MLLE AP addressing
Legacy STA1
Legacy STA2
MLLE AP
M
M1
M
M2
L1
L2
MAC-SAP
MLLESTA
M
L3
Links enabled for both MLLE and legacy operation have two MAC addresses:
- M: single Multi-Link MAC address towards MLLE-STA (use EHT PPDU)
M1, M2 for communication with legacy STAs
Only links which operate both MLLE and legacy mode would need to have 2 MACs
MAC-SAP of MLLE AP:
M when communicating with MLLE STAs
No need for one when communicating with Legacy STAs
MLLE STA:
Only one MAC address
It can still have multiple MAC addresses when operating as a legacy STA with multiple independent radios
Benefits:
No retransmission issues introduced
MAC-SAP usage comes with no constrains/limitations
Full flexibility retained
No internal MAC address translation needed
Cons: ?

## Slide 7: Beacons in Hybrid MLLE AP addressing
Legacy STA1
Legacy STA2
MLLE AP
M
M1
M
M2
L1
L2
MAC-SAP
MLLESTA
M
L3
L1 and L2 transmits regular beacon with “MLLE IE”
L3 may transmit an “MLLE beacon”, which is not recognized as a beacon by legacy STAs
  MLLE Beacon content tbd

## Slide 8: Keys in Hybrid MLLE AP addressing
Legacy STA1
Legacy STA2
MLLE AP
M
M1
M
M2
L1
L2
MAC-SAP
MLLESTA
M
L3
Quasi agreement in the last f2f:
GTK/IGTK unique per link
BIGTK unique per link (if there is beacon)
Group addressed frames to be sent from M1/M2 on L1/L2 or M on L3 addresses
MLLE STA to receive frames with both M and M1 on L1 or M and M2 on L2.