## Slide 1: Considerations on EHT-SIG Compression Modes
Date: 2020-03-14
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 

## Slide 2: Background
Two EHT-SIG compression modes have been proposed in [1]
  Compression mode 1: Used for Full BW SU or Full BW MU-MIMO; RU allocation info in the common field is omitted
  Compression mode 2: Used for Punctured SU or Punctured MU-MIMO; RU allocation info in the common field is replaced by a punctured channel info
This contribution addresses use cases of two EHT-SIG compression modes and the corresponding compression mode signaling.

## Slide 3: Observations on Compression Mode 1
It is desirable to increase use cases for compression mode 1 since compression mode 1 results in more EHT-SIG overhead reduction than compression mode 2.
  In addition to full BW SU or MU-MIMO, compression mode 1 can be enabled for punctured SU or MU-MIMO if
  U-SIG comprises punctured channel info; and
  punctured channel info in U-SIG is able to indicate channel puncturing pattern that is applied to EHT PPDU.

## Slide 4: Proposed Compression Modes
Compression mode 1:
      Use case 1: full BW SU or full BW MU-MIMO
      Use case 2: punctured SU or MU-MIMO when punctured channel info in U-SIG is able to indicate channel puncturing pattern that is applied to EHT PPDU.
      RU allocation info in the common field is omitted.
Compression mode 2:
      Use case: punctured SU or MU-MIMO transmission when punctured channel info in U-SIG is not able to indicate channel puncturing pattern that is applied to EHT PPDU.
      RU allocation info in the common field is replaced by a supplemental punctured channel info.
      For this compression mode, punctured channel info in U-SIG and supplemental punctured channel info in EHT-SIG joint indicate channel puncturing pattern that is applied to EHT PPDU

## Slide 5
Example
U-SIG comprises a 4-bit Punctured Channel Info field
    Three LSBs indicates whether each 20MHz subchannel within primary 80MHz which is not primary 20MHz is punctured
    The MSB indicates whether at least one 20MHz subchannel outside primary 80MHz is punctured when the BW of EHT PPDU is larger than 80 MHz
Use cases of compression modes
  Compression mode 1:
        Use case 1: full BW SU or full BW MU-MIMO
        Use case 2.1: Punctured SU or MU-MIMO when BW = 80 MHz
        Use case 2.2: Punctured SU or MU-MIMO when BW > 80 MHz and no 20MHz subchannel outside primary 80MHz is punctured.
  Compression mode 2:
        Use case: Punctured SU or MU-MIMO transmission when BW > 80 MHz and at least one 20MHz subchannel outside primary 80MHz is punctured.

## Slide 6
Example (cont.)
EHT-SIG Compression field value | Punctured Channel Info field value | BW field value | Meaning
0 | Any | Any | No compression
1 | All 0 | Any | Compression mode 1 (use case 1)
 | At least one of 3 LSBs is set to 1 and MSB is set to 0 | Indicate BW = 80MHz | Compression mode 1 (use case 2.1)
 |  | Indicate BW> 80MHz | Compression mode 1 (use case 2.2)
1 | MSB is set to 1 | Indicate BW > 80 MHz | Compression mode 2
U-SIG | Field names | Field size (bits)
U-SIG1 | PHY version identifier | 3
 | UL/DL flag | 1
 | BSS color | 6
 | TXOP duration | 7
 | BW | 3
 | Reserved | 2
 | PPDU type | 2
 | EHT-SIG Compression | 1
 | EHT-SIG DCM | 1
U-SIG2 | EHT-SIG EHT MCS | 3
 | Number Of EHT-SIG Symbols Or Non-OFDMA Users | 5
 | Spatial reuse | 4
 | Punctured Channel Info | 4
 | CRC | 4
 | Tail | 6
 | Total | 52
Compression mode signaling

## Slide 7
Example (cont.)
The common field of EHT-SIG may comprise a N-bit Supplemental Punctured Channel Info field.
  Like RU Allocation field, Supplemental Punctured Channel Info field is specific to EHT-SIG content channel in which it is included.
    N = 2 when BW = 160MHz or 80+80MHz
    N = 4 when BW = 240MHz or 160+80MHz
    N = 6 when BW = 320MHz or 160+160MHz
  Each bit indicates whether a corresponding 20MHz subchannel outside primary 80MHz is punctured.

## Slide 8: Summary
In addition to full BW SU or full BW MU-MIMO, we proposed to enable EHT-SIG compression mode 1 for punctured SU or MU-MIMO when punctured channel info in U-SIG is able to indicate channel puncturing pattern that is applied to EHT PPDU.

## Slide 9: Reference
IEEE 802.11-20/0049r2, PPDU Types and U-SIG Content, January 2020

## Slide 10: SP #1
Do you agree that in an EHT PPDU used for punctured SU or MU-MIMO transmission, U-SIG comprises punctured channel info and EHT-SIG may comprise supplemental punctured channel info?

## Slide 11: SP #2
Do you agree that in an EHT PPDU used for punctured SU or MU-MIMO transmission, EHT-SIG does not comprise supplemental punctured channel info if punctured channel info in U-SIG is able to indicate channel puncturing pattern that is applied to the EHT PPDU?

## Slide 12: SP #3
Do you agree that in an EHT PPDU used for punctured SU or MU-MIMO transmission, supplemental punctured channel info, if present in EHT-SIG, is specific to EHT-SIG content channel in which it is carried?