## Slide 1: Link Enablement Considerations
Date: 2020-03-08
Authors:

## Slide 2: Re-cap of Link Enablement
Passed motions
  For each of the enabled links, frame exchanges are possible when the corresponding non-AP STA of the enabled link is in the awake state.
    NOTE-A link is enabled when that link can be used to exchange frames subject to STA power states.
    NOTE-When a link is disabled (i.e. not enabled) by an MLD the frame exchanges are not possible.
  A link, that is setup as part of a multi-link setup, is defined as Enabled if that link can be used for frame exchange and at least one TID is mapped to that link
    Note: frame exchange on a link is subject to the power state of the corresponding non-AP STA
Status of a link can switch from enable to disable and vice versa through TID-mapping update

## Slide 3: Link from Disable back to Enable
In a disable state, hardware, including RF radio, digital circuits, MCU, and memories of the link may be in various conditions
  Different levels of power save
  Use for other connectivity purposes, such as Bluetooth and sensing
How much time required to bring back the link to enable is very different
  Hardware of each link being highly integrated or being from separate modules (chipsets) results in different requirements
  Highly implementation specific and dependent of resource allocation design of the non-AP STA
Link configuration can be updated after being enabled again, such as operational mode change

## Slide 4: Different Levels of Power Save
Disable link’s hardware could be in different levels of power save
Time required to back to active ranges from several nano seconds to tens of TXOP
  “active” here means being able to exchange frames
Mode | Actions | Time required to back active
Idle | Partial digital circuits are clock gated | several clock ticks
Light Sleep | Baseband and partial RF are OFF | 100us ~ 300us
Deep Sleep | Partial system is OFF, including memories and CPUs | 5ms ~ 30ms
Shutdown | All RF, analog, and digital circuits are OFF | > 100 ms

## Slide 5: 11ba Wake-up Operation
Transition Delay in the capability element
  Indicates the maximum time that the non-AP STA requires to transition from the doze state to the awake state
If the WUR AP schedules a transmission that is not a WUR PPDU to the WUR non-AP STA, the WUR AP shall verify that either of the conditions below is met:
  The transition delay indicated by the WUR non-AP STA in the WUR Capabilities elements following the most recent transmitted WUR Wake-up frame intended to the WUR non-AP STA has expired.
  The WUR non-AP STA has indicated that it is in the awake state (see 11.2.1 (General)) by transmitting a frame to the WUR AP.
11be MLO link transition delay is more dynamic

## Slide 6: A Scenario
MLD AP has urgent DL data to a 2-link MLD STA whose one link is disable.
AP sends a TID-mapping update to request enabling the disable ink to the STA and the STA responds with confirmation the disable link will be enabled
  However, STA needs 100ms to resume the link because link’s hardware is totally shutdown
Consider cases the STA can respond
  The response frame to confirm the request only
  The response frame to confirm the request with 100ms transition delay to AP (preferred)

## Slide 7: Summary
In addition to responding to the TID-mapping update to enable a link, the response frame should be able to carry information of the link to be enabled from disable state
  Operational parameters of the link, E.g.,
    Transition delay: Indicates the maximum time that the link requires to transition from disable to enable
    power management mode and power state if they will be different from default settings
    Operation mode update

## Slide 8: Straw Poll 1
Do you agree that the response frame corresponds to the link TID-mapping update should be able to carry operational parameters of the link to be enabled?

## Slide 9: Straw Poll 2
Do you agree that the response frame corresponds to the link TID-mapping update should be able to carry transition delay of the link to be enabled?
  Transition delay indicates the maximum time that the link requires to transition from disable to enable