## Slide 1: SU PPDU SIG Contents Considerations
Date: 2020-03-05
Authors:

## Slide 2: Introduction
IEEE 802.11be adopted U-SIG where it can serves multiple generations of IEEE 802.11
U-SIG contains version-independent bits as well as version-dependent bits
Followings are agreed to be included in U-SIG
  PHY version identifier: 3 bits
  UL/DL flag: 1 bit
  BSS color: TBD bits
  TXOP duration: TBD bits
  Bandwidth: TBD bits. This field may also convey some puncturing information
  PPDU Type
  EHT-SIG MCS (for multiple users)
  Number of EHT-SIG Symbols (for multiple users)
In this contribution, we discussed what will be contents of SIG (U-SIG and EHT-SIG) for SU

## Slide 3: Bandwidth Field (1/2)
Bandwidth field conveys PPDU BW as well as (some) preamble puncturing information
If not all preamble puncturing information is carried in Bandwidth field, then remaining information shall be included in (common field of) EHT-SIG
So far, we have 36 BW+puncturing options (including agreed preamble puncturing patterns in Jan. 2020)
  20/40/80/160 or 80+80/240 or 160+80/320 or 160+160 MHz: 6 non-punctured mode
  Aggregated BW: 60MHz: 3 options, 120MHz: 3 options, 140MHz: 7 options, 160MHz: 2 options, 200MHz: 5 options, 240MHz: 3 options, 280MHz: 7 options
  Note1: Excluding primary channel puncturing
  Note2: Other puncturing patterns (e.g. aggregated BW=40MHz) are TBD

## Slide 4: Bandwidth Field (2/2)
Option1: U-SIG informs PPDU BW and all puncturing pattern
  6 bits BW field in U-SIG to inform 36 options (or 40 options to inform exact puncturing pattern without knowing primary channel, see appendix)
Option2: U-SIG informs PPDU BW and telling whether it is punctured PPDU or not and whether the secondary 20MHz is punctured or not (same as 11ax)
  4 bit BW field in U-SIG informs 12 candidates (see appendix)
  EHT-SIG to inform detail information (maximum 10 options)
Option3: U-SIG informs PPDU BW and puncturing pattern in primary 80MHz
  5 bit BW field in U-SIG informs 21 candidates (see appendix)
  EHT-SIG to inform detail information (maximum 6 options)
In option 1 and option 3, receiver knows exactly how to combine EHT-SIG (if 11be adopts repeated structure, e.g. [1 2 1 2]) which may enable higher EHT-SIG MCS level

## Slide 5: PPDU Type Field (1/2)
What kinds of PPDU type to support in 11be?
  TB, SU, MU, and potentially ER-SU
Don’t need a separate PPDU Type code for ER-SU in U-SIG
  Can be distinguished by similar mechanism as in 11ax
  Supporting ER-SU is TBD
If we need other PPDU type(s) for release 2, then we would like to discuss it and decide size of PPDU Type in release 1 to prevent over-designing

## Slide 6: PPDU Type Field (2/2)
In uplink transmission, we can have 1 bit PPDU Type Field to distinguish TB from SU
  UL/DL=1, PPDU Type = 0: SU
  UL/DL=1, PPDU Type = 1: TB
In downlink transmission, we can have 1 bit PPDU Type Field to distinguish compressed EHT-SIG from non-compressed EHT-SIG
  According to analysis in appendix, U-SIG is not enough to carry all information even for SU PPDU
  In this case, it is natural to support a single format for EHT SU PPDU and EHT MU PPDU as pointed out in [1]
  UL/DL=0, PPDU Type = 0: Compressed (SU PPDU and full bandwidth MU PPDU)
  UL/DL=0, PPDU Type = 1: Non-compressed

## Slide 7: Compressed Mode
In 11ax, there is no Common field in compressed mode
In BW field option 1, Common field is not needed in EHT as well
In BW field option 2 or 3, we need a Common field to further inform puncturing information
Note that in case of BW field option 1, it may be possible to have a single symbol EHT-SIG
In any BW field options, it seems very difficult to put 4 bit Spatial Reuse field in U-SIG (See appendix for an example)
  We may consider to limit SR operation in TB PPDU or under coordinated SR only where there is a control frame before SR

## Slide 8: Example of EHT-SIG User Specific Field Contents: SU Case
Field | Number of Bits | Note
[Partial] STA-ID | [6] | Partial/Hash version of STA-ID
NSTS | [2] | Together with Number of HE-LTF Symbols And Midamble Periodicity+Doppler 2 bits to inform exact NSTS
Beamformed | [1] | 
Beam Change | [1] | 
EHT-MCS | [5] | Including 4K QAM, [DCM], [more MCS level]
Coding | [1] | 
CRC + Tail | 10 | 
Indicated by “Number Of HE-SIG-B Symbols Or MU-MIMO Users = 0”
STA-ID related information is to help non-STR STA operation
  To resume back-off in other link in receive/CCA mode
  Not to send (by STR STA) to whom already sends data in other link
  See reference [2]. Copied some slides in appendix

## Slide 9: Summary
We presented three options for BW field in U-SIG
  Option1: U-SIG informs PPDU BW and all puncturing pattern
  Option2: U-SIG informs PPDU BW and telling whether it is punctured PPDU or not and whether the secondary 20MHz is punctured or not (same as 11ax)
  Option3: U-SIG informs PPDU BW and puncturing pattern in primary 80MHz
We proposed one bit PPDU Type
  UL/DL=1, PPDU Type = 0: TB
  UL/DL=1, PPDU Type = 1: SU
  UL/DL=0, PPDU Type = 0: Compressed
  UL/DL=0, PPDU Type = 1: Non-compressed
We proposed to include STA-ID related information in EHT-SIG even for SU PPDU

## Slide 10: Straw Poll #1
Do you support that U-SIG in each 80MHz shall carry puncturing channel info for at-least the specific 80MHz where it is transmitted?
  Note1: Each STA needs to decode U-SIG in only one 80MHz segment
  Note2: Within each 80MHz segment, U-SIG is duplicated in every non-punctured 20MHz
  BW/Puncturing info can be different for different 80MHz
  TBD: separate BW and puncturing info bits in U-SIG

## Slide 11: Straw Poll #2
Do you agree to have STA-ID related information for SU PPDU in EHT-SIG?

## Slide 12: Reference
[1] 11-20/0049r1, “PPDU Types and U-SIG Content”
[2] 11-19/1405r7, “Multi-link Channel Access Discussion”

## Slide 13: Appendix: BW field option
Option1: U-SIG informs PPDU BW and all puncturing pattern
  Assigning one pattern as one option
    e.g. 0: 20MHz, 1: 40MHz, 2: 80MHz, 3: 160/80+80MHz, 4: 240/160+80MHz, 5: 320/160+160MHz, 6: Agg 60MHz [x 1 1 1], 7: Agg 60MHz [1 x 1 1], 8: Agg 60MHz [1 1 x 1], 9: Agg 60MHz [1 1 1 x]
    1 or x represents each 20MHz channel and 1 means non-punctured, x means punctured
  By allocating current 80MHz pattern as a first pattern, 3rd party STA can understand puncturing pattern at least for 80MHz
    e.g. Actual pattern: [1 1 1 1 x 1 1 1]
      In lower 80MHz channel, BW field in U-SIG indicates [1 1 1 1 x 1 1 1]
      In upper 80MHz channel, BW field in U-SIG indicates [x 1 1 1 1 1 1 1]
    Intended receiver already knows BSS BW channel construction
  Total 40 cases excepts puncturing first 80MHz
    0: 20MHz, 1: 40MHz, 2: 80MHz, 3: 160/80+80MHz, 4: 240/160+80MHz , 5: 320/160+160MHz,
    6: Agg 60MHz [x 1 1 1], 7: Agg 60MHz [1 x 1 1], 8: Agg 60MHz [1 1 x 1], 9: Agg 60MHz [1 1 1 x],
    10: Agg 120MHz [x x 1 1 1 1 1 1], 11: Agg 120MHz [1 1 x x 1 1 1 1], 12: Agg 120MHz [1 1 1 1 x x 1 1], 13: Agg 120MHz [1 1 1 1 1 1 x x],
    14: Agg 140MHz [x 1 1 1 1 1 1 1], 15: Agg 140MHz [1 x 1 1 1 1 1 1], 16: Agg 140MHz [1 1 x 1 1 1 1 1], 17: Agg 140MHz [1 1 1 x 1 1 1 1], 18: Agg 140MHz [1 1 1 1 x 1 1 1], 19: Agg 140MHz [1 1 1 1 1 x 1 1], 20: Agg 140MHz [1 1 1 1 1 1 x 1], 21: Agg 140MHz [1 1 1 1 1 1 1 x],
    22: Agg 160MHz [1 1 1 1 x x x x 1 1 1 1], 23: Agg 160MHz [1 1 1 1 1 1 1 1 x x x x],
    24: Agg 200MHz [x x 1 1 1 1 1 1 1 1 1 1], 25: Agg 200MHz [1 1 x x 1 1 1 1 1 1 1 1], 26: Agg 200MHz [1 1 1 1 x x 1 1 1 1 1 1], 27: Agg 200MHz [1 1 1 1 1 1 x x 1 1 1 1], 28: Agg 200MHz [1 1 1 1 1 1 1 1 x x 1 1], 29: Agg 200MHz [1 1 1 1 1 1 1 1 1 1 x x],
    30: Agg 240MHz [1 1 1 1 x x x x 1 1 1 1 1 1 1 1], 31: Agg 240MHz [1 1 1 1 1 1 1 1 x x x x 1 1 1 1], 32: Agg 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x x x],
    33: Agg 280MHz [x x 1 1 1 1 1 1 1 1 1 1 1 1 1 1], 34: Agg 280MHz [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1], 35: Agg 280MHz [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1], 36: Agg 280MHz [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1], 37: Agg 280MHz [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1], 38: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1], 39: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1], 40: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x]

## Slide 14: Appendix: BW field option
Option2: 4 bits BW field in U-SIG and max 4 bits puncturing pattern in EHT-SIG
  Similar to 11ax
  Primary 20MHz channel in first 20MHz, 1 means non-punctured, x means punctured, ? means don’t know at this moment
  4 bit BW field in U-SIG informs following 12 candidates
    20/40/80/160 or 80+80/240 or 160+80/320 or 160+160 MHz: 6 non-punctured mode
    BW 80MHz: 2 options [1 x 1 1] [1 1 ? ?]
    BW 160MHz: 2 options [1 x 1 1 1 1 1 1] [1 1 ? ? ? ? ? ?]
    BW 240MHz: 1 options [1 1 ? ? ? ? ? ? ? ? ? ?]
    BW 320MHz: 1 options [1 1 ? ? ? ? ? ? ? ? ? ? ? ? ? ?]
  EHT-SIG to inform following cases
    BW 80MHz: 2 options [1 1 1 x] [1 1 x 1]
    BW 160MHz: 9 options [1 1 x x 1 1 1 1] [1 1 1 1 x x 1 1] [1 1 1 1 1 1 x x] [1 1 x 1 1 1 1 1] [1 1 1 x 1 1 1 1] [1 1 1 1 x 1 1 1] [1 1 1 1 1 x 1 1] [1 1 1 1 1 1 x 1] [1 1 1 1 1 1 1 x]
    BW 240MHz: 7 options [1 1 1 1 x x x x 1 1 1 1] [1 1 1 1 1 1 1 1 x x x x] [1 1 x x 1 1 1 1 1 1 1 1] [1 1 1 1 x x 1 1 1 1 1 1] [1 1 1 1 1 1 x x 1 1 1 1] [1 1 1 1 1 1 1 1 x x 1 1] [1 1 1 1 1 1 1 1 1 1 x x]
    BW 320MHz: 10 options [1 1 1 1 x x x x 1 1 1 1 1 1 1 1] [1 1 1 1 1 1 1 1 x x x x 1 1 1 1] [1 1 1 1 1 1 1 1 1 1 1 1 x x x x] [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1] [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1] [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1] [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1] [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1] [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1] [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x]

## Slide 15: Appendix: BW field option
Option3: 5 bits BW field in U-SIG and max 3 bits puncturing pattern in EHT-SIG
  Primary 20MHz channel in first 20MHz, 1 means non-punctured, x means punctured, ? means don’t know at this moment
  5 bit BW field in U-SIG informs following 21 candidates
    20/40/80/160 or 80+80/240 or 160+80/320 or 160+160 MHz: 6 non-punctured mode
    Aggregated BW 60MHz: 3 options [1 1 1 x] [1 1 x 1] [1 x 1 1]
    Aggregated BW 120MHz: 2 options [1 1 1 1 ? ? ? ?] [1 1 x x 1 1 1 1]
    Aggregated BW 140MHz: 4 options [1 1 1 1 ? ? ? ?] [1 1 1 x 1 1 1 1] [1 1 x 1 1 1 1 1] [1 x 1 1 1 1 1 1]
    Aggregated BW 160MHz: 1 options [1 1 1 1 ? ? ? ? ? ? ? ?]
    Aggregated BW 200MHz: 2 options [1 1 1 1 ? ? ? ? ? ? ? ?] [1 1 x x 1 1 1 1 1 1 1 1]
    Aggregated BW 240MHz: 1 options [1 1 1 1 ? ? ? ? ? ? ? ? ? ? ? ?]
    Aggregated BW 280MHz: 2 options [1 1 1 1 ? ? ? ? ? ? ? ? ? ? ? ?] [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1]
  EHT-SIG to inform following cases for greater than 80MHz PPDU
    Aggregated BW 120MHz: 2 options [1 1 1 1 1 1 x x] [1 1 1 1 x x 1 1]
    Aggregated BW 140MHz: 4 options [1 1 1 1 1 1 1 x] [1 1 1 1 1 1 x 1] [1 1 1 1 1 x 1 1] [1 1 1 1 x 1 1 1]
    Aggregated BW 160MHz: 2 options [1 1 1 1 1 1 1 1 x x x x] [1 1 1 1 x x x x 1 1 1 1]
    Aggregated BW 200MHz: 4 options [1 1 1 1 1 1 1 1 1 1 x x] [1 1 1 1 1 1 1 1 x x 1 1] [1 1 1 1 1 1 x x 1 1 1 1] [1 1 1 1 x x 1 1 1 1 1 1]
    Aggregated BW 240MHz: 3 options [1 1 1 1 1 1 1 1 1 1 1 1 x x x x] [1 1 1 1 1 1 1 1 x x x x 1 1 1 1] [1 1 1 1 x x x x 1 1 1 1 1 1 1 1]
    Aggregated BW 280MHz: 6 options [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x] [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1] [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1] [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1] [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1] [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1]

## Slide 16: Appendix: U-SIG is enough for SU PPDU?
Following information is information for SU PPDU
  PHY version identifier: 3 bits
  UL/DL flag: 1 bit
  BSS color: [6] bits
  TXOP duration: [7] bits
  Bandwidth: [6] bits. This is only option without EHT-SIG.
  CRC and Tail: [10] bits  Version independent bits + CRC and Tail: Until here is 33 bits
  PPDU Type: [2] (DL MU PPDU compressed mode, DL MU PPDU non-compressed mode and DL SU PPDU)
  MCS: [5] bits, 4K QAM, [DCM], [more MCS level]
  GI+EHT-LTF Size: [2] bits
  NSTS And Midamble Periodicity+Doppler: 5 bits- to support 16 stream
  LDPC Extra Symbol Segment: [1] bit
  Pre-FEC Padding Factor: [2] bits
  PE Disambiguity: [1] bit
  Beamformed: [1] bit
  Coding: 1 bit  Until here is 53 bits  Overflowed
  [STBC: [1] bit]
  [Beam Change: 1 bit]
  [Spatial Reuse: 4 bits]

## Slide 17: Appendix: SIG Contents for SU and MU
HE SU SIG-A | HE MU SIG-A | HE MU user field | Example EHT SU/MU
Format (1) |  |  | PPDU Type [1]: U-SIG Version Dependent
Beam Change (1) |  |  | Beam Change [1]: EHT user field (Only for SU)
UL/DL (1) | UL/DL (1) |  | UL/DL (1): U-SIG Version Independent
HE-MCS (4) |  | HE-MCS (4) | EHT-MCS [5]: EHT user field
DCM (1) |  | DCM (1) | Maybe merged with EHT-MCS
BSS Color (6) | BSS Color (6) |  | BSS Color [6]: U-SIG Version Independent
Spatial Reuse (4) | Spatial Reuse (4) |  | TBD
Bandwidth (2) | Bandwidth (3) |  | Bandwidth [6]: U-SIG Version Independent
GI+HE-LTF Size (2) | GI+HE-LTF Size (2) |  | GI+HE-LTF Size [2]: U-SIG Version Dependent
NSTS And Midamble Periodicity (3) | Number of HE-LTF Symbols And Midamble Periodicity (3) |  | Number of HE-LTF Symbols And Midamble Periodicity+Doppler [4]: U-SIG Version Dependent
TXOP (7) | TXOP (7) |  | TXOP [7]: U-SIG Version Independent
Coding (1) |  | Coding (1) | Coding [1]: EHT user field
LDPC Extra Symbol Segment (1) | LDPC Extra Symbol Segment (1) |  | LDPC Extra Symbol Segment [1]: U-SIG Version Dependent

## Slide 18: Appendix: SIG Contents for SU and MU
HE SU SIG-A | HE MU SIG-A | HE MU user field | Example EHT SU/MU
STBC (1) | STBC (1) |  | STBC [1]: U-SIG Version Dependent
Beamformed (1) |  | Beamformed (1) | Beamformed [1]: EHT user field
Pre-FEC Padding Factor (2) | Pre-FEC Padding Factor (2) |  | Pre-FEC Padding Factor [2]: U-SIG Version Dependent
PE Disambiguity (1) | PE Disambiguity (1) |  | PE Disambiguity [1]: U-SIG Version Dependent
Doppler (1) | Doppler (1) |  | Maybe merged with Number of HE-LTF Symbols or NSTS And Midamble Periodicity+Doppler
 | HE-SIG-B-MCS (3) |  | EHT-SIG MCS+DCM [3]: U-SIG Version Dependent
 | Number Of HE-SIG-B Symbols Or MU-MIMO Users (4) |  | Number Of HE-SIG-B Symbols Or MU-MIMO Users [4]: U-SIG Version Dependent
 | HE-SIG-B Compression (1) |  | PPDU Type [1]: U-SIG Version Dependent
 |  | STA-ID (11) | STA-ID [11]: EHT user field
 |  | NSTS (3) or Spatial Configuration (4) | NSTS [4] or Spatial Configuration [TBD]: EHT user field

## Slide 19: Appendix: Example of EHT SU/MU U-SIG Contents
Field | Number of Bits | Note
PHY version identifier | 3 | 
UL/DL flag | 1 | 
BSS color | [6] | 
TXOP duration | [7] | 
Bandwidth | [4-6] | See option 1
PPDU Type | [1] | See slide 6
GI+HE-LTF Size | [2] | 
Number of HE-LTF Symbols And Midamble Periodicity+Doppler | [4] | 1/2/4/6/8/12/16 1/2/4 with Midamble two options (11ax)
EHT-SIG MCS+DCM | [3] | 
Number Of HE-SIG-B Symbols Or MU-MIMO Users | [4] | 
LDPC Extra Symbol Segment | [1] | 
Pre-FEC Padding Factor | [2] | 
PE Disambiguity | [1] | 
STBC | [1] | 
TBD | [2-0] | 
CRC | 4 | 
Tail | 6 | 

## Slide 20: Opportunistic Backoff Countdown Resume at non-STR STA
For certain conditions, non-STR STA resumes countdown on link B during busy state on link A
Similar to 802.11ax SRP-based spatial reuse backoff procedure
Inter-BSS PPDU (e.g. BSS Color)
  Backoff countdown can be resumed as frame not for non-STR STA
Intra-BSS Uplink PPDU
  Backoff countdown can be resumed, similar to above
  UL/DL bit in HE-SIG-A for HE SU PPDU/ER SU PPDU
  UL MU identified by HE TB PPDU
Intra-BSS Downlink PPDU
  Backoff countdown can be resumed if PPDU identified to be not destined to itself
  STA ID in HE-SIG-B for HE MU PPDU or unable to decode HE-SIG-B of HE MU PPDU
  No STA ID info in PHY preamble for SU PPDU and MAC header decoding can take long
  Proposal: STA ID info in EHT PHY preamble for SU PPDU
From IEEE 802.11-19/1450r7

## Slide 21: Non-STR STA indication in Uplink
Preventing AP from transmitting to any non-STR STA while receiving any intra-BSS PPDU may be too conservative
Trigger-based PPDU
  AP knows which non-STR STAs are transmitting (except random RUs)
SU PPDU
  STA ID info in EHT PHY preamble
  If STA ID info indicates a non-STR STA, AP can still transmit to other non-STR STAs
From IEEE 802.11-19/1450r7

## Slide 22: Straw Poll #1
Which BW field option do you support?
  Option1: U-SIG informs PPDU BW and all puncturing pattern
    6 bits in U-SIG
  Option2: U-SIG informs PPDU BW and telling whether it is punctured PPDU or not and whether secondary 20MHz is punctured (same as 11ax) or not
    4 bits in U-SIG, 4 bits in Common field of EHT-SIG
  Option3: U-SIG informs PPDU BW and puncturing pattern in primary 80MHz
    5 bits in U-SIG, 3 bits in Common field of EHT-SIG

## Slide 23: Straw Poll #3
Do you agree to have one bit “PPDU type” as a version dependent field in U-SIG?