## Slide 1: MLO: BSS Color
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Overview
Past contributions [1, 2, 3] have discussed the benefits of multi-link operation and examined the functionality split between MLD and each STA instance.
Contributions [4, 5] clarify that each AP affiliated with an AP MLD has a different MAC address
This contribution discusses multi-link architecture with the focus on BSS color selection for APs of an AP MLD.
  It further generalizes the concepts to other operational parameters

## Slide 3: BSS Color: Background
11ax introduced the concept of BSS color with the objective of identifying a BSS
  The color information is carried in the preamble of a PPDU and assists a receiving STA quickly identify the BSS from which a PPDU originated
The color helps a STA make decisions on power-save, NAV and whether to perform SR
  These decisions are link specific
Further, an AP selects a color value for its BSS based on local conditions such as the colors already in used by other APs in the neighborhood
  Again this is a link specific decision
11ax provides mechanisms for identifying color collision, selecting a new color and advertising a new color
  Once again, these decisions are specific to the link

## Slide 4: BSS Color for MLA
Should color be per-link or per-MLD?
BSS color is a short representation of a BSSID and a BSSID is per-link, therefore it is natural to have the color selected per-link instead of per-MLD
Further, the purpose of BSS color is to influence decisions that are specific to a link
  Having the color selected per-link would also align with the MLA design philosophy of keeping link specific features within the purview of each STA instance
In conclusion, each AP of an AP MLD independently selects and manage its BSS color

## Slide 5: Generalizing to other operational params
The idea of independently selecting BSS color is applicable to other operation parameters
  For example, each AP can independently select (MU)EDCA, UORA, SRP etc.
As such, the concept is applicable to all operational parameters for a STA (AP or a non-AP) of an MLD
  unless the 11be standard specifically provides rules that require coordination of a certain parameter amongst the STAs of an MLD.

## Slide 6: Summary
We discuss the topic of BSS color selection for APs belonging to an AP MLD and present our reasoning on why the color assignment should be per-link.
  We extend the reasoning and generalize the concept to be applicable to other operational parameters

## Slide 7: SP #1
Do you support that each STA of an MLD may independently select and manage it operational parameters unless specified otherwise in the 11be standard?
  Y:
  N:
  A:

## Slide 8: References
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai, Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek, Qualcomm)
[3]:11-19-0821 multiple band discussion (Liwen, Marvell)
[4]: 11-19-0822 Extremely efficient multi-band operation (Po-Kai, Intel)
[5]: 11-19-1899 MLA MAC addresses considerations (Duncan, Qualcomm)
[6]: 11-19-1262 Specification Framework for TGbe