## Slide 1: Group addressed frame transmission in constrained multi-link operation
Date: 2020-03-16
Authors:

## Slide 2: Recap: Constrained Multi-Link Device (MLD)
A constrained MLD is a MLD with which in-device coexistence (IDC) interference occurs when more than one STA within the MLD simultaneously transmits and receives frames on multiple links.
  When simultaneous Tx and Rx occur on 2.4 GHz band and 5 GHz links, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx on 5 GHz band and 6 GHz band links may be significantly worse depending on some implementation factors such as RF filter performance.

## Slide 3: Motivation
It is necessary that a constrained MLD avoids transmitting and receiving frames on multiple links simultaneously.
This contribution discuss a reliable group addressed frame transmission to a constrained MLD.

## Slide 4: Group addressed frame transmission in constrained multi-link operation
In order to reliably deliver a group addressed frame to the constrained non-AP MLDs, the AP MLD should schedule the group addressed frames when all constrained MLDs are not transmitting.
But, because the non-AP MLDs do not know when the group addressed frames will be transmitted from the AP MLD, they may access the channel without any restriction.
Consequently, scheduling the group addressed frames when all constrained MLDs are not transmitting can be difficult.

## Slide 5: Group addressed frame transmission in constrained multi-link operation
As in the below figure, because the constrained non-AP MLDs are transmitting frames on the link 2, the AP MLD does not transmit the group addressed frames on the link 1.
  Otherwise, the group addressed frame transmission will be failed.
L1 STA in AP MLD
L2 STA in AP MLD
L1 STA in non-AP MLD1
L2 STA in non-AP MLD1
Beacon
BA
L1 STA in non-AP MLD2
L2 STA in non-AP MLD2
A-MPDU (to AP MLD)
Beacon
A-MPDU (to non-AP MLDn)
A-MPDU (to AP MLD)
BA
A-MPDU (to non-AP MLDn)
During this duration, the AP MLD may not transmit the group addressed frames on the link 1.

## Slide 6: Group addressed frame transmission in constrained multi-link operation
The proposed solution is that the AP MLD provides the scheduling information of the group addressed frames to the constrained non-AP MLDs.
And, the constrained non-AP MLD that intends to receive the group addressed frames does not access the channel on all links during the scheduled service period of the group addressed frame.

## Slide 7: Group addressed frame transmission in constrained multi-link operation
As in the below figure, because the constrained non-AP MLD does not access the channel during the scheduled service period of the group addressed frame, the AP MLD can have a chance to more reliably deliver the group addressed frames.
L1 STA in AP MLD
L2 STA in AP MLD
L1 STA in non-AP MLD1
L2 STA in non-AP MLD1
Beacon
BA
L1 STA in non-AP MLD2
L2 STA in non-AP MLD2
A-MPDU (to AP MLD)
Beacon
A-MPDU (to non-AP MLDn)
Group addressed MPDU
Group addressed frame SP
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
During this duration, the AP MLD may not transmit the group addressed frames on the link 1.

## Slide 8: Conclusion
For a reliable group addressed frame transmission to a constrained MLD,
  The constrained non-AP MLDs needs to know the scheduling information of the group addressed frames.
  The constrained non-AP MLDs does not access the channel at the target transmission time of the group addressed frame.
    The same rule should be applied for TBTTs.

## Slide 9: Straw Poll 1
Do you support the following group addressed frames delivery mechanism for the constrained multi-link operation?
  When a non-AP MLD intends to receive the group addressed frames, other STAs in the non-AP MLD that can't simultaneously transmit and receive with the STA in the non-AP MLD which is configured to receive the group addressed frames shall not access a channel for the service period of the group addressed frames that is signaled by the AP MLD.