## Slide 1: Group addressed frame transmission in constrained multi-link operation
Date: 2020-04-06
Authors:

## Slide 2: Recap: Constrained Multi-Link Device (MLD)
A constrained MLD is a MLD with which in-device coexistence (IDC) interference occurs when more than one STA within the MLD simultaneously transmits and receives frames on multiple links.
  When simultaneous Tx and Rx occur on 2.4 GHz band and 5 GHz links, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx on 5 GHz band and 6 GHz band links may be significantly worse depending on some implementation factors such as RF filter performance.

## Slide 3: Motivation
It is necessary that a constrained MLD avoids transmitting and receiving frames on multiple links simultaneously.
This contribution discuss a reliable group addressed frame transmission to a constrained MLD.

## Slide 4: Group addressed frame transmission in constrained multi-link operation
In order to reliably deliver a group addressed frame to a constrained non-AP MLD, an AP MLD should not schedule to the non-AP MLD a frame exchange sequence which overlaps with the group addressed frame of other link(s).
STA1 in Non-AP MLD
DTIM Beacon (Rx)
Group addressed frame (Rx)
STA2 in Non-AP MLD
Block Ack (Tx)
Individually addressed frame (Rx)
Interference leakage from STA2

## Slide 5: Group addressed frame transmission in constrained multi-link operation
If the AP MLD does not know the link(s) on which the non-AP MLD is listening the group addressed frame, the AP MLD should not schedule to the non-AP MLD any frame exchange sequence which overlaps with the group addressed frame of other link(s).
AP1 in AP MLD
AP2 in AP MLD
D
AP3 in AP MLD
D
D
D
D
D
During this time, the AP does not schedule to the non-AP MLD any frame exchange sequence.

## Slide 6: Group addressed frame transmission in constrained multi-link operation
In order to improve an efficiency of the multi-link operation, the non-AP MLD should configure to the AP MLD the link(s) on which it is listening the group addressed frame.
Then, the AP MLD should not schedule to the non-AP MLD a frame exchange sequence which overlaps with the group addressed frame of the configured link(s).

## Slide 7: Group addressed frame transmission in constrained multi-link operation
Also, when a non-AP MLD intends to receive the group addressed frame on the configured link, other STAs in the non-AP MLD, which can't simultaneously transmit and receive with the STA in the non-AP MLD which is configured to receive the group addressed frames, shall not access a channel during the group addressed frame transmission time.

## Slide 8: Group addressed frame transmission in constrained multi-link operation
As in the below figure, the constrained non-AP MLD does not access the channel during the group addressed frame transmission time of the configured link. But, at the group addressed frame transmission time of other links, the non-AP MLD can access the channel.
L1 STA in AP MLD
L2 STA in AP MLD
L1 STA in non-AP MLD1
L2 STA in non-AP MLD1
DTIM beacon
L1 STA in non-AP MLD2
L2 STA in non-AP MLD2
DTIM beacon
Group addressed MPDU
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
Channel access from non-AP MLD is not allowed
BA
A-MPDU (to AP MLD)
Group addressed MPDU

## Slide 9: Conclusion
For a reliable group addressed frame transmission to a constrained MLD,
  The constrained non-AP MLD needs to configure to the AP MLD the link(s) on which it is listening the group addressed frame.
  The AP MLD should not schedule to the non-AP MLD a frame exchange sequence which overlaps with the group addressed frame of the configured link(s).
  The non-AP MLD intends to receive the group addressed frame shall not access a channel during the group addressed frame transmission time on the configured link(s).

## Slide 10: Straw Poll 1
Do you support the following group addressed frames delivery mechanism?
  The non-AP MLD configure a link with the AP MLD to receive group addressed frame.

## Slide 11: Straw Poll 2
Do you support the following group addressed frames delivery mechanism?
  The AP MLD should not schedule to the non-STR MLD a frame exchange sequence which overlaps with the group addressed frame of the configured link(s).
  The non-AP MLD intends to receive the group addressed frame shall not access a channel during the group addressed frame transmission time on the configured link(s).