## Slide 1: MAC Privacy and PMKSA Caching
Date: 2020-02-14
Authors:

## Slide 2: Abstract
CID 2689 requested a means for a STA to use PMKSA caching while it dot11MACPrivacyActivated is true.
The purpose of this presentation is to propose a solution to the comment.
CID | Page | Clause | Duplicate of CID | Resn Status | Comment | Proposed Change
2689 | 294.00 | 4.10.7 |  |  | In PMKSA caching, STA sends one or more PMKIDs in the clear in (Re)Assoc Request frame (or Auth frame in FILS case). In cases where PMK lifetime and caching period are long, the same PMKID might be sent each time a STA connects to the same AP/network, and this could be used by bad actors to track a user's location with privacy implications. | Provide means by which, e.g. during each auth/assoc procedure, the AP can securely provision STA with a randomly-generated pseudonym for the PMKID which the STA uses on the next auth/assoc with that AP

## Slide 3: High Level Solution Description
The model for association is as follows:
  Device associates to a BSS with a random MAC address and generates a SA
  As part of the security association, a PMKID is generated.
  Device disassociates from network
  Device changes MAC address to new random address.
  Device attempts to associate to BSS with cached PMK the PMKID.
  AP recognizes the PMKID and STA establishes a new SA (and generates a new PMKID)
Note that any network state associated with the old MAC address would be lost.

## Slide 4: Requirements
The AP and STA would advertise/negotiate an association with this capability.
A new PMKID will be generated for each subsequent association (to prevent tracking)
  The STA and AP generate a new PMKID (rPMKID) each association
The feature expedites the establishment of a security association – changing the MAC address will affect bridging and higher layer communications.
The solution will work for any AKM.

## Slide 5: Solution
AP advertises support for rPMKSA caching in Extended RSNE
STA associates and signals intention to use rPMKSA caching
A new PMKID will be generated for each subsequent association (to prevent tracking)
  The STA and AP generate a new PMKID (rPMKID) each association
If this feature is supported by both STA and AP, the STA includes the rPMKID in the PMKID List field at Association.
NOTE: The feature expedites the establishment of a security association – changing the MAC address will affect bridging and higher layer communications.

## Slide 6: rPMKID derivation
The rPMKID is derived from the PTK for each association, recall PTK is:
  (NOTE: FT and FILS have different PTK derivations)

## Slide 7: rPMKID Derivation Options
Adopt an approach based on TGaz D2.0 for PASN:
  Option 1. Using IEEE 802.11 KDF
    rPMKID = L(0, 128, HMAC-HASH(HLTK, "rPMKID expansion")
  Option 2. Using IETF RFC 5869
    rPMKID-PRK = HKDF-Extract(current PMKID, HLTK)
    rPMKID = HKDF-Expand(rPMKID-PRK, "rPMKID expansion", 16)

## Slide 8: Next Steps
Produce text submission based on this presentation and feedback received.