## Slide 1: Multi-link BSS Parameter Update
Date: 2020-03-13
Authors:

## Slide 2: Motivation
A non-AP Multi-link Device (MLD) monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s). [1]
A non-AP MLD only needs to follow one configured link among the links setup with the an AP MLD to receive broadcast addressed frame. [2]

## Slide 3: Motivation
Among STAs within a non-AP MLD, some STA may not monitor its associated BSS parameter update.
In such case, if the BSS parameter associated with the STA is updated, it shall be directly announced or noticed through different STA within the non-AP MLD.

## Slide 4: Explicit Multi-link BSS Parameter Update
A STA within a AP MLD may send the updated BSS parameter of another STA within the AP MLD.
  On this purpose, a new Multi-link IE is proposed to encapsulate the information element (IE) related with the BSS parameter of STAs which is different with the STA transmitting this IE.
  As one of usage scenarios, the Extended Channel Switch Announcement (ECSA) is described in the following slides.
Element ID | Length | Element ID Extension | Link ID | Optional Subelements
1 octet | 1 octet | 1 octet | 1 octet | variable
<Multi-link IE>

## Slide 5: Explicit Multi-link BSS Parameter Update
The optional subelements field in the Multi-link IE contains the ECSA IE.
Assuming that a non-AP MLD does not monitor a link whose channel will be switched, the non-AP MLD may be fail to track the TBTT on that link.
  A reference of a channel switch time (refer the Channel Switch Count field) is a target beacon transmission time (TBTT).
In such case, the optional subelements field in the Multi-link IE may contain the beacon interval (BI) and the TSF offset between two links in order to track the TBTT.

## Slide 6: Explicit Multi-link BSS Parameter Update
For example, a non-AP MLD only monitors the link 1 for the BSS parameter update. The STA1 within the AP MLD is providing to the non-AP MLD the ECSA information related with the STA2 within the AP MLD through the Multi-link IE.
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch2
Ch2
Ch2
Ch2
STA1 in AP MLD
(Link 1)
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 3
B
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 1
B
B
B
B
B
B
STA2 in AP MLD
(Link 2)
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 2
B
B
B
B
B
B
B
50ms
50ms
50ms
BI : 100ms
Multi-link IE
Multi-link IE
Multi-link IE
50ms

## Slide 7: Implicit Multi-link BSS Parameter Update
A STA within a AP MLD may send the Change Sequence IE that indicates a change of system information within a BSS associated with another STA within the AP MLD.
  In which case, the optional subelements field in the Multi-link IE contains the Change Sequence IE (see 9.4.2.198 (Change Sequence element)).
  Or, a new Multi-link Change Sequence IE is defined as the following.
Element ID | Length | Element ID Extension | Link ID | Change Sequence
1 octet | 1 octet | 1 octet | 1 octet | 1 octet
<Multi-link Change Sequence IE>

## Slide 8: Implicit Multi-link BSS Parameter Update
The STA within the AP MLD shall increase the value (modulo 256) of the Change Sequence field in the next transmitted Beacon frame(s) when a critical update occurs to any of the elements inside the Beacon frame sent on the link indicated by the Link ID field by another STA within the AP MLD.
  The following events shall classify as a critical update:
    Inclusion of an Extended Channel Switch Announcement
    Inclusion of a BSS Color Change Announcement
    Modification of the EDCA parameters
    Modification of the MU EDCA Parameter Set element
    Modification of the Spatial Reuse Parameter Set element

## Slide 9: Implicit Multi-link BSS Parameter Update
When a STA in a non-AP MLD receives a Change Sequence field that contains a value that is different from the previously received Change Sequence field associated with a STA within an AP MLD, another STA in the non-AP MLD shall either be awake on the link indicated by the Link ID field to receive the next Beacon frame by the STA within the AP MLD or shall queue for transmission a Probe Request frame to the STA within the AP MLD.

## Slide 10: Implicit Multi-link BSS Parameter Update
For example, a non-AP MLD only monitors the link 1 for the BSS parameter update. A STA in the non-AP MLD is awake to receive on the link 2 the next Beacon frame sent by the STA2 within the AP MLD, after receiving the Change Sequence field set to 2 on the link 1 which is different with the previously received Change Sequence field (i.e., 1).
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch2
Ch2
Ch2
Ch2
STA1 in AP MLD
(Link 1)
Link ID: 2
Change Seq: 1
B
Link ID: 2
Change Seq: 2
B
B
B
B
B
B
STA2 in AP MLD
(Link 2)
Link ID: 2
Change Seq: 1
B
B
B
B
B
B
B
Multi-link IE
Multi-link IE
Multi-link IE
Link ID: 2
Change Seq: 2
Multi-link IE
…
Awake
Change Seq: 1
Change Seq: 2
Change Seq: 1
Change Seq: 2
…
STA in non-AP MLD
(Link 2)
Doze

## Slide 11: Conclusion
A non-AP MLD may not monitor and performs basic operations on one or more enabled link(s).
When the BSS parameter of the link on which the a non-AP MLD does not monitor is updated, such update is explicitly or implicitly informed to the non-AP MLD.
  The proposed Multi-link IE may encapsulate the IE related with the updated BSS parameter.
  Also, instead of an explicit signaling of the updated BSS parameter, an AP MLD may just announce a change of system information related with the BSS of other link.
    A non-AP MLD that received such announcement updates the changed BSS parameter on the same link on which the BSS parameter update is occurred.

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1526-03-00be-multi-link-power-save.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-1542-02-00be-multi-link-broadcast-addressed-frame-reception.pptx

## Slide 13: Straw Poll 1
Do you support that an AP within an AP MLD shall send a change sequence that indicates a change of system information of another AP within the same AP MLD when a critical update to the Beacon frame in another AP has occurred, where the change sequence is initialized to 0, that increments as the critical update is occurred?
  The signaling of the change sequence is TBD.
  The critical updates are defined in 11.2.3.15 TIM Broadcast and the additional update can be added if needed.

## Slide 14: Straw Poll 2
Do you support that an AP within a AP MLD may send the updated BSS parameter of another AP within the same AP MLD when a critical update to the Beacon frame in another AP has occurred?