## Slide 1: Multi-link BSS Parameter Update
Date: 2020-06-04
Authors:

## Slide 2: Motivation
A non-AP Multi-link Device (MLD) monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s). [1]
A non-AP MLD only needs to follow one configured link among the links setup with the an AP MLD to receive broadcast addressed frame. [2]

## Slide 3: Motivation
Among STAs within a non-AP MLD, some STA may not monitor its associated BSS parameter update.
In such case, if the BSS parameter associated with the STA is updated,
  It can be explicitly announced through different STA within the non-AP MLD.
  Or, it can be implicitly noticed through different STA within the non-AP MLD and the STA may update the changed BSS parameter on the same link on which the BSS parameter update is occurred.
In this contribution, we focus on the implicit multi-link BSS parameter update mechanism.

## Slide 4: Implicit Multi-link BSS Parameter Update
An AP within an AP MLD includes in the Beacon and Probe Response frames it transmits the Change Sequence IE that indicates a change of system information within a BSS associated with another AP within the same AP MLD.
  In which case, the optional subelements field in the Multi-link IE contains the Change Sequence IE (see 9.4.2.198 (Change Sequence element)).
  Or, a new Multi-link Change Sequence IE is defined as the following.
Element ID | Length | Element ID Extension | Link ID | Change Sequence
1 octet | 1 octet | 1 octet | 1 octet | 1 octet
<Multi-link Change Sequence IE>

## Slide 5: Implicit Multi-link BSS Parameter Update
An AP within an AP MLD shall increase the value (modulo 256) of the Change Sequence field in the next transmitted Beacon frame(s) when a critical update occurs to any of the elements inside the Beacon frame sent on the link indicated by the Link ID field by another AP within the same AP MLD.
  The following events shall classify as a critical update:
    Inclusion of an Extended Channel Switch Announcement
    Inclusion of a BSS Color Change Announcement
    Modification of the EDCA parameters
    Modification of the MU EDCA Parameter Set element
    Modification of the Spatial Reuse Parameter Set element

## Slide 6: Implicit Multi-link BSS Parameter Update
When a STA in a non-AP MLD receives a Change Sequence field that contains a value that is different from the previously received Change Sequence field associated with an AP within an AP MLD, another STA in the same non-AP MLD shall either be awake on the link indicated by the Link ID field to receive the next Beacon frame sent by the AP within the AP MLD or shall queue for transmission a Probe Request frame to the AP within the AP MLD.

## Slide 7: Implicit Multi-link BSS Parameter Update
For example, a non-AP MLD only monitors the link 1 for the BSS parameter update. A STA in the non-AP MLD is awake to receive on the link 2 the next Beacon frame sent by the AP2 within the AP MLD, after receiving the Change Sequence field set to 2 on the link 1 which is different with the previously received Change Sequence field (i.e., 1).
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch2
Ch2
Ch2
Ch2
AP1 in AP MLD
(Link 1)
Link ID: 2
Change Seq: 1
B
Link ID: 2
Change Seq: 2
B
B
B
B
B
B
AP2 in AP MLD
(Link 2)
Link ID: 2
Change Seq: 1
B
B
B
B
B
B
B
Multi-link IE
Multi-link IE
Multi-link IE
Link ID: 2
Change Seq: 2
Multi-link IE
…
Awake
Change Seq: 1
Change Seq: 2
Change Seq: 1
Change Seq: 2
…
STA in non-AP MLD
(Link 2)
Doze

## Slide 8: Conclusion
A non-AP MLD may not monitor and performs basic operations on one or more enabled link(s).
When the BSS parameter of the link on which the a non-AP MLD does not monitor is updated, an AP MLD announces a change of system information related with the BSS of other link.
  A non-AP MLD that received such announcement updates the changed BSS parameter on the same link on which the BSS parameter update is occurred.

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1526-03-00be-multi-link-power-save.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-1542-02-00be-multi-link-broadcast-addressed-frame-reception.pptx

## Slide 10: Straw Poll 1
Do you support that an AP within an AP MLD shall include in the Beacon and Probe Response frames it transmits the Change Sequence fields that indicate changes of system information for other APs within the same AP MLD, where the change sequence field value for the reported AP is initialized to 0, that increments as the critical update of the reported AP is occurred?
  The signaling of the Change Sequence field is TBD.
  The critical updates are defined in 11.2.3.15 TIM Broadcast and the additional update can be added if needed.

## Slide 11: Backup

## Slide 12: Explicit Multi-link BSS Parameter Update
An AP within an AP MLD may send the updated BSS parameter of another AP within the same AP MLD.
  On this purpose, a new Multi-link IE is proposed to encapsulate the information element (IE) related with the BSS parameter of APs which is different with the AP transmitting this IE.
  As one of usage scenarios, the Extended Channel Switch Announcement (ECSA) is described in the following slides.
Element ID | Length | Element ID Extension | Link ID | Optional Subelements
1 octet | 1 octet | 1 octet | 1 octet | variable
<Multi-link IE>

## Slide 13: Explicit Multi-link BSS Parameter Update
The optional subelements field in the Multi-link IE contains the ECSA IE.
Assuming that a non-AP MLD does not monitor a link whose channel will be switched, a non-AP MLD may be fail to track the TBTT on that link.
  A reference of a channel switch time (refer the Channel Switch Count field) is a target beacon transmission time (TBTT).
In such case, the optional subelements field in the Multi-link IE may contain the beacon interval (BI) and the TSF offset between two links in order to track the TBTT.

## Slide 14: Explicit Multi-link BSS Parameter Update
For example, a non-AP MLD only monitors the link 1 for the BSS parameter update. An AP1 within an AP MLD is providing to the non-AP MLD the ECSA information related with another AP2 within the same AP MLD through the Multi-link IE.
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch1
Ch2
Ch2
Ch2
Ch2
AP1 in AP MLD
(Link 1)
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 3
B
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 1
B
B
B
B
B
B
AP2 in AP MLD
(Link 2)
Link ID: 2
BI: 100ms
TSF Offset: 50ms
New Ch Number: 2
Ch Switch Count: 2
B
B
B
B
B
B
B
50ms
50ms
50ms
BI : 100ms
Multi-link IE
Multi-link IE
Multi-link IE
50ms